## Slide 1: Behcet Sarikaya Frank Xia November 2011
Flow Binding Extensions to PMIPv6 IETF 82
draft-sarikaya-netext-fb-support-extensions-01

## Slide 2: Problem Statement
  LMA initiated flow mobility is not possible in PMIPv6 of RFC 5213
  PMIPv6 Multihoming extension (RFC 5213) treats each interface independently
  LMA does not know about different interfaces MN may have, LMA does not manage bindings from different interfaces of the mobile node in an integrated fashion
  Each interface creates a different independent mobility session at the LMA
  Flow mobility is not possible MN uses different source addresses when sending packets over these interfaces

## Slide 3: draft-sarikaya-netext-fb-support-extensions
We have a simple solution:
The bindings in binding cache from each interface are kept together so that the flows can be moved among interfaces.
MN may have as many binding entries as it has active interfaces, one “home” and many “secondary”, flagged “H” or “S”
A new H flag in HNP option is set to ‘H’ for home and ‘S’ for other interfaces
Incoming flows always directed to home interface, flow state set at LMA to direct flows to different active interfaces
MN always sends non-local packets with source address assigned from HNPs of its home “H” interface