## Slide 1: NETEXT WG IETF 82
Service Selection for Mobile IPv6
RFC5149bis
WEDNESDAY, November 16, 2011
Jouni Korhonen

## Slide 2: Background
RFC5149 was defined for RFC6275 (MIPv6) and RFC5213 (PMIPv6).
There are known implementations for PMIPv6 (yes, live deployments and multiple vendors).
RFC5149 has few areas that the authors think need enhancing & clarifications.
RFC5149 is Informational, however the authors feel it should already be Standards Track.

## Slide 3: RFC5149bis – change summary
Echoing the Service Selection option in (P)BAs – this is what running code does.
Updates to RFC5213 BCE lookup considerations. The Service Selection is used as one lookup key – this is what running code does.
New Status Code: MISSING_OR_UNKNOWN_SERVICE.
  Different from SERVICE_AUTHORIZATION_FAILED, which is not a good for a case where the requested service is not known the HA & LMA – this is what running code does.
Updating the document category from Informational to Standards Track.
  Multiple implementations, deployed, operation experience, ...

## Slide 4: For [discussion]
Some deployments encode the Service Selection Identifier field using RFC1035 style domain name encoding.. should that be described somehow? Current “standard” encoding is UTF-8.
How to extend Identifier with an additional “index” for a case where:
  The same service is accessed multiple times using the same Identifier name to configure multiple prefixes; example 2x “Internet”. The index allows to distinguish between “services” when prefix is not available (handoff).
  This was proposed at the early stages of RFC5149 but removed. However, it is not trivial to add such “index” now (backward compatibility).
  Existing deployments have such but those chose not to “decorate” the Identifier and instead use RFC5094 VSMs.

## Slide 5: Questions & Next Steps
Adopt as a WG document?