## Slide 1: MN Status Option for Proxy Mobile IPv6
YangweiTu(ZTE)
Nov. 2011

## Slide 2: Background
PMIPv6 deployments support communication using multiple access technologies simultaneously.
The PMIPv6 flow mobility draft specifies extensions for the traffic/IP flow to be moved from one access type to another.
The PMIPv6 flow mobility draft assumes a Mobile Node connectivity status of (1) connect or (2) disconnect. However some access technologies allow for a MN status of sleep or idle mode.

## Slide 3: Identified Problem
For flow mobility the LMA essentially decides the routing rules for the specific IP flow (s), however,
  the connectivity status of a node in sleep (idle) mode for a specific is not carried to the LMA.
  so that it is impossible to guarantee the flow mobility can be done successfully.

## Slide 4: Problem Illustration
LMA
MAG 1
MN
MAG 2
WiFi
3GPP
IP Flow X
IP Flow Y

## Slide 5: Problem Illustration
LMA
MAG 1
MN
MAG 2
WiFi
3GPP
IP Flow X
Sometime IP Flow Y is deleted, and the 3GPP access of the MN is changed to sleep or Idle mode

## Slide 6: Problem Illustration
LMA
MAG 1
MN
MAG 2
WiFi
3GPP
IP Flow X
the IP Flow X is decided to move from WiFi to 3GPP, and LMA determines the 3GPP access is in connect mode(the PMIP tunnel exist)

## Slide 7: Problem Illustration
LMA
MAG 1
MN
MAG 2
WiFi
3GPP
IP Flow X
MN maybe move out of the coverage of the MAG 2 in Idle Mode, then the MAG2 will fail to wake up the MN
MAG 2 can not establish the link to the MN, and the flow mobility of IP flow X is fail to complete.

## Slide 8: Initial idea for addressing issue
A new option is defined for using it in messages (PBU/PBA) exchanged between MAGand LMA.
MN-status Length
  8-bit unsigned integer indicating the length in octets of the option,excluding the type and length fields.
Mobile Node status
  The status of the mobile node attached from a specific accessnetwork, such as WiFi,WiMAX and 3GPP. Currently the value of the MNstatus can be as follow:1,connect mode,2,disconnect mode,3,idle/Power saving mode,4,reserved.

## Slide 9: Next steps
If the working group agrees that this is a problem and that the NETEXT resolve this issue.