## Slide 1: Quality of Service Option for Proxy Mobile IPv6 draft-liebsch-netext-pmip6-qos-00.txt
S. Gundavelli, J. Korhonen, M. Liebsch, P. Seite, H. Yokota,
IETF82, Taipei
NetExt WG
16th November 2011

## Slide 2: Motivation and Scope
Mobile operator systems establish QoS to serve access through 3G radio access
  Specific access, utilizes radio bearers with different QoS
QoS policy control for 3G radio access from Policy and Charging Control (PCC) system
Connectivity through non-3G acccess supported for handover (WiFi, WiMax)
IP network QoS accomplished by DiffServ mechanisms
No QoS support so far for non-3G radio access
  3GPP started interfacing PCC to MAG for non-3G radio access
Demand for a PCC-independent solution
  For networks, which do not deploy a PCC system
  For all networks until PCC support available for non-3G access

## Slide 3: Exemplary architecture
LMA
PCEF
PCC
3G access
Non-3G access
MAG
MAG
AP
AP
AP
QoS rules for downlink traffic mapping to transport network QoS
access bearer
IP connectivity
access bearer
access bearer
PCEF
DiffServ for Transport Network Layer QoS
e.g. .11e QoS support
IP-based transport network QoS support
WLANC
Convey new IP session info from MAG to LMA with PMIPv6 signaling
Convey available QoS info from LMA to MAG with PMIPv6 signaling

## Slide 4: Scope of this work
Support enabling QoS differentiation of traffic between MAG and LMA for any non-3G access
  Mainly enforcement and validation of uplink QoS at the MAG
Support mapping of QoS policies between radio-specific QoS classes and IP network
  Transport of Flow Information and QoS Class indexes
  Interpretation of QoS Class indexes is deployment specific, hence out of scope
Focus on the signaling between MAG and LMA
Handover of available and enforced QoS policy rules
  Established while MN accesses through 3G radio access
Establish QoS for sessions which start at non-3G radio access

## Slide 5
Is this of interest to the NetExt WG?