## Slide 1: Enabling Binding Update via access authorization
Charles Perkins, Basavaraj Patil
IETF 82 [netext] WG / Taipei
November 16, 2011

## Slide 2: The problem
Mobile devices often have to carry out two separate authentications before receiving packets at from home network
  Access authorization at local access network
  Binding Update to home network
This typically makes smooth handovers impossible.

## Slide 3: A solution
Enable access authorization to be relayed by the Home Agent which can then perform the Binding Update
For access authorizations using EAP, this can be done very simply by defining a new format for authentication data that is the same as the required EAP authentication data

## Slide 4: EAP Authentication Data [EAPAD]
The EAP Authentication Data [EAPAD] subtype has exactly the format defined in RFC 3748 for an EAP message.
This enables the LMA to unwrap the EAP message for delivery to AAA, acting as a simple AAA relay
LMA uses the EAP reply status to determine whether to apply the Binding Update

## Slide 5: Binding Acknowledgement Authentication Data
LMA needs to complete the authentication sequence by returning PBAck to the MAG.
The PBAck Authentication Data option uses, similarly to the PBU previously described, data as defined by RFC 3748
When MAG receives the data, then it can complete the EAP sequence, say according to 802.1x

## Slide 6: Combined Auth/Reg in PMIP6
MN
AP
AR/MAG
LMA
AAA
802.11 Assoc
(Access blocked)
EAPOL-Start
EAP-Req/Identity
EAP-Method
RADIUS Access Req
LMA acts as a AAA proxy/relay
Binding created
EAP Success
RA or DHCP
PBU with EAPAD
PBA with EAPAD

## Slide 7: Combined Auth/Reg in MIP6
MN
AP
AR
HA
AAA
802.11 Assoc
(Access blocked)
EAPOL-Start
EAP-Req/Identity
EAP-Method
RADIUS Access Req
HA acts as a AAA proxy/relay (Extract/Process BU)
Binding created
EAP Success
Assumption: MN obtains CoA from AR prior to start of EAP
Include BU inside the EAP message

## Slide 8: Role of NAI
The MN should naturally be identified by its NAI, and MN-NAI extension applied to PBU / PBAck. The NAI should identify which home agent / LMA is appropriate for the home address of the mobile node.
If there are thousands of home agent for the same AAA, then a local AAA relay can be configured with this information instead of configuring each MAG separately.