## Slide 1: Management Information Base for Load Balancer
Lianyuan Li , Chen Li China Mobile
tina.tsou Huawei
draft-li-opsawg-loadbalance-mib-03

## Slide 2: Why we do this？
There is a requirement to build a unique Load Balancer network management system where two or more vendors‘ LB devices are used. We propose the standard MIBs for unique NMS.
There is not a standard for LB mib till now. It’s difficult to develop a unique NMS.
Core Router
Access SW
aggregation
LB
LB
Firewall
Server farm
These LBs belongs to variant vendors
Internet

## Slide 3: The basic LB MIB nodes
The LB MIB may have Notifications, Objects, Conformance or some other attributes. However in my draft, we only concern on the common features for LB, just include:
  Virtual Service
  Real Service
  Real Service Group
  Health Monitoring
  Statistic

## Slide 4: Detailed Description-- Virtual Service
The function of Virtual Service is that LB config the interface to WAN.
The Virtual Service table is shown as below :
  lbVSEntry ::= SEQUENCE {
    lbVSId Unsigned32,
    lbVSAddr IpAddress,
    lbVSPort INTEGER,
    lbVSmode INTEGER,
    lbVSproto INTEGER}
/*virtual service IP address of cluster/LB, used for users to request services*/
/*The LB distributes the requests with the same source IP address and source port to a specific server*/
/*LB virtual service identifier*/
/*Layer 4 server load balancing can be classified into Network Address Translation (NAT)-mode server load balancing and Direct routing (DR)-mode server load balancing*/
/*LB can support protocol for user*/

## Slide 5: Detailed Description-- Real Service
Services provided by real servers are real Service.
A real service can be a traditional FTP or HTTP service, and can also be a forwarding service in a generic sense.
The Real Service table is shown as below :
  lbRSEntry ::= SEQUENCE {
    lbRSId Unsigned32,
    lbRSGId Unsigned32}
    lbRSAddr IpAddress,
    lbRSPort INTEGER,}
/*LB real service identifier*/
/* IP address of a server, used by the LB device to distribute requests */
/*The LB uses the port for communication with server*/
/*a real service group is a logical concept. Servers can be classified into different groups according to the common attributes of these servers*/

## Slide 6: Detailed Description-- Real Service Group
Real Server group is a logical concept. Servers can be classified into different groups according to the common attributes of these servers.
The Real Service table is shown as below :
  lbRSGEntry ::= SEQUENCE {
    lbRSGId Unsigned32,
    lbRSID Unsigned32,
    lbRSGschdalgorithm INTEGER,
    lbRSGhealth INTEGER}
/*LB real service group identifier*/
/*An LB needs to distribute service traffic to different real services according to a load balancing scheduling algorithm*/
/*LB real service identifier*/
/* The health monitoring method of RSG. It allows an LB device to detect whether real servers can provide services. The common method includes DNS\ICMP\HTTP, etc.*/

## Slide 7: Detailed Description-- Health Monitoring
Health monitoring allows an LB to check the statuses of real servers or links, collect the corresponding information
mark whether servers or links can work normally
collect statistics of the response time of the servers or links for selecting servers or links
The Health Monitoring table is shown as below :
  lbHealthchkEntry ::= SEQUENCE {
    lbHealthchkId Unsigned32,
    lbHealthchkAddr IpAddress,
    lbHealthchkPort INTEGER,
    lbHealthchktype INTEGER,
    lbHealthchkintvl Integer32,
    lbHealthchkretrytimes Integer32}
/*LB health check identifier*/
/*The remote IP address of server*/
/*The remote port of server supporting service*/
/*The set of health check method that include ICMP\DNS\HTTP*/
/*The definite length of between two packets*/
/* the LB will retry the defined times when server doesn't reply health check packet in time */

## Slide 8: Detailed Description-- Statistic
The statistic for Virtual Service or Real Service session, transmission rate.
The Statistic table contains the following items :
  lbStaEntry ::= SEQUENCE {
    lbStaId Unsigned32,
    lbStasession INTEGER,
    lbStarate INTEGER}
/*LB statistic table identifier*/
/*the max or min session number of a RS or RSG*/
/*the max or min flow rate of a RS or RSG*/

## Slide 9: Questions & Comments?

## Slide 10: Updates in the draft
Thanks for the comments from Juergen schoenwaelder and Jean-Philippe Dionne

## Slide 11: Thanks!