## Slide 1: Virtual Subnet: A Scalable Cloud Data Center Interconnect Solution draft-xu-virtual-subnet-06
Xiaohu Xu
(xuxh@huawei.com)
IETF82, TAIWAN

## Slide 2: Why VM Mobility across Data Centers
Data center maintenance
  Applications on a server or data center infrastructure requiring maintenance can be migrated offsite without downtime.
Disaster avoidance:
  Data centers in the path of natural calamities (such as hurricanes) can proactively migrate the mission-critical application environment to another data center.
Data center migration or consolidation:
  Migrate applications from one data center to another without business downtime as part of a data center migration or consolidation effort.
Data center expansion:
  Migrate virtual machines to a secondary data center as part of data center expansion to address power, cooling, and space constraints in the primary data center.
Notes: Data center maintenance without downtime:
  Applications on a server or data center infrastructure requiring maintenance can be migrated offsite without downtime.
Disaster avoidance:
  Data centers in the path of natural calamities (such as hurricanes) can proactively migrate the mission-critical application environment to another data center.
Data center migration or consolidation:
  Migrate applications from one data center to another without business downtime as part of a data center migration or consolidation effort.
Data center expansion:
  Migrate virtual machines to a secondary data center as part of data center expansion to address power, cooling, and space constraints in the primary data center.
Workload balancing across multiple sites:
  Migrate virtual machines between data centers to provide compute power from data centers closer to the clients (“follow the sun”) or to load-balance across multiple sites. Enterprises with multiple sites can also conserve power and reduce cooling costs by dynamically consolidating virtual machines in fewer data centers ,another feature enabling the green data center of the future

## Slide 3: Cloud Data Center Interconnect Requirements
Subnet extension.
  Allow VMs to move across data centers without requiring renumbering.
Scalability.
  Multi-tenancy capability (Beyond 4K VLANs).
  MAC table scalability (Millions of VMs within a data center) .
Unknown unicast reduction/avoidance
ARP broadcast reduction/avoidance.
Multi-homing.
Active-active DC exits.
Path optimization.

## Slide 4: Virtual Subnet Overview
Virtual Subnet (VS) is a host route based IP-only L2VPN service.
  BGP/MPLS IP VPN [RFC4364] signaling is used to distribute CE host routes across PE routers. Thus, the subnet is extended across data centers.
In comparison to VPLS, VS has the following advantages as a DCI solution:
  Reduce MAC table size of CE switches.
  Avoid flooding unknown unicast and ARP broadcast traffic across data centers.
  Natural multi-homing capability.
  Support active-active DC exits while guaranteeing path symmetry.
  Support path optimization.

## Slide 5: Control Plane: Routing Table
VPN Subnet: 1.1.0.0/16
Host D:
1.1.1.4
Host B:
1.1.1.3
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol 1.1.1.1/32 PE-1 BGP
1.1.1.2/32 PE-1 BGP
1.1.1.3/32 Local ARP
1.1.1.4/32 Local ARP
1.1.0.0/16 Null Direct
Prefix Next-hop Protocol 1.1.1.1/32 Local ARP
1.1.1.2/32 Local ARP
1.1.1.3/32 PE-2 BGP
1.1.1.4/32 PE-2 BGP
1.1.0.0/16 Null Direct
Host C:
1.1.1.2
Host A:
1.1.1.1
VRF:
VRF:
VPN Site #2
Host route exchange
via L3VPN signaling
Host discovery
via ARP/ICMP etc.
Host discovery
via ARP/ICMP etc.
1
1
3
2
Local host route
creation according
to ARP cache
4
Routing table
built up!
ARP
Proxy
ARP
Proxy
Notes: Host routes (i.e., /32) for local CE hosts, which are generated automatically according to their corresponding ARP entries, are distributed among PE routers with the existing L3VPN signaling.
Acting as an ARP proxy, each PE router returns its own MAC as a response to the ARP request for a remote CE host which is originated from any local CE host.
Ingress PE routers tunnel received customer packets that are destined for remote CE hosts to the corresponding next-hop egress PE routers in accordance with the current L3VPN forwarding process.

## Slide 6: Data Plane: Unicast
VPN Subnet: 1.1.0.0/16
Host D:
1.1.1.4
Host B:
1.1.1.3
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol 1.1.1.1/32 PE-1 BGP
1.1.1.2/32 PE-1 BGP
1.1.1.3/32 Local ARP
1.1.1.4/32 Local ARP
1.1.0.0/16 Null Direct
Prefix Next-hop Protocol 1.1.1.1/32 Local ARP
1.1.1.2/32 Local ARP
1.1.1.3/32 PE-2 BGP
1.1.1.4/32 PE-2 BGP
1.1.0.0/16 Null Direct
Host C:
1.1.1.2
Host A:
1.1.1.1
VRF:
VRF:
IP MAC
IP(B) MAC(PE-1)
ARP:
IP(A)->IP(B)
VPN Label
Tunnel to PE-2
IP(A)->IP(B)
VLAN ID
MAC(PE-2)->MAC(B)
VPN Site #2
2
Route
look-up
3
5
4
Route
look-up
0
Local PE returns
its own MAC
as ARP proxy
ARP
Proxy
ARP
Proxy
IP(A)->IP(B)
VLAN ID
MAC(A)->MAC(PE-1)
1
Notes: Host routes (i.e., /32) for local CE hosts, which are generated automatically according to their corresponding ARP entries, are distributed among PE routers with the existing L3VPN signaling.
Acting as an ARP proxy, each PE router returns its own MAC as a response to the ARP request for a remote CE host which is originated from any local CE host.
Ingress PE routers tunnel received customer packets that are destined for remote CE hosts to the corresponding next-hop egress PE routers in accordance with the current L3VPN forwarding process.

## Slide 7: MAC Table Reduction on CE Switches
The otherwise whole MAC learning domain associated with a given IP subnet, which has been extended across the MPLS/IP backbone, are partitioned into multiple isolated sub-domains.
  Thus, CE switches only need to learn MAC addresses of local CE hosts and local PE routers.
VPN Subnet: 1.1.0.0/16
MPLS/IP Backbone
MAC learning
domain #1
MAC learning
domain #2
VPN Site #1
VPN Site #2
IP(A)->IP(B)
VLAN ID
MAC(PE-2)->MAC(B)
Host D
Host B
Host C
Host A
IP(A)->IP(B)
VLAN ID
MAC(A)->MAC(PE-1)
PE-1
ARP
Proxy
PE-2
ARP
Proxy
CE
Switch
CE
Switch

## Slide 8: Unknown Unicast Flooding Avoidance
No flooding of unknown unicast traffic across the IP/MPLS backbone.
  Ingress PE routers forward customer packets according to the corresponding VPN routing table.
VPN Subnet: 1.1.0.0/16
MPLS/IP Backbone
PE-2
VPN Site #1
VPN Site #2
Host D
Host B
Host C
Host A
No route, no pass
ARP
Proxy
ARP
Proxy
PE-1
IP(A)->IP(?)
VLAN ID
MAC(A)->MAC(PE-1)

## Slide 9: ARP Broadcast Prevention
No flooding of ARP broadcasts across the IP/MPLS backbone:
  For an ARP request for a local CE host, discards it.
  For an ARP request for a remote CE host, returns its own MAC as a response.
  For an ARP request for an unknown CE host (i.e., no matching host route found), discards it.
VPN Subnet: 1.1.0.0/16
MPLS/IP Backbone
PE-1
PE-2
VPN Site #1
VPN Site #2
Host D
Host B
Host C
Host A
B’MAC=?
B’MAC=MAC(PE-1)
Q
A
ARP broadcast
domain #1
ARP broadcast
domain #2
ARP
Proxy
ARP
Proxy

## Slide 10: Site Multi-homing
VPN Subnet: 1.1.0.0/16
Host B:
1.1.1.3
MPLS/IP Backbone
PE-1
PE-2
Prefix Next-hop Protocol 1.1.1.1/32 PE-1 BGP
1.1.1.1/32 PE-3 BGP
1.1.1.3/32 Local ARP
1.1.0.0/16 Null Direct
Prefix Next-hop Protocol 1.1.1.1/32 Local ARP
1.1.1.3/32 PE-2 BGP
1.1.0.0/16 Null Direct
Host A:
1.1.1.1
VRF:
VRF:
VRRP Master/
ARP Proxy
PE-3
VRRP Slave
VPN Site #1
VPN Site #2
ECMP
ARP
Proxy
Active-active multi-homing is available for inbound traffic.
  Both VRRP master and VRRP slaver advertise host routes for their local CE hosts.
Notes: VRRP is enabled among the PE routers of a multi-homed site and only the VRRP master is entitled to act as an ARP proxy.
Active-active multi-homing is available for incoming traffic since all PE routers attached to a multi-homed site could advertise the corresponding host routes for their local CE hosts.

## Slide 11: CE Host Mobility(VM Mobility)
VPN Subnet: 1.1.0.0/16
Host B
MPLS/IP Backbone
PE-1
PE-2
Host A
VPN Site #1
VPN Site #2
Gratuitous ARP
1
BGP update
for host C
3
Gratuitous ARP
IP(C)->MAC(PE-1)
5
Create a local host route
for host C
2
Update host route
for host C
4
0
Host C moves from
Site #1 to Site #2
ARP
Proxy
ARP
Proxy
Host C
Host C
Host route for the moved VM is updated after the gratuitous ARP is received by the current PE of the moved VM.
ARP entries for that VM cached on both routers and other CE hosts are updated.
Notes: When a CE host moves from one VPN site to another,
  The PE router attached to the current VPN site will advertise a CE host route upon receiving a gratuitous ARP request or reply from that CE host.
  The PE router attached to the previous VPN site, upon receiving the above host route announcement, immediately sends an ARP request for that CE host to check whether that host is still connected to it.
    If not, the PE router should delete the corresponding ARP entry and host route for that CE host, and accordingly withdrawn the corresponding BGP route advertised before.
    Otherwise, it is judged as a case of CE multi-homing.

## Slide 12: Active-active DC Exits (Path Symmetry Guaranteed )
VPN Subnet: 1.1.0.0/16
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol
1.1.1.1/32 Local ARP
1.1.1.255/32 Local ARP
2.0.0.0/8 PE-1 BGP
3.0.0.0/8 GW-2 Static
Prefix Next-hop Protocol
1.1.1.1/32 PE-2 BGP
1.1.1.255/32 Local ARP
2.0.0.0/8 GW-1 Static
3.0.0.0/8 PE-2 BGP
Host A: 1.1.1.1
GW=1.1.1.255
VRF:
VRF :
VPN Site #2
Internet
Client Y(near DC#2)
Client X(near DC#1)
2.2.2.2.->IP(A)
2
GW-1
GW-2
1.1.1.255
1.1.1.255
NAT inside pool:
2.0.0.0/8
NAT outside pool:
3.0.0.0/8
3.3.3.3->IP(A)
2
IP(Y)->IP(A)
1
IP(X)->IP(A)
1
IP(A)->2.2.2.2
3
3
IP(A)->3.3.3.3
4
IP(A)->IP(Y)
IP(A)->IP(X)
4
Each DC exit router advertises a route for the subnet (e.g., 1.1.0.0/16) into the Internet.
Inbound traffic is source NATed when arriving at any DC exit router and routes for the NAT inside pools are advertised across the PE routers of that IP-only L2VPN.

## Slide 13: Path Optimization for VPN Access
VPN Subnet: 2.2.0.0/16
Host routes for VMs are distributed to remote VPN sites (e.g., enterprise site) thus forwarding path between enterprise site and cloud data centers can be optimized automatically.
VPN Subnet: 1.1.0.0/16
Host B
MPLS/IP Backbone
PE-1
PE-2
Host A
VPN Site #1
VPN Site #2
1
BGP update for host C
3
2
0
Host C moves from
Site #1 to Site #2
ARP
Proxy
ARP
Proxy
Host C
Host C
Traffic flow before the VM movement
Traffic flow after the VM movement

## Slide 14: Path Optimization for Internet Access
VPN Subnet: 1.1.0.0/16
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol
1.1.1.1/32 Local ARP
1.1.1.255/32 Local ARP
2.0.0.0/8 PE-1 BGP
3.0.0.0/8 GW-2 Static
Prefix Next-hop Protocol
1.1.1.1/32 PE-2 BGP
1.1.1.255/32 Local ARP
2.0.0.0/8 GW-1 Static
3.0.0.0/8 PE-2 BGP
Host A: 1.1.1.1
VRF:
VRF :
VPN Site #2
Internet
Connection established before the VM movement
2.2.2.2<->IP(A)
GW-1
GW-2
1.1.1.255
1.1.1.255
NAT outside pool:
4.0.0.0/8
NAT inside pool:
2.0.0.0/8
NAT outside pool:
5.0.0.0/8
NAT inside pool:
3.0.0.0/8
IP(Y)<->5.5.5.5
IP(X)<->4.4.4.4
3.3.3.3<->IP(A)
It’s not practical to propagate host routes for VMs into the Internet.
Hence DNS-based GLSB is resorted and it will be updated dynamically when the VM moves from one data center to another.
Connection established after the VM movement
VM Motion
GLSB/DNS
DNS update
DNS-ALG
FQDN(A)->4.4.4.4
5.5.5.5
1
0
Client X
Client Y

## Slide 15: FIB Scalability on PE: On-Demand FIB Installation (using VA-Auto)
VPN Subnet: 1.1.0.0/16
Host D:
1.1.1.4
Host B:
1.1.1.3
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol 1.1.1.3/32 Local ARP
1.1.1.4/32 Local ARP
1.1.0.0/16 RR BGP
Prefix Next-hop Protocol 1.1.1.1/32 Local ARP
1.1.1.2/32 Local ARP
1.1.1.3/32 PE-2 BGP
1.1.0.0/16 RR BGP
Host C:
1.1.1.2
Host A:
1.1.1.1
VRF: FIB
VRF FIB:
VPN Site #2
RR/APR advertises a VP route for the subnet and tags “can-suppress” to the host routes when advertising them to its clients.
1
ARP
Proxy
ARP
Proxy
RR/ARP
Prefix Next-hop Protocol 1.1.1.1/32 PE-1 BGP
1.1.1.2/32 PE-1 BGP
1.1.1.3/32 PE-2 BGP
1.1.1.4/32 PE-2 BGP
1.1.0.0/16 Null Direct
B’MAC=?
ARP Request triggers PE to install the corresponding host route from RIB to FIB.
2
0
3

## Slide 16: RIB Scalability on PE: On-Demand Route Announcement(using prefix-ORF)
VPN Subnet: 1.1.0.0/16
Host D:
1.1.1.4
Host B:
1.1.1.3
MPLS/IP Backbone
PE-1
VPN Site #1
PE-2
Prefix Next-hop Protocol 1.1.1.3/32 Local ARP
1.1.1.4/32 Local ARP
1.1.0.0/16 RR BGP
Prefix Next-hop Protocol 1.1.1.1/32 Local ARP
1.1.1.2/32 Local ARP
1.1.1.3/32 PE-2 BGP
1.1.0.0/16 RR BGP
Host C:
1.1.1.2
Host A:
1.1.1.1
VRF: RIB
VRF RIB:
VPN Site #2
RR distributes host routes to its clients (PEs) on demand when receiving prefix-based ORF.
1
ARP
Proxy
ARP
Proxy
RR
Prefix Next-hop Protocol 1.1.1.1/32 PE-1 BGP
1.1.1.2/32 PE-1 BGP
1.1.1.3/32 PE-2 BGP
1.1.1.4/32 PE-2 BGP
1.1.0.0/16 Null Direct
B’MAC=?
ARP Request triggers PE to request the corresponding host routes from its RR by using prefix-based ORF.
2
3
4
PE advertises its local host routes to its RR.
RR advertises a route for the subnet to its clients.
0

## Slide 17: Comments and Questions?

## Slide 18: Multicast/Broadcast (P-Multicast Tree Mode)
VPN Subnet: 1.1.0.0/16
P-Multicast Tree
PE-1
PE-2
MVRF MVPN Peer P-GROUP
BLUE {PE-1 ,PE-3} 225.1.1.1
PE-3
MVRF MVPN Peer P-GROUP
BLUE {PE-2,PE-3} 225.1.1.1
MVRF MVPN Peer P-GROUP
BLUE {PE-1 ,PE-2} 225.1.1.1
C-Multicast
C-Multicast
mGRE
IP(PE-3)->225.1.1.1
VPN Site #1
VPN Site #2
VPN Site #3
Notes: MVPN technologies including the ingress replication mechanism can be almost reused with minor change to distribute customer multicast/broadcast traffic across sites.
  Here the customer broadcast traffic is processed as the customer multicast traffic of a special group.

## Slide 19: Multicast/Broadcast (Ingress Replication Mode)
VPN Subnet: 1.1.0.0/16
Ingress Replication
PE-1
PE-2
MVRF MVPN Peer P-GROUP
BLUE {PE-1 ,PE-3} -----
PE-3
MVRF MVPN Peer P-GROUP
BLUE {PE-2,PE-3} -----
MVRF MVPN Peer P-GROUP
BLUE {PE-1 ,PE-2} -----
C-Multicast
C-Multicast
VPN ID
Tunnel to PE-2
C-Multicast
VPN ID
Tunnel to PE-1
VPN Site #1
VPN Site #2
VPN Site #3