## Slide 1: PAWS: Use Cases
I-D: draft-ietf-paws-problem-stmt-usecases-rqmts
Basavaraj Patil, Scott Probasco (Nokia)
Juan Carlos Zuniga (Interdigital)
IETF 82

## Slide 2: Updates from Rev 00 to 01
Added the Mobility, Indoor networking and machine-2-machine use cases
Deleted the location based service use case

## Slide 3: Database Discovery
Available channels or spectrum can be used by a device only after it has queried a database and obtained a response
Device needs to discover the relevant database to query
Databases are region/country/regulatory domain specific and hence the device needs to discover the relevant database based on its current location
The database discovery itself can be done via various approaches
  Examples include:
    Pre-programmed/configured list of databases on the device
    Query a well-known website operated by the regulator
    Etc.

## Slide 4: Database Discovery
Steps to discovering a database:
Master device is connected to the Internet via means other than WS radio
Device constructs and broadcasts/multicasts a database discovery message
Receives response(s) from available databases or a list of databases from a website
Device can choose a database from the responses for subsequent queries

## Slide 5: Registration with the DB (1)
After discovering a trusted database, the device needs to register with it prior to querying it for channel availability info
Requirements for registration can be regulatory domain specific
Various conditions require the device to perform registrations. Examples are:
  Power up
  Change of location by a certain distance
  Periodically based on a time interval
Registration information includes Device ID, Serial number etc.

## Slide 6: Registration with the DB (2)
Device has non-WS based connectivity to the Internet through which it can register with the selected database
Master Device
WS DB

## Slide 7: Registration with the DB (3)
A secondary Master device with no direct connectivity to the WS DB can query the DB using another Master as a relay
Master Device1
WS DB
Master Device2
TDD WS Air I/F

## Slide 8: Hotspot: Urban Internet connectivity
WS Device (Slave)
WS Device (Slave)
WS Device (Slave)
WS Device (Slave)
WS Master
WS DB
Internet
WS Master
Master/AP devices use a TDD radio technology and transmit at or
below a relatively low transmit power threshold.

## Slide 9: Hotspot: Urban Internet connectivity
Operation
The master/AP powers up (WS Radio in idle mode)
Master/AP discovers a database and registers with it
Master/AP queries the database requesting a list of available channels at its current location
Database responds with a list of available channels
Master/AP selects a channel(s) and activates the WS radio interface
Slave devices scans the WS bands and detects the Master/AP and attaches to it
Slave devices have Internet connectivity over WS radio channels

## Slide 10: Rural internet broadband access
Internet access is provided as a WAN or Wireless Regional Area Network (WRAN)
Typically characterized by one or more fixed master(s)/BS(s), cells with relatively large radius (tens of kms, up to 100 km), and a number of available radio channels
The BS in this scenario use a TDD radio technology and transmit at or below a transmit power limit established by the local regulator
Each base station has a connection to the internet and provides internet connectivity to multiple slave/end-user devices which can be fixed or mobile

## Slide 11: Offloading: Moving traffic to a WS network
Mobile devices using 3G/4G Cellular networks for data can offload the session to a WS network if a network is available
A device attached to a 3G/4G cellular network has an ongoing video streaming session
Policy on the device is configured to use an alternate access network such as WS when one is available for use

## Slide 12: Offloading
Cellular/WS Device
WS Master
Internet
WS DB
Video
Server
1
2

## Slide 13: Backhaul
WS spectrum can be used as a backhaul and thus enable various types of network deployments (mesh, Muni wifi etc.)
WS Master
Internet
WS DB
Wifi
AP
Wifi Device
Wifi
AP
Wifi
AP

## Slide 14: Rapid deployed network for emergency scenario
In the event of an emergency spectrum can be made available for the establishment of a rapid response network
WS Master devices can be deployed or existing ones use the freed spectrum in such scenarios

## Slide 15: Mobility in white space
Operation
The master/AP powers up (WS Radio in idle mode)
Master/AP discovers a database and registers with it
Master/AP queries the database requesting a list of channels that are available at its current location and also a future location.
Database responds with a list of available channels that are available at all locations identified in the request.
Master/AP selects a channel(s) and activates the WS radio interface
Master/AP may use channels from the list while moving within the predicted area without requirement to query the database due to mobility (i.e. moving more than 100 m). Time based restrictions are still applicable

## Slide 16: Indoor networking use case
User devices are inside a house or office, requiring connectivity to the Internet or to equipment in the same or other houses/offices
Database query from the master device includes geolocation and location uncertainty and optional additional information such as device ID
Response is list of channels available, and optional additional information such as channel validity time and maximum radiated power
The master authenticates the response and selects one or more channels from the list
The user device scans the TVWS bands to locate the master device transmissions, and associates with the master

## Slide 17: Machine to machine (M2M) use case
Machines include a whitespace device and can be located anywhere, fixed or on the move. Each machine needs connectivity to the internet and/or to other machines in the vicinity
Database query from the master device includes geolocation and location uncertainty and optional additional information such as device ID
Response is list of channels available, and optional additional information such as channel validity time and maximum radiated power
The master authenticates the response and selects one or more channels from the list
The slave devices fitted to the machines scan the TV bands to locate the master transmissions, and associate with the master device.
Note: Further signalling can take place (outside the scope of PAWS) to establish direct links among those slave devices that have associated with the master device. Machine communication over a TVWS channel, whether to a master device or to another machine (slave device), is under the control of a master device

## Slide 18: Next Steps
Request further reviews and comments
Would like to progress the I-D to WGLC before IETF83