## Slide 1: The IEEE 802.22 WRAN Standard and its interface to the White Space Database REQUIREMENTS FOR PAWS
Apurva N. Mody, apurva.mody@ieee.org
Chair, IEEE 802.22 Working Group (www.ieee802.org/22)
Gérald Chouinard, gerald.chouinard@crc.ca
IEEE 802.22 Working Group Vice-chair and lead editor
Jerome Kalke, (CBS), Ranga Reddy, Nancy Bravin
IETF PAWS Working Group Meeting
Notes: <number>

## Slide 2: Characteristics of 802.22 WRAN:
30 km
23 km
16 km
QPSK
16-QAM
64-QAM
Max throughput per 6 MHz: DS: 7.8 Mbit/s, US: 768 kbit/s
Max throughput per 6 MHz: 22.69 Mbit/s
Minimum service availability: location= 50%, time= 99.9%
Base station power: 100 W Antenna height: 75 m
User terminal (CPE) power: 4 W antenna height: 10 m
USA: ≤ 4 W max EIRP
Height ≤ 30 m (106 m HAAT)
Canada: ≤ 500 W max EIRP
Height ≤ 500 m HAAT (4 W)
Notes: <number>
The service availability is defined as F(50, 90), that is one household over 2 can be reached at the edge of the coverage (unlike 1 over 4 over most of the coverage for WLAN as explained by STORM yesterday) (availability will be much better inside the coverage area) and once connection is feasible, its availability in time will be very high for stable service, i.e., 99.9%). This can be achieved with Customer Premise Equipment (CPE) transmit power of 4 W as specified by the FCC and a base station power of 100 W at 75 m antenna height for the maximum throughtput indicated. In order to re-use a DTV frequency, the base station will need to be located at some 30 km from the edge of the DTV coverage area. This will reduce to 1 km if a first adjacent channel is used. The CPEs can be located at 3 km from the edge of the DTV coverage area for the co-channel case and only 70 m for the first adjacent channel. Since it is considered that the distance between neighbor can be as small as 10 m, CPEs operating on first adjacent channels will not be allowed inside the DTV coverage area.

## Slide 3: IEEE 802.22 WRAN Standard Key features
WRAN: Wireless Regional Area Network
  Aimed at bringing broadband access to hard-to-reach, low population density areas, typical of rural environments and developing countries
Operate in vacant channels in TV broadcast bands to take advantage of better signal propagation at lower frequencies
Operate as license-exempt equipment although the base station (BS) and possibly the customer premise equipment (CPE) have to be professionally installed
Point-to-multipoint network topology
  Base station connected to the Internet through a backhaul
  Base station provides service to up to 512 CPEs (fixed or portable) and controls all their RF characteristics (“master-slave”)
Use cognitive radio capabilities to avoid interference to broadcast incumbents and other WRAN systems
  Access to databases
  RF sensing

## Slide 4: 802.22 Unique Proposition
First IEEE 802 Standard for operation in Television Whitespaces
First IEEE Standard that is specifically designed for rural and regional area broadband access aimed at removing the digital divide
First IEEE Standard that has all the Cognitive Radio featur
Recipient of the IEEE SA Emerging Technology Award

## Slide 5: REQUIREMENTS

## Slide 6: 802.22 database interface model
To comply with the FCC R&O 08-260, the IEEE 802.22 interface to the database will take place entirely between the database service and the Base Station (BS) rather than with its individual CPEs (BS has to find the channel that is common to all its CPEs rather than the CPEs doing it individually (MO&O 10-174: 15.711(e)). In other words, BS acts as a proxy to all the CPEs

## Slide 7: DATA MODEL REQUIREMENTS (1)
Antenna height | Integer | 1 byte | Antenna height above ground level in meters.
[Note: our assumption is that the database will compute the HAAT in meters from the antenna AGL and ground elevation at the specified location (lat, long) obtained from a topographic database by the database server.]
[Note: portable antenna height may be 1.5 m. Base stations in Canada can be at up to 500 m HAAT which could be completely contributed by the antenna AGL (e.g., mounted on a broadcast tower). Two bytes are therefore necessary.]

## Slide 8: DATA MODEL REQUIREMENTS (2)
Gain Parameters
  Antenna directionality information in dB: relative to the main lobe maximum gain for every 5 degree azimuth clockwise starting from the direction of the maximum antenna gain expressed in unit of 0.25 dB over the range –63.75 dB (encoded 0x00) to 0 dB (0xFF): Character String of 72 bytes
  Antenna azimuth in degrees, clockwise from true North: 2 bytes INT
Example: 802.22 primitive:
Antenna information | Character String | 72 bytes | Antenna directionality information of the device in dB relative to the main lobe maximum gain for every 5 degree azimuth clockwise starting from the direction of the maximum antenna gain expressed in unit of 0.25 dB over the range –63.75 dB (encoded 0x00) to 0 dB (0xFF). (to allow the database calculation of the channel availability and the maximum allowed EIRP values at the registering location19)
Antenna azimuth | Integer | 2 bytes | Antenna azimuth in degrees, clockwise from true North
(Continued)

## Slide 9: DATA MODEL REQUIREMENTS (3)
Gain Parameters (Continued)
Note:
Antenna directionality will represent the antenna gain pattern in the horizontal plane in dB referred to the gain of its main lobe and it is assumed that the database service will use its knowledge of the geolocation of the base station and the device being enlisted to calculate the azimuth of the device antenna main lobe for interference calculations in the case of base station and CPE operation. Omni-directional antennas shall be assumed as the default.

## Slide 10: DATA MODEL REQUIREMENTS (4)
RF Mask Parameters (Master WSD => database)
  Regulatory Domain (3 ASCII Letters), Device Type (Regulatory Class: e. g., Fixed, Personal/Portable, Mobile, etc.) (1 byte INT), Mask Number Index (2 byte INT) (where Mask Number Index corresponds to a particular RF Mask of an equipment that is stored in the database and that has passed the regulatory certification).
Example: 802.22 primitive:
Device Type | Integer | 1 byte | The value identifies the type of device at the geolocation registering 0x00 = Fixed base station 0x01 = Fixed CPE 0x02 = Personal/portable mode 0x03–0xFF = Reserved

## Slide 11: DATA MODEL REQUIREMENTS (5)
Name | Type | Length | Description
Device Type | Integer | 1 byte | The value identifies the type of device at the geo-location registering 0x00 = Fixed base station 0x01 = Fixed CPE 0x02 = Personal/portable mode 0x03-0xFF = Reserved
Device-ID Length | Integer | 2 bytes | Length of Device-ID field (# of characters)
Device-ID | Character String | Variable | In US, this is FCC-ID
Serial Number Length | Integer | 2 bytes | Length of Serial Number field (# of characters)
Serial Number | Character String | Variable | 
Note: The device-ID and Serial Number could be replaced by a universal identifier made of one or many parts . The master WSD must also specify, as part of its registration process with the database, the technology that it uses (e.g., IEEE 802.22, IEEE 802.11af, etc.) (see requirement O.7).

## Slide 12: DATA MODEL REQUIREMENTS (6)
Name | Type | Length | Description
Location Data String Length | Integer | 2 bytes | Length of Location Data String field (# of characters)
Location Data String | Character String | NMEA 0183 Character String | The value identifies the location of the device (latitude, longitude).20
Note: NMEA 0183 $GPGGA or $GPGLL String can carry latitude and longitude information. In the work of the IEEE 802.22 Working Group, it was assumed that the altitude of a geographic point would be derived at the database based on the latitude and longitude of the location of the WSD (see the note related to HAAT in D.1 above for which ground elevation information would need to be known). In 802.22 networks, the CPEs acquire their geolocation and transmit their latitude and longitude to the base station at the time of association. The base station would augment the location information defined in the NMEA string format with uncertainty (m) and confidence level (%) as the local regulator may want to define it. These uncertainty and confidence values would be generated at the base station based, for example, on the technology used by the WSDs to acquire their geolocation. The uncertainty could also be artificially increased to take into account the size of the area around a WSD where other WSD’s not requiring geolocation (e.g., Mode I devices in the USA) would operate.

## Slide 13: DATA MODEL REQUIREMENTS (7)
Name | Type | Length | Description
Number of Channels Available | Integer | 1 byte | 
{ If( Number of Channels Available > 0) |  |  | If the number of channels is equal to 0, this means that the device cannot operate.
For (i=1; i≤ Number of Channels Available; i++) { Channel_Number Max_Allowed_EIRP (dBm) Availability schedule } | Vector of 2xN bytes and a number of pairs of NMEA 0183 $ZDA strings | Variable | List of available channel numbers and corresponding maximum allowed EIRP expressed in dBm over the range –64 dBm (encoded 0x00) to +63.5 dBm (encoded 0xFF) as well as the availability schedule (start and stop date/time) for each channel in Universal date and time system.
} |  |  | 
(See D.4 above. Also, specifying the “maximum output power” is not sufficient since it may or may not include the antenna gain. Specifying the EIRP is needed. D.5 should be deleted since it is proposed to be covered in D.4.)

## Slide 14: DATA MODEL REQUIREMENTS (8)
[AMENDED] D.6: The Data Model MUST support specifying channel availability information for single and multiple locations. The database MUST also allow a master device to act as a proxy for other WSDs and query on their behalf. (Master WSD => Database)
In case of 802.22 systems which are to provide point-to-multipoint broadband access service primarily to rural areas, the BS acts as a proxy for all its associated CPEs and queries the database for each device. If a query is to be grouped or made in a batch mode, all the information related to each device shall be provided to the BS (i.e., the database is not to perform the intersection for all these devices and locations).
….. continued

## Slide 15: DATA MODEL REQUIREMENTS (8)
[AMENDED] D.6: The Data Model MUST support specifying channel availability information for single and multiple locations. The database MUST also allow a master device to act as a proxy for other WSDs and query on their behalf. (Master WSD => Database)
…. Continued from previous slide
[Note: This option may be useful to ‘batch’ the database query process but it is not clear whether this would really increase the data transfer efficiency. In the case of the 802.22 WRAN systems, the base station will need to acquire all the information about the available channels for each of these CPEs (and the related maximum EIRP’s) so that the operating channel and the backup channels (to which the WRAN cell will need to move if the current operating channel becomes unavailable to ensure a transparent channel move) can be determined locally from the best ‘intersection’ of these channels for all the associated CPEs. This will allow database queries for only new CPEs coming on board or being moved, and constraints to be added locally at the base station to execute the ‘intersection’ process to produce the updated list of operational and backup channels that is to be transmitted to all CPEs for refreshing.

## Slide 16: DATA MODEL REQUIREMENTS (9)
[DISAGREE] D.7: The Data Model MUST support specifying channel availability information for an area around a specified location. (Database => Master WSD)
In our opinion, this can be done through the normal query process if a query to the database can be done with dummy device IDs, for example for planning purposes, and hence, we feel that this is not really needed. If a query is done to the database with dummy device ID, the database should not register these new devices and only provide the list of available channels. There should therefore be a need to identify whether the included device ID is a real one or not.

## Slide 17: DATA MODEL REQUIREMENTS (10)
[NEW] D.8: The Data Model should support reporting to the database the channels that the master WSD has selected as the operating channel and the backup channels (see requirement O.7).

## Slide 18: PROTOCOL REQUIREMENTS

## Slide 19: PROTOCOL REQUIREMENTS (1)

## Slide 20: PROTOCOL REQUIREMENTS (2)
[NEW] P.7: The protocol MUST require the master WSD to maintain contact with the database as specified by the local regulator as well as to specify and re-register its operating and backup channels with at least the same periodicity.

## Slide 21: OPERATIONAL REQUIREMENTS

## Slide 22: OPERATIONAL REQUIREMENTS (1)

## Slide 23: OPERATIONAL REQUIREMENTS (2)

## Slide 24: OPERATIONAL REQUIREMENTS (3)

## Slide 25: OPERATIONAL REQUIREMENTS (4)
[NEW] O.7: The database must be capable of keeping track of the channels that are currently being utilized by the master devices and the technology that they use (e.g., IEEE 802.22, IEEE 802.11af, etc.).
If a request for the available channel is made by another master WSD from the same area and it is found that the new requesting master device technology cannot co-exist, then that channel should be removed from the available channels list going to this new device. Unless the given master WSD fails to re-query within the specified contact period, the database should make that channel available. Accordingly, the protocol should provide the master WSDs with a means to release their operating channel when not needed.
Note that without an active channel management mechanism (e.g., 802.22 spectrum manager), it is unlikely that having the database just specifying which channels are available to protect incumbent services on a 24 hours cycle will be sufficient to allow for proper operation of multiple WSDs in an area without interference being caused among themselves. Without area specific centralized spectrum management that directs and juggles master WSD channel assignments virtually instantaneously, the result will be inefficient use of White Space spectrum.

## Slide 26
INTERFACES
Presented Earlier by Gerald Chouinard in Quebec City
July 2011

## Slide 27: IEEE 802 Standards Process
IEEE
802
802.11
WLAN
802.15
WPAN
802.16
WMAN
802.11g
54 Mbit/s
802.11b
11 Mbit/s
…
802.15.1
Bluetooth
802.15.3
High rate
802.11n
100 Mbit/s
…
802.16d
Fixed
802.16e
Mobile
…
802.18
Regulatory
Matters
802.22
WRAN
802.22.1
Enhanced Part 74 protection
802.22.2
Recommended Practice
802.11j
Relay
…
802.15.4
Zigbee
Wi-Fi
Wi-MAX
802.19
802 systems
coexistence
Sensing
Tiger Team
Geolocation
Tiger Team
802.19.1
TVWS
coexistence
Notes: <number>
The 802.22 Working Group is developing the WRAN standard. It is one of the many 802 WGs as can be seen. This WG is the first one that considers the sensing on incumbent systems already operatin in the frequency range to be used. Each CPE and base station will sense the spectrum in its surrounding and will report it to the base station so that a network level decision is made on either continuing to operate on the channel or switch channel to avoid interference to an incumbent system.
802.22 already has a Task Group 802.22.1 dealing with the development of a standard for a wireless microphone beacon to protect wireless microphone operation in the TV bands since the power of the microphone themselves suffers too much attenuation and cannot be relied upon for sensing.
A second 802.22 Task Group 802.22.2 will be formed in September to develop the “Recommended Practice” to define the proper Installation and Deployment of IEEE 802.22 WRAN Systems so that interference to incumbent systems is avoided. This extra piece will be needed to convince the broadcasters that actual operation will not be harmful to their operation.

## Slide 28: IEEE 802 Standards
IEEE 802.22
RAN
“Regional Area Network”
30 km
54 - 862 MHz
Multipath absorption Window (Cyclic prefix )
0.25
2.2 μsec
0.8
37 μsec
23, 27, 31 Mbit/s
BW= 6,7,8 MHz
Notes: <number>
The IEEE 802.22 Working Group which is developing the WRAN standard is adding anotherr layer to the set of licensed-exempt wireless systems. It will be able to operate in the low-VHF (ch. 2-6), high-VHF (ch. 7-13) and UHF (ch. 14 to 51 and 69 where possible). It will use the standard TV channels, 6, 7 and 8 MHz wide. Each channel can carry some 20 Mbit/s capacity and its modulation (2000 carriers OFDMA) will be robust to long echoes (up to about 25 usec) found on these longer paths.

## Slide 29: IEEE 802.22 WRAN Standard Key features
WRAN: Wireless Regional Area Network
  Aimed at bringing broadband access to hard-to-reach, low population density areas, typical of rural environments and developing countries
Operate in vacant channels in TV broadcast bands to take advantage of better signal propagation at lower frequencies
Operate as license-exempt equipment although the base station (BS) and possibly the customer premise equipment (CPE) have to be professionally installed
Point-to-multipoint network topology
  Base station connected to the Internet through a backhaul
  Base station provides service to up to 512 CPEs (fixed or portable) and controls all their RF characteristics (“master-slave”)
Use cognitive radio capabilities to avoid interference to broadcast incumbents and other WRAN systems
  Access to databases
  RF sensing

## Slide 30: Typical CPE installation
Sensing antenna
GPS antenna
TX/RX WRAN Antenna
Notes: <number>

## Slide 31: 802.22 database interface model
To comply with the FCC R&O 08-260, the IEEE 802.22 interface to the database will take place entirely between the database service and the BS rather than with its individual CPEs (BS has to find the channel that is common to all its CPEs rather than the CPEs doing it individually (MO&O 10-174: 15.711(e)).

## Slide 32: 802.22 database interface procedure
The BS will initially enlist with the database service as a fixed device. It will also enlist all its associated CPEs with their geographic location, device identification, etc., as obtained at association on a real time basis.
On an ongoing basis, the BS will then query the database (at least once every 24 hours) using the M-DB-AVAILABLE-CHANNEL-REQUEST message so that it can retrieve the channel availability information.
The database service could also send any update relevant to the BS operation through ‘push’ internet technology since the network address of the base station is provided as part of the messages (this will allow better reaction time than the 24 hours minimum access time while keeping the database traffic to a minimum).

## Slide 33: Security of the database interface
SSL will be supported on the link between the database service and the BS to provide transport layer security:
  to allow authentication of the database service provider as well as the WRAN system querying the service
  to avoid the message exchange being altered on the backhaul connection
protocols used for device and database service authentication and for interacting with the database: EAP-TLS or EAP-TTLS
database service primitives are exchanged between the CPE/BS and the database service via Attribute Value Pairs of EAP messaging
formatting of these messages should conform to the authentication service that the database service employs: (e.g., RADIUS/RFC 2865 or DIAMETER/RFC 3588).

## Slide 34: Database service primitives
M-DB-AVAILABLE-REQUEST: Message that allows the BS to verify that it is connected to the database service in order to receive channel availability and maximum allowed EIRP updates.
M-DB-AVAILABLE-CONFIRM: Message that allows the database service to confirm that the BS is connected to the database service.
M-DEVICE-ENLISTMENT-REQUEST: Message that allows the BS to enlist with the database service a device that has joined its WRAN network.
M-DEVICE-ENLISTMENT-CONFIRM: Message that allows the database service to confirm to the BS that the new device has been successfully registered.

## Slide 35: Database service primitives
M-DB-AVAILABLE-CHANNEL-REQUEST: Message by which the BS requests a list of available channels and maximum allowed EIRP per channel from the database service for the specified type of device at the particular location.
M-DB-AVAILABLE-CHANNEL-INDICATION: Message that is used to return to the BS the list of available channels as provided by the database service in the form of channel number, maximum allowed EIRP, and availability schedule.
M-DB-DELIST-REQUEST: Message that allows the BS to request the database service to remove the enlistment of a device that was associated with that base station.
M-DB-DELIST-CONFIRM: Message that is used to inform the BS whether its request to remove the enlistment of a device that was associated with that base station was successfully received and executed by the database service.

## Slide 36: M-DB-AVAILABLE-REQUEST

## Slide 37: M-DB-AVAILABLE-CONFIRM

## Slide 38: M-DEVICE-ENLISTMENT-REQUEST (a)

## Slide 39: M-DEVICE-ENLISTMENT-REQUEST (b)

## Slide 40: M-DEVICE-ENLISTMENT-REQUEST (c)

## Slide 41: M-DEVICE-ENLISTMENT-CONFIRM

## Slide 42: M-DB-AVAILABLE-CHANNEL-REQUEST

## Slide 43: M-DB-AVAILABLE-CHANNEL-INDICATION

## Slide 44: M-DB-DELIST-REQUEST

## Slide 45: M-DB-DELIST-CONFIRM

## Slide 46: References
IEEE Std 802.22-2011TM, Standard for Wireless Regional Area Networks—Part 22: Cognitive Wireless RAN Medium Access Control (MAC) and Physical Layer (PHY) specifications: Policies and procedures for operation in the TV Bands, July 2011
IEEE 802.22 WG inputs to PAWS: https://mentor.ieee.org/802.22/dcn/11/22-11-0127-06-0000-ieee-802-22-inputs-to-ietf-paws.doc
U.S. FCC, ET Docket 08-260, “Second Report and Order and Memorandum Opinion and Order in the Matter of Unlicensed Operation in the TV Broadcast Bands,” November 14, 2008.
U.S. FCC, ET Docket 10-174, “Second Memorandum Opinion and Order in the Matter of Unlicensed Operation in the TV Broadcast Bands,” September 23, 2010.
NMEA 0183, Interface Standard of the National Marine Electronics Association, Version 4.00 http://www.nmea.org/content/nmea_standards/nmea_083_v_400.asp.
IETF RFC 2865, “Remote Authentication Dial In User Service (RADIUS),” June 2000.
[B1] DIAMETER/RFC 3588, “Diameter Base Protocol,” September 2003.
IETF RFC 3748, “Extensible Authentication Protocol (EAP),” June 2004.
Notes: <number>
doc.: IEEE 802.22-06/0006r0
January 2006
Gerald Chouinard, CRC
Page <number>