## Slide 1: Forward-Search P2P/P2MP TE LSP Inter-Domain Path Computation
draft-chen-pce-forward-search-p2p-path-computation
draft-chen-pce-forward-search-p2mp-path
Huaimo Chen (huaimochen@huawei.com)

## Slide 2: Requirements for Inter-domain Path
Page <number>
RFC 4105 “Requirements for Inter-Area MPLS TE”
The solution SHOULD provide the capability to compute a shortest path dynamically, satisfying a set of specified constraints across multiple IGP areas.
The solution MUST provide the ability to re-optimize in a minimally disruptive manner (make before break) an inter-area TE LSP, should a more optimal path appear in any traversed IGP area.
RFC 4216 “MPLS Inter-AS TE Requirements”
The solution SHOULD provide mechanisms to compute a shortest end-to-end path for a TE LSP crossing multiple ASes and satisfying a set of specified constraints dynamically.
Once an inter-AS TE LSP has been established, and should there be any resource or other changes inside anyone of the ASes, the solution MUST be able to re-optimize the LSP accordingly and non-disruptively, either upon expiration of a configurable timer or upon being triggered by a network event or a manual request at the TE tunnel Head-End.

## Slide 3: Forward Search P2P Inter-domain Path
Page <number>
Start from the source node and the source domain.
Consider the optimal path segment from source node or an entry boundary node to every exit boundary node of the source domain or a domain as a special link; and the segment is computed as needed.
The whole topology consisting of many domains can be considered as a special topology, which contains those special links, the normal links in the destination domain and the inter-domain links.
Compute an optimal path in this special topology from the source to the destination using CSPF.
Domain 120
J
I
F
C
G
K
L
M
N
O
Q
T
U
X
A
B
R
H
V
B1
E
D
S
W
A1
Y
Z
P
Domain 150
Domain 180
PCE2
PCE1
PCC
PCE3
Boundary Node
Boundary Node
Src Node
Dest Node
2
4
3
1
C1
Best path:
A-C-F-J-L-O-U-X-A1-C1
Src to Boundary path computed as a link
In Boundary to Out Boundary path computed as a link

## Slide 4: Forward Search P2P Inter-domain Path (Animated)
Domain 120
J
I
F
C
G
K
L
M
N
O
Q
T
U
X
A
B
R
H
V
B1
E
D
S
W
A1
Y
Z
P
Domain 150
Domain 180
PCE
PCE
113
115
PCC
111
PCE
117
Boundary Node
Boundary Node
Src Node
Dest Node
2
4
3
1
C1
Best path:
A-C-F-J-L-O-U-X-A1-C1
Src to Boundary path computed as a link
In Boundary to Out Boundary path computed as a link
A3
B3
C3
B4
A4
C4
B2
A2
C2
8
10
10
2
3
4
6
11
5
6
3
15
7
7
7
6
8
8
16
9
8
8
10
10
18
18
On the shortest path tree

## Slide 5: Forward Search P2MP Inter-domain Path
On shortest path
Similar to Forward Search P2P Inter-domain Path
Build a shortest path tree in the special topology from the source to the destinations using CSPF.
Count the number of destinations on the tree until all the destinations on it.

## Slide 6: Next Step
Welcome comments
Request to make it into a working group document