## Slide 1: Stateful PCE
Kexin Tang
Wang Xuerong
Cao Xuping
ZTE Corporation
draft-tang-pce-stateful-pce-02.txt

## Slide 2: A Problem without Stateful PCE
Figure 1:Sequence of events with stateless PCE
T 5
LSP 1 setup
success(AB)
Unreserved Bandwidth
Unavailable
Bandwidth
C
A
B
100 M
20 M
LSP1:80 M
100 M
100 M
PCReq1( LSP 1:
A-B, 80M)
PCRep 1
(LSP 1:AB)
PCRep2:
( LSP 2:AB)
PCReq2(LSP 2:
A-B,80M)
LSP 2 setup failed
(insufficient bandwidth)
Time
T 1
T 2
T 3
T 4
T7
LSP 2 setup failed
IGP Flooding: LSP1 setup
T 6

## Slide 3: Realization of stateful PCE
PCC discovers stateful PCE
PCE computed path, and save the result
Notify each PCE the E2E path computation result
Notify PCE
the LSP setup/deletion result

## Slide 4: PCED Extension
Bit | Capabilities
0 | Path computation with GMPLS link constraints
1 | Bidirectional path computation
2 | Diverse path computation
3 | Load-balanced path computation
4 | Synchronized path computation
5 | Support for multiple objective functions
6 | Support for additive path constraints (max hop count, etc.)
7 | Support for request prioritization
8 | Support for multiple requests per message
9 | P2MP path computation
TBD | Stateful PCE
10-31 | Reserved for future assignments by IANA
New PCE Capability Flag of
PCE-CAP-FLAG
Extended PCED TLV(RFC 5088), defined a new capability flag
With the stateful PCE capability flag, the PCC can select which PCE to be used.
Notes: 1、PCE能力发现
扩展PCED对象，通过OSPF洪泛发现PCE是否具有有状态的能力。
PCC选择PCE时可以选择无状态或有状态能力的PCE
--扩展在此内容补充
<number>

## Slide 5: Protocol Extensions: PCEP
  Notification-type=TBD: LSP Status
    Notification-value=1/2: end-to-end path computation success/ failure
    Notification-value=3/4: LSP setup success/ failure.
    Notification-value=5: LSP deletion success.
  <PCNtf Message>::=<Common Header><notify-list>
  <notify-list>::=<notify> [<notify-list>]
  <notify>::=[<request-id-list>]<notification-list>
  <request-id-list>::=<RP>[<path>][<request-id-list>]
  <path>:=<ERO><attribute-list>
  <attribute-list>::=[<LSPA>][<BANDWIDTH>][<metric-list>][<IRO>]
  <notification-list> ::=<NOTIFICATION>[<notification-list>]

## Slide 6: Synchronization between PCC/PCE and PCE/PCE
PCC/PCE | PCE/PCE
Path setup result : PCC sends the path setup result to the PCE: Notification-value=3/4 Success: PCE saved the resources for the <path> carried in the PCNtf Failed:PCE removed the resources for the <path> carried in the PCNtf | End-to-End Path Computation Result: PCE of the first domain Sends PCNtf to each PCE in the PCE chain: Notification-value=1/2 Success: Each PCE released resources except those belong to the <path> carried in the PCNtf Failed:Each PCE released all the resources saved for the LSP in TED
Path deletion result: Notification-value=5 Deletion Success: removed the resources of the deleted LSP in its local TED. | (Note: When path setup/deletion result sent from PCC to PCE, the PCE that received the notify message play the role of PCC, and notify the next PCE, as PCC/PCE synchronization.)

## Slide 7: Stateful PCE Avoid Resource Conflict
Figure 2:Sequence of events with stateful PCE
T 5
LSP 1 setup
success(AB)
Unreserved Bandwidth
Unavailable
Bandwidth
100 M
20 M
LSP1:80 M
100 M
100 M
PCReq1( LSP 1:
A-B, 80M)
PCRep 1
(LSP 1:AB)
PCReq2:
( LSP 2:ACB)
PCReq2(LSP2:
A-B,80M)
IGP Flooding: LSP1 setup
Time
T 1
T 2
T 3
T 4
T7
LSP2 setup
Success(ACB)
T 6
A
C
B
LSP2:80 M
20 M
20 M
LSP2:80 M
Notify PCE LSP1 setup success
Notify PCE LSP2 setup success

## Slide 8
BRPC compute Inter-area/AS path
H
F
D
B
1. PCNtf
(ABDFHJ)
2. PCNtf
(ABDFHJ)
4. PCNtf
(ABDFHJ)
3. Release saved resource: EF
5. Release saved resource: IJ

## Slide 9: Stateful vs Stateless PCE in RWA
Wavelength block rate under different network load
Wavelength block rate with different PCReq interval

## Slide 10: Next Steps
Refine it according to the feedback from the meeting or mailing list.
More emulation under different condition.

## Slide 11
Thank You！
Comments?