## Slide 1: Extensions to the PCEP to compute service aware LSP.
82nd IETF @ Taipei
draft-dhody-pce-pcep-service-aware
Dhruv Dhody (dhruv.dhody@huawei.com)
Vishwas Manral (vishwas.manral@hp.com)

## Slide 2: Introduction
82nd IETF @ Taipei
Many service providers SLA depends on performance metrics –
  Latency (delay)
  Latency-Variation (jitter)
  Packet loss
Important Applications/Scenarios
  Electronic Financial Market
  High Performance computing on Cloud
Moving forward the service aware WAN will become more and more critical.
Extension to PCEP to support Latency, Latency-variation and Loss as constraints for end to end path computation.

## Slide 3: Requirement for PCEP
82nd IETF @ Taipei
PCE have capability to compute end-to-end path with latency, latency- variation and packet loss constraints.
  In itself
  Combination with other constraints
PCC able to request new constraints in PCReq
  Key constraint to be optimized
  Boundary Condition
Non-Supporting Service aware PCE
PCE returns end-to-end value of the computed path
PCEP should handle multiple domains

## Slide 4: PCEP Extension
82nd IETF @ Taipei
Three new metric types are added
  * T=13(IANA): end-to-end Latency (delay) metric
  * T=14(IANA): end-to-end Latency-Variation (Jitter) metric
  * T=15(IANA): end-to-end Packet Loss metric
As per [RFC5440] the format of the METRIC object body is as follows:
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Reserved | Flags |C|B| T |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| metric-value |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
T (Type - 8 bits): Specifies the metric type.
Three values are currently defined:
* T=1: IGP metric
* T=2: TE metric
* T=3: Hop Counts

## Slide 5: PCEP Extension
82nd IETF @ Taipei
Example:
If a PCC sends a path computation request to a PCE where the metric to optimize is the latency and the packet loss must not exceed the value of M
o First METRIC object with B=0, T=13, C=1, metric-value=0x0000
o Second METRIC object with B=1, T=15, metric-value=M
As explained in [RFC5440], The METRIC object is optional and can be
used for several purposes. In a PCReq message, a PCC MAY insert one
or more METRIC objects:
o To indicate the metric that MUST be optimized by the path
computation algorithm (Latency, Latency-Variation or Loss)
o To indicate a bound on the path METRIC (Latency, Latency-Variation
or Loss) that MUST NOT be exceeded for the path to be considered
as acceptable by the PCC.

## Slide 6: Related work
82nd IETF @ Taipei
WG | ID | Details
MPLS | RFC 6374 | Packet Loss and Delay Measurement for MPLS Networks
 | draft-ietf-mpls-tp-loss-delay-00 | Packet Loss and Delay Measurement for MPLS Transport Profile
 | draft-fuxh-mpls-delay-loss-rsvp-te-ext-00 | RSVP-TE extensions for services aware MPLS
OSPF | draft-giacalone-ospf-te-express-path-02 | OSPF Traffic Engineering (TE) Express Path
ISIS | draft-previdi-isis-te-metric-extensions-00 | IS-IS Traffic Engineering (TE) Metric Extensions
CCAMP | draft-fuxh-ccamp-delay-loss-te-framework | Framework for latency and loss traffic engineering application

## Slide 7: Next Steps
82nd IETF @ Taipei
Continue analysis for
  Inter-Domain (especially Inter-as-link)
  Multi-Layer
  Reoptimization
  Policy Consideration
  P2MP
Managebility and security considerations needs analysis.

## Slide 8: Questions & Comments?
82nd IETF @ Taipei

## Slide 9: Thanks!
82nd IETF @ Taipei