## Slide 1: Extensions to PCEP for Backup Ingress and Egress of LSP
draft-chen-pce-compute-backup-ingress
draft-chen-pce-compute-backup-egress
Huaimo Chen (huaimochen@huawei.com)
Cyril Margaria (cyril.margaria@nsn.com)

## Slide 2: draft-chen-pce-compute-backup-ingress
-03 just posted, looks solid
One major change needs review:
External Source Node Representation
  Option 1: New External Source Node (ESN) Object
  ESN Object Body (IPv4)
External source node IPv4 address (4 bytes)
  Option 2: Existing END-POINTS with new type
Type (11)
External source node IPv4 address (4 bytes)

## Slide 3: draft-chen-pce-compute-backup-egress
-03 just posted, looks solid
One major change needs review:
External Destination Node (EDN) Representation
  Option 1: EDN Object
  EDN Object Body (IPv4)
  Option 2: END-POINTS
  END-POINTS Object Body
Encode of External Destination Nodes (2)
Egress IPv4 address
External Destination IPv4 address
External Destination IPv4 address
……
Egress IPv4 address
External Destination IPv4 address
Egress IPv4 address
External Destination Nodes Type (13)
Egress IPv4 address
External Destination IPv4 address
External Destination IPv4 address
……
Egress IPv4 address
External Destination IPv4 address
Egress IPv4 address

## Slide 4: Next Step
Welcome comments
Request to make it into a working group document

## Slide 5: P2MP LSP Ingress & Egress Local Protection
P2MP
Multicast
Source
Multicast
Receiver
Data
PE6
PE5
PE4
PE3
CE4
CE3
CE2
CE1
New solution:
One P2MP LSP for all: Every part locally protected
Big resource saving, Faster failure recovery
P2MP LSP
Backup LSP
Data
PE1
PE2
CE1
(S,G)Join
BFD
Existing solution: double ingress and every egress
Create two global P2MP LSP from each ingress to egresses, carrying data at same time
External Source Node
Backup Ingress Node
Backup Egress Node
External Destination Node