## Slide 1: The Application of the Path Computation Element Architecture to the Determination of a Sequence of Domains in MPLS & GMPLS draft-ietf-pce-hierarchy-fwk-00.txt
Daniel King, Old Dog Consulting
Adrian Farrel, Old Dog Consulting
Quintin Zhao, Huawei Technology
Fatai Zhang, Huawei Technologies
IETF 82 - Taipei

## Slide 2: Hierarchical PCE (Recap)
The Parent PCE maintains a topology map
  The nodes are the Child domains
  The map contains the inter-domain links
  The TE capabilities of the links are also known
Parent PCE knows the identify and location of the child PCEs responsible for the Child domains
  Statically configured
Domain confidentiality
  A Parent PCE is aware of the topology and connections between domains, but is not aware of the contents of the domains
  Child domains are completely confidential
    One child cannot know the topology of another Child.
    Child domains do not know the general domain mesh connectivity
IETF 82 - Taipei

## Slide 3: Applicability
Inter-domain Path Computation
  When the Domain Path is Not Known
ASON architecture (G-7715-2)
  H-PCE mechanism fits well within the ASON routing architecture
    Multiple Routing Areas
    Multi-level
IGP Areas
  Path computation across multi-area networks consisting of a backbone area and various peripheral areas
Inter-layer
  IP over Optical
IETF 82 - Taipei
Notes: <number>

## Slide 4: Current Status / Next Steps
Relatively stable
  Thorough reviews always welcome.
Solution draft now exists
  draft-zhang-pce-hierarchy-extensions
  Open Issues
    Parent PCE TED Management
    Domain Representation
    Reachability
    OF Codes
Next Steps
  Await resolution of relevant open issues in the solution document.
  Add “Use Cases”.
  Look to develop a scalability analysis.
IETF 82 - Taipei