## Slide 1: PIM ECMP Redirect
draft-ietf-pim-ecmp-01
IETF 82, Taipei
Notes: <number>

## Slide 2: Change Log
First presented to IETF in IETF80
Accepted as WG document after IETF81
Changed name to ECMP Redirect (many thanks to Jeffrey from Juniper)
IETF 82
draft-ietf-pim-ecmp-01
<number>
Notes: <number>

## Slide 3: PIM ECMP Redirect
Current ECMP RPF selection is downstream driven using address hashing
  Does not consider load, cannot handle sticky RPF decisions
  There is no mechanism in PIM to “Assert” between different paths
ECMP Redirect message is proposed to improve control of RPF path selection.
  Sent by upstream routers to “recommend” a different path based on load, administrative preference or other factors
  Allow downstream routers to use information such as available bandwidth to choose an RPF neighbour
IETF 82
draft-ietf-pim-ecmp-01
<number>
Notes: <number>

## Slide 4: PIM ECMP Redirect
Key features
  Triggered by PIM Joins
  Sent in a different subnet (used to choose a path, instead of an RPF neighbour)
  Using “non-routing” metric (uptime, bandwidth etc…)
New PIM Hello Option
IETF 82
draft-ietf-pim-ecmp-01
<number>
Notes: <number>

## Slide 5: Going forward
IANA numbers requested (not granted yet)
  ECM Redirect Hello Option: 32 (0x20)
  ECMP Message Type: 11 (0xB)
  Revisiting IANA PIM registry requirement?
Authors would like to request WG Last Call.
IETF 82
draft-ietf-pim-ecmp-01
<number>
Notes: <number>