## Slide 1: PIM DR Load Balancing
draft-hou-pim-drlb-00
IETF 82, Taipei
{ycai, svallepa, hou }@cisco.com
andy.da.green@bt.com
Notes: <number>

## Slide 2: Agenda
Problem Statement
Solution Overview and Applicability
Protocol Change
Example
Discussion
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 3: Problem Statement
PIM DR is elected based on DR priority or IP address (per RFC4601)
In the last hop LAN, only one router, the DR, is responsible for forwarding
Forwarding load is not distributed
Failover takes longer time
  All forwarding states must be rebuilt on the new DR after a failover
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 4: Solution Overview
Elect multiple forwarders on the last hop LAN
  Each is called a GDR (Group DR)
  Hashing is used to determine which candidate GDR becomes the GDR
Forwarding load is now distributed
During a failover only a subset of the forwarding states need to be rebuilt
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 5: Applicability
Last hop only
  First hop router is determined by incoming Join not DR state
  The complexity of supporting this at FHR outweighs the benefits of distributing load for sending registers
SM/SSM/DM only
Bidir TBD (probably not)
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 6: Protocol Change
GDR Election
  DR election procedures remain unchanged
  A router announces hash masks in new Hello Option TLV to indicate its capability
    Hash masks include RP, Group, Source
  All candidate GDRs must have the same DR priority as the DR
  DR announces the list of candidate GDRs and the hash masks to be used on this LAN
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 7: Protocol Change
Creating forwarding states
  Upon receiving IGMP reports, a candidate GDR runs a hash algorithm to determine if it is the GDR for the RP of the group, the group and/or source
  If it is, it becomes the forwarder on the LAN
  Forwarding states are recalculated if the list of the candidate GDR changes or the hash masks change (per announcement by DR)
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 8: Protocol Change
GDR Assert
  Used to reduce packet loss during GDR state change
  A GDR becoming non-GDR MAY choose not to remove the oif immediately
    This will lead to Assert
  GDR state is preferred before using IP address as a tie-breaker
    See discussion for non-ECMP case
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>

## Slide 9: Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>
A
B
C
D
E
A, B, C, D have the same DR priority
A would become the DR (per RFC4601)
RP mask is 0.0.0.0
Group mask is 0.255.0.0 (IPv4)
Source mask is 0.0.0.0
Notes: <number>

## Slide 10
B
B comes up first, announces mask (0, 0.255.0.0, 0)
When B becomes the DR, it also includes its own address in the LB TLV
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>

## Slide 11
A
B
A comes up, announces mask (0, 0.255.0.0, 0) first
A wins DR election, announces both A and B in the LB TLV.
B loses DR election, announces mask only
  Some groups for which B isn’t GDR anymore may experience traffic disruption
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>

## Slide 12
A
B
Since there are only two routers, A will be the GDR for groups with hash value 0
  E.g., 239.0/16, 239.2/16, …
B will be the GDR for groups with hash value 1
  E.g., 239.1/16, 239.3/16 …
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>

## Slide 13
A
B
E
E comes up, announces mask (0, 0.255.0.0, 0)
E loses DR election due to DR priority
  Continues to announce mask (0, 0.255.0.0, 0)
  A will not include E in the LB TLV
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>
Priority10
Priority10
Priority 9

## Slide 14
A
B
C
D
E
C and D come up, announce mask (0, 0.255.0.0, 0)
A now announces A, B, C, D in LB TLV
  A will be GDR for 239.{0, 4, 8…}.0.0/16
  B will be GDR for 239.{1, 5, 9…}.0.0/16
  C will be GDR for 239.{2, 6, 10…}.0.0/16
  D will be GDR for 239.{3, 7, 11…}.0.0/16
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>

## Slide 15
A
B
D
E
C is shutdown, or its DR priority decreases
A now announces A, B, D in LB TLV
  A will be GDR for 239.{0, 3, 6…}.0.0/16
  B will be GDR for 239.{1, 4, 7…}.0.0/16
  D will be GDR for 239.{2, 5, 8…}.0.0/16
Example For SM (239.0.0.0/8)
IETF 82
draft-hou-pim-drlb-00
<number>

## Slide 16: Discussion
Welcome comment/collaboration, in particular,
  Hash masks priority between RP mask and Group mask
  Hash algorithm
  GDR Assert: should metric be considered first after GDR state?
Working Group document?
Thank You!
IETF 82
draft-hou-pim-drlb-00
<number>
Notes: <number>