## Slide 1: IGMP/MLD-Based Explicit Membership Tracking Function for Multicast Routers draft-ietf-pim-explicit-tracking-00
Hitoshi Asaeda
Nicolai Leymann
82nd IETF, November 2011, Taipei, Taiwan
<number>
82nd IETF, November 2011.

## Slide 2: Objectives
The explicit tracking function on routers works for:
  Per-host accounting
  Reducing the number of transmitted Query and Report messages
  Shortening leave latencies
  Maintaining multicast channel characteristics (or statistics)
<number>
82nd IETF, November 2011.

## Slide 3: Objective 1: the Number of Messages Transmission
Whenever a router (querier) receives the State-Change Report, it sends the corresponding Group-Specific or Group-and-Source Specific Query messages to confirm whether the Report sender is the last member host or not.
<number>
82nd IETF, November 2011.

## Slide 4: Lowering Specific Query Transmission
A router (querier) enabling the explicit tracking function does not need to always ask Current-State Report message transmission to the member hosts whenever it receives the State-Change Report
  Because the router can expect whether the State-Change Report sender is the last remaining member of the channel or not
<number>
82nd IETF, November 2011.

## Slide 5: Objective 2: Leave Latency
[Last Member Query Interval] (LMQI) and [Last Listener Query Interval] (LLQI)
  The maximum time allowed before sending a responding Report
[Last Member Query Count] (LMQC) and [Last Listener Query Count] (LLQC)
  The number of Group-Specific Queries or Group-and-Source Specific Queries sent before the router assumes there are no local members
[Last Member Query Time] (LMQT) and [Last Listener Query Time] (LLQT)
  Total time the router should wait for a report, after the Querier has sent the first query
<number>
82nd IETF, November 2011.

## Slide 6: Shortening Leave Latencies
[Last Member Query Timer (LMQT)] and [Last Listener Query Timer (LLQT)]
  Default: LMQI * LMQC (= 2 sec.)
  Shorter value contributes to shortening leave latency
  Example:
    LMQC = 1, then LMQT = 1 sec.
    LMQI can be shorter, e.g., 0.5 sec.
Note
  There is a risk that a router misses Report messages from remaining members if the router adopts small LMQC/LLQC
  However the wrong expectation would be lower happened for the router enabling the explicit tracking function.
<number>
82nd IETF, November 2011.
Notes: <number>

## Slide 7: Membership State Information
Membership state information
  (S, G, Number of receivers, (Receiver records))
  Receiver records
    (IGMP/MLD Membership/Listener Report sender's addresses)
ASM
  “S” is with “Null”
EXCLUDE mode (S,G) join
  Integrate (*,G) join into the state information
<number>
82nd IETF, November 2011.

## Slide 8: Compatibility
Not work for IGMPv1/v2 and MLDv1
  Because of the Report suppression mechanism
  Tracking router keeps the current state as is
Not work for IGMPv3/MLDv2 router changing its compatibility mode to the older version
  The router keeps the current state as is
<number>
82nd IETF, November 2011.

## Slide 9: Open Issues in Interoperability with Non-supported/Disabled Routers
In case when querier enables exp. tracking but non-querier(s) do not support or disable it
  Querier does not query to confirm the last member (when it knows there are other members), but non-querier (who is a forwarder but does not know other members) prunes the state
Possible solutions
  Disable exp. tracking function when [Other Querier Present Interval] is not 0?
    But routers SHOULD be able to configure disabling this disable function to avoid DoS
  Preferably, new IGMP/MLD message for informing that querier/non-querier(s) enables/disables exp. tracking and synchronizing the behavior is defined?
82nd IETF, November 2011.
<number>

## Slide 10: Next Step
Intended status
  Informational RFC
Document improvement
  Address open issue
Comments?
<number>
82nd IETF, November 2011.