## Slide 1: IETF Taiwan Multicast-only Fast ReRoute (MoFRR)
Clarence Filsfils
Apoorva Karan
Dino Farinacci
November, 2011

## Slide 2: Agenda
Problem Statement
Solution Statement
Two-Plane Network Design
Generalization to Non-ECMP
Failure Detection
IPR Disclosure

## Slide 3: Problem Statement
<50msec upon network outage

## Slide 4: Solution Statement
Fast switch-over on pre-installed secondary and disjoint path
Optimized for simplicity
  Similar trade-off to LFA FRR

## Slide 5: Advantages
Incremental deployment at the edge, without core upgrade/specialization
No planning for any extra backup bw
No dependency on IGP convergence
An alternative to source redundancy, but
  Don’t have to provision sources
  Don’t have to sync data streams
  No duplicate data to multicast receivers

## Slide 6: Disadvantages
Topology dependent
  Similar to LFA FRR
  Not meant to be a generic solution for all topologies. Rather, a simple solution that applies to a frequent network design
  Planning tool available to optimize topology for MoFRR
Two behaviors
  ECMP and non-ECMP

## Slide 7: ECMP Example
S
R
A
B
C
D
join
path
data path
alt
path
alt data path
wasted bandwidth
wasted bandwidth
R
not
1) D has ECMP path {BA, CA} to S
2) D sends join on RPF path through C
3) D can send alternate-join on BA path
4) A has 2 oifs leading to a single receiver
5) When RPF path is up, duplicates come to D
6) But D RPF fails on packets from B
7) If upstream of D there are
receivers, bandwidth is only
wasted from that point to D
8) When C fails or DC link fails, D makes
local decision to accept packets from B
9) Eventually unicast routing says B is new
RPF path
rpf path (RPF join)
alt join (sent on non-rpf)
redundant path
link down or RPF-failed packet drop
data path

## Slide 8: Two-Plane Network Design
Many SP networks apply the Two-Plane Design
  two symmetric backbone planes (green and red)
  interconnected by grey links with large metrics to ensure that a flow entering the red plane goes all the way to its exit via the red plane
  pop’s are dual-homed to each plane
  important content (IPTV source) is dual-homed to both planes
IPTV source
Pop2
PopN
Notes: Transcript:
So I'll first explain this, and then I'll explain what we do with this, which is the switchover or the repair. This is basically a Deutsche Telekom design, but I think most of Europe is like this. And unfortunately in the US it's getting in this direction because there's a lot of like thinking to evolve the backbones with the huge increase of the traffic. So there are several projects where they are re-architecting the backbone, and they are getting closer to this. Hopefully they'll get to this because there are lots of benefits from this. But in Europe it's pretty common to have this. So the network is built in the backbone with two meshes, which are exactly symmetric. And so for example in Paris you have two backbone routers in two different buildings. In London you have two backbone routers in two different buildings, same in Frankfurt. And so you have always like a blue router and a red router so that you have also fire section or like if there is a terrorist attack they are isolated physically from each other. So you have a blue backbone and a red backbone with symmetry, and they are interconnected with gray links. These gray links, they have a poor IGP metric because the idea is that when a flow gets inside the red backbone, it will go all its way to the destination via the red backbone. When a flow becomes red, it stays red until the end. When a flow becomes blue, it stays blue until its end. And so you would need partitioning of the red plane to force the red flows to the blue plane because it's not like in each plane you have redundancy. And so obviously one single failure is not going to partition the blue plane. So you have ECMP blue or red, but within blue you have ECMP. And within red you have ECMP. So for example BT21C was built like this. And on top of the blue and red, in blue you had three ECMP from the PoP and so on, and then eight in the backbone. So there are variation with a lot of ECMP path there. One thing is that when we talk about IPTV and the resiliency property, we specifically focus about TV channels that are watched by many people or they watch it with KLS. If they are watched by many people, it means that our receivers are everywhere. So it means that the tree is dense.

## Slide 9: Two-Plane Network Design
An IPTV SSM Tree for a premium channel is densely covering the two-plane design
Dense trees : key to analysis. For IPTV, we assume there are many receivers
From a capacity planning viewpoint, all Green and Red routers in a PoP are or must be assumed to be connected to the tree
IPTV source
Pop2
PopN
Notes: Transcript:
It's key for the analysis. With this assumption, this topology, the fact that the trees you care about are densely watched, we're going to see that it's just automatic to build disjoint trees and there is zero impact on capacity planning. Doing live-live doesn't cost you any megabits of additional bandwidth to the contrary of what could be thought. Why? If I am a PE in PoP1 and I receive an IGMP join for CNN, I have two path to CNN, which is my yellow circle over there. I can go via blue or red. Here you don't know. It's statistical. We do hash on S-Comanche. Let's say that the first PE does a hash and he selects let's go left, so blue. So he's going to send a PIM join on the blue distribution router. And so it creates the first branch of the CNN tree. Then the next PE also receive an IGMP join for CNN. Same dilemma for him, left or right? He takes a hash; here, let us say picks the same. So he sends a PIM join and it draft immediately in the PoP. Now if you have another PE, then statistically you'll have always one that will pick the red path. And so it will build another disjoin path. And so if you go on through all the PEs like this, we're going to see two properties. The first property is that any backbone router is part of the tree. Just because the branches come from all over the place, CNN is densely watched in the topology. So backbone routers are anyway part of the tree. Worse, from a PoP viewpoint the two distribution routers are connected all the time in two ways to CNN. And these two connection today in these networks are disjoint. This is not something new. It's the way IPTV is being done at France Telecom today. This is the way IPTV is being done in Deutsche Telekom today. And so the only question when you see this, and that's France Telecom that basically told us this, is, Is it not possible to just break the loop and just add in this join there, such that the PE would be joined on two branches? And that's basically MoFRR. MoFRR from a routing component is that if you receive on IGMP join for CNN, you lookup in the routing table. If there are ECMP path to it you select two, the primary where you send your PIM join, a secondary that through the links database, you pick the most disjoint ones. And so if the primary is blue, it's obvious from the links-type topology that the most disjoint is red. And you send another PIM join. This PIM join, is it different? No, it's exactly the same PIM join as the primary one. So it's always a property of the fast convergence, BGP PIC, IPFRR. It's all incremental deployment; no standardization at the IETF. So you do not need any interoperability. We don't want to go to the IETF for this; there's no need.

## Slide 10: MoFRR Applied to Two-Plane Network Design
MoFRR only needs to be deployed on PE’s (!)
Does not create any additional capacity demand (!)
Disjointness does not need to be created by explicit routing techniques. This is a native property of the design (!)
Pop1
IPTV source
PopN
Notes: Transcript:
So by simply loading MoFRR capability on the PE, we are going to let them in the simple topology send an (inaudible) join on the other link to the distribution router in the PoP. And so from a Deutsche Telekom viewpoint, you get your PEs and they are all the time fed by two disjoints feed of CNN. In the data plane we only receive packets if they are matching the RPF interface. So the RPF interface is the primary interface. So it means that we are leveraging the fact that data plane is doing drop on RPF failure, which is for CRBU we do it so we can make this assumption. So it means that the packets that are coming from the red branch to this PE are dropped here because they are not coming from the RPF interface. And so this is the additional component we're going to look at. How are we going to change the RPF interface when the primary path fail to failover on the backend? Before doing this, two generalization. For Deutsche Telekom we would be fine like this, and France Telecom partially. But there are two generalization we added to extend the scope of topology that we could cover. And don't hesitate to talk to us if you would have something else in mind. Likely we can find ways to extend a bit more.

## Slide 11: MoFRR Generalization to Non-ECMP
Re-use LFA-FRR intelligence to choose a loop-free alternative
Sends an additional PIM join to any IGP neighbor who is strictly closer to the source than you because you’re sure that router will never send a join to you
  If multiple candidates, leverage LSDB to choose the most disjoint candidate
Notes: Transcript:
But the first extension is to reuse IPFRR intelligence. Exactly like IPFRR, in a non-ECMP case I can choose the equivalent of a loop-free alternate. So if I compute that to go to CNN my left arm is the shortest path and there is no other ECMP choice, but I am connected on my right arm to a node, and from the links-type topology I can compute it, he is closer, strictly closer to a CNN than I am, then I can send him a join as well because I am sure he will never do the same to me. I will not create any PIM loop by doing it because he's closer. So if he would use the same algorithm, he would not send a PIM join at me. So that's the first thing. We compute what is the visibility of our neighbors. If they are closer than us and we'd like to use them, then we send a PIM join to them. And we use the topology in order to select the neighbor who is closer to the source than us and whose path will be the most efficient compared to our primary path.

## Slide 12: MoFRR and Generic Topology
Capacity Planning tool available to assess MoFRR coverage
And optimize it
  Topology changes
  MoFRR deployment at core locations
If the topology does not support natural disjoint paths, then extra cost and complexity need to be incurred (MT, RSVP) to create these disjoint paths.
Notes: Transcript:
If your topology does not give you the disjoint trees for free, then obviously you need to have more complex technology, multi-topology routing, traffic engineering with RSVP tunnels. Yes, but the impact is on the complete network. MTR will not work before the entire network has been migrated to MTR. So the complexity that you're getting on the entire backbone for specific service is huge.

## Slide 13: Failure Detection Algorithm
50 ms MoFRR
  IPTV Inter-packet Gap is 0(1msec).
  Monitor SSM (S, G) counter and if no packet received within 50msec switch onto the backup branch
  Local detection with end-to-end protection!
MoFRR Zero-Loss
  IPTV flows to use RTP
  MoFRR PE device to repair any loss thanks to RTP sequence match on the disjoint branch

## Slide 14: Failure Detection Algorithm
MoFRR based on RIB trigger
  Upon failure along the primary path, IGP converges and the best path to the source is modified.
  This triggers the use of the already-established MoFRR backup branch.
  Gain over FC: no time incurred due to the building of the new branch
  Target: subx00msec
Connected link failure
  This option makes sense when MoFRR is deployed across the network (not only at PE).
Notes: Transcript:
Now reality what we are doing in IOX 3.8, so it's committed for 3.8. We are going to do MoFRR based on IGP Trigger. So it's a first step. Next we will do 50 milliseconds with the counter check. But as a first step in 3.8, we're going to allow a PE to send two PIM joins, install only a primary RPF, drop all the packets on the backup branch, and then simply trust the IGP to detect any failure converge. And when the IGP converge it updates the best path in the ring. And this will be the trigger to PIM to change the RPF. And we know that the IGP is sub-200 milliseconds, so our target is to be sub-200 milliseconds with this first phase. And that's really like minimum amount of work because it only requires PIM multicast code. And so we just receive the code drop, and we're doing the characterization and insight in Brussels started yesterday. So you should have the first results I would say in two weeks.

## Slide 15: MoFRR and MPLS Transport
MoFRR is as applicable to MLDP as to PIM
Notes: Transcript:
MoFRR is entirely applicable to MPLS. I mean, if you send two PIM joins or two MLDP joins, it's exactly the same. So like IPFRR, IPFRR is entirely applicable to MPLS.

## Slide 16: IPR Disclosure
MoFRR Patent Application
  Filed April 26, 2007
MoFRR extensions for Ring Topologies
  Filed February 12, 2008

## Slide 17: Going Forward
Work is done in RTGWG
Generalize the solution to include mLDP
There are no protocol changes