## Slide 1: Avoiding Unnecessary Upstream Traffic in Bidir-PIM
Jeffrey Zhang
Weesan Lee
Juniper Networks
82th IETF, Taipei

## Slide 2: Scenario #1 of unnecessary upstream traffic
The tree depicts all routers and their RPF interfaces (towards RP)
  Assuming RPA is on a loopack interface
    More general situation described later
No receiver anywhere – traffic should be stopped at the FHR R3/R7
RP
R1
R2
R3
R4
R5
R6
R7
R8
src1
src2
traffic
traffic to be
avoided

## Slide 3: Scenario #2 of unnecessary upstream traffic
RP
R1
R2
R3
R4
R5
R6
R7
R8
rcvr1
rcvr2
src3
src1
src4
src2
(*,g)
(*,g)
(*,g)
(*,g)
traffic
traffic to be
avoided

## Slide 4: RP-Prune procedures for scenario #1
RP has (*, G-prefix) notification route
  vs. the normal “forwarding to RPL” route
  Traffic hitting the route triggers throttled control plane notification
    Indicating traffic is being received unnecessarily
      Otherwise it would have hit specific (*,G) forwarding route
  The notification triggers RP-Prune out of the incoming IF
    Multicast to ALL-PIM-ROUTERS
      Interface-wide RP-Prune
Upon receiving the RP-Prune, downstream router installs (*, G) notification route
  Subsequent traffic hits the (*, G) notification route, triggering RP-Prune further downstream, instead of being forwarded upstream
RP-Prune is data-triggered hop-by-hop:
  by the pre-installed (*,G-prefix) notification route on RP
  by the triggered (*,G) notification route on downstream routers

## Slide 5: RP-Prune scenario #1 illustration
RP
R1
R2
R3
R4
R5
R6
R7
R8
src1
src2
RP-Prune

## Slide 6: RP-Prune procedures for scenario #2
RP sends periodic neighbor-specific RP-Prune to the only downstream neighbor in (*,G) join state
  Assumes Explicit Tracking
    If ET is not used, another downstream with the (*,G) state needs to trigger overriding (*,G) join upon receiving the RP-Prune, and the target of RP-Prune needs to ignore the RP-Prune when receiving that overriding (*,G) join
Downstream router prunes the RPF IF from (*,G) forwarding route’s OIF list
  Stops traffic from going upstream
Downstream router further propagates RP-Prune to its only downstream neighbor
  Terminates when there are more than one downstream IF/neighbor – R4 in the example

## Slide 7: RP-Prune scenario #2 illustration
RP
R1
R2
R3
R4
R5
R6
R7
R8
rcvr1
rcvr2
src1
src3
src2
src4
(*,g)
(*,g)
(*,g)
(*,g)
RP-Prune

## Slide 8: RP-Prune states
Upstream IF & Neighbor
List of downstream IF where RP-Prune was sent
  Flag for interface-wide or nbr-specific RP-Prune
  List of downstream neighbor on the IF
    A nbr-specific prune was sent to it, or
    A RP-Prune-Keep was received from it
      A timer to time out if downstream stops refreshing RP-Prune-Keep
      Interface-wide RP-Prune case (scenario #1)

## Slide 9: RP-Prune state maintenane: Interface-wide RP-Prunes (Scenario #1)
Maintained from downstream upwards
  FHR keeps receiving data traffic, keeps the RP-Prune state alive for the incoming interface, and refreshes RP-Prune-Keep towards its upstream
    Each hop will refresh its upstream by RP-Prune-Keep
  After source stops sending, FHR times out its RP-Prune state, and sends RP-Prune-Cancel upstream
    Each hop propagates the RP-Prune-Cancel if it no longer has other downstream in the RP-Prune state (i.e., no other sending branches)

## Slide 10: RP-Prune state maintenance: Neighbor-specific RP-Prunes (Scenario #2)
Maintained from RP downwards
  RP refreshes RP-Prune as long as it has only one downstream neighbor
  Each hop propagates the RP-Prune unless it has more than one downstream IF/Nbr

## Slide 11: RP-Graft Procedures
RP sends interface-wide RP-Graft to wherever it sent interface-wide RP-Prune before, when it gets initial corresponding (*,G) join state
  also sends neighbor-specific RP-Prune to the new/only downstream neighbor (scenario #1 becomes #2)
Any router (RP or not) who sent Neighbor-specific RP-Prune before triggers RP-Graft when it first gets more than one downstream IF/nbr for a (*, G) join state
  Neighbor-specific RP-Graft sent to the downstream neighbor recorded in the RP-Prune state
Upon receiving RP-Graft, downstream routers:
  Removes (*,G) notification route (scenario #1), or
  Adds RPF IF to (*,G) forwarding route (scenario #2)
  Reply with RP-Prune-Cancel as acks
    Upstream retransmits RP-Graft until all applicable downstream neighbors in the RP-Prune state have ack’ed

## Slide 12: What if RPA is not on a loopback IF?
Normal Bidir-PIM behavior:
  Traffic always forwarded to the RPL
  Join/Prunes not sent to the RPL
Modified behavior:
  Join/Prunes sent to ALL-PIM-ROUTERs on RPL
    But not further downstream
  Traffic forwarded to the RPL only if a corresponding join has been received on the RPL
  Each router on the RPL is called a virtual RP and follows the RP-Prune/Graft procedures defined earlier
    Another virtual RP considered as a downstream for a particular group if a join has been received from it
    RP-Graft/Prune/Prune-Keep/Prune-Cancel messages are not sent to the RPL though

## Slide 13: Virtual RP illustration
R1
R5
R6
R3
R4
R2
RPA
(*,g)
(*,g)
(*,g)
(*,g)
(*,g)
rcvr
Virtual RP R1~R3 all have only one downstream (R4 on the RPL), but do not send RP-Prune (to R4 on the RPL)
Virtual RP R4 has one downstream R6 and sends RP-Prune to it
If R5 gets a receiver, R4 will send RP-Graft to R6 because it now has two dowstream: R6 and R3
RPL

## Slide 14: Handling of topology changes
When RPF IF/nbr changes
  Sends RP-Graft downstream
  Remove RP-Prune states
    Remove (*,G) notification routes, or
    Add back, or add new RPF IF to (*,G) forwarding route

## Slide 15: Scaling properties
Scenario #1
  Data-driven (*,G) RP-Prune states on relevant sending branch only
    For traffic that nobody wants
      traffic with receivers does go through w/o data-driven events
    Time out when source stops sending
Scenario #2
  Control-driven (*,G) RP-Prune states on relevant single-downstream routers only
Minimum states for stopping unnecessary upstream traffic

## Slide 16: Next steps
Fill in some missing details in draft -00
Seek comments and WG adoption