## Slide 1: IETF Taiwan draft-wijnands-pim-source-discovery-bsr-00
IJsbrand Wijnands, ice@cisco.com
Stig Venaas, stig@cisco.com
Michael Brig, michael.brig@mda.mil
November, 2011

## Slide 2: Problem Statement
Highly redundant Multicast network.
No single point of failure.
Simplification.
Supports source discovery.

## Slide 3: Problem Statement
This sounds a lot like PIM SSM, no?
Yes, it does 
But, source discovery remains to be challenging in order to do SSM.
  applications not capable.
  IGMPv3 not available.
  Sources not known in advance.
SSM Mapping often used otherwise.

## Slide 4: Problem Statement
This proposal focuses on a specific sort of deployment where;
The sources are not known in advance.
Its not important to deliver the first (couple) of packets.
Relatively low number of flows < 10K

## Slide 5: Solution
The First Hop Router (FHR) detects a active source.
  The packet is NOT PIM registered.
It uses RPF flooding to distribute the Source – Group mapping in network.
Last Hop Routers that receive the SG-mapping and have local interest join the (S,G) tree via PIM.

## Slide 6: RPF flooding
There are already 2 protocols that flood ‘RP – Group’ mappings through the network
  BSR
  Auto-RP
Why not re-use one of these to flood the S-G mappings.
BSR seems to be a logical choice.

## Slide 7: BSR
Defined new BSR encoding to include Source.
The Source sort of replaces the RP.
Each FHR becomes a BSR router for advertizing the Source directly connected to it.

## Slide 8: Advantages
Allows to do ‘sparse-mode’ without RP’s
Simplification of the network.
Highly redundant, no single point of failure.

## Slide 9: Disadvantages
Initial packet(s) received by FHR are dropped.
  This is fundamentally different from PIM Sparse.
All potential last-hop routers will need to cache all S-G mappings.

## Slide 10: First packet
PIM sparse-mode made a very large sacrifice in order to support delivering the first packet.
Applications like SDR depend on it…
There are many applications of multicast that don’t depend on the first packet, like video for example.
Many deployments could benefit.

## Slide 11: PIM Bidir
Applications that are sensitive to the first packet may use PIM Bidir.
These are mostly low bandwidth, so no worry about best path forwarding.
With PIM Bidir the first packet is always delivered.

## Slide 12: Conclusion
Until the day comes that applications becomes SSM aware;
This could be a good intermediate solution.
It could co-exist with existing PIM modes, and do this only for specific group ranges.

## Slide 13: Going forward
Like to get feedback from the group.
Adopt as a WG doc?

## Slide 14: Questions?