## Slide 1: PPSP Tracker Protocol
draft-gu-ppsp-tracker-protocol
PPSP WG
IETF 82 Taipei
Rui Cruz (presenter)
Mário Nunes, Yingjie Gu, Jinwei Xia, David Bryan, João Taveira, Deng Lingli

## Slide 2: Main functional entities related with PPSP
Client Media Player
  is the entity providing a direct interface to the end user at the client device, and includes the functions to select, request, decode and render contents.
  interfaces with the Peer using request and response mechanisms.
Peer
  Is a logical entity at the client device embedding the P2P core engine, with a client serving side interface to respond to Client Media Player requests and a network side interface to exchange data and PPSP signaling with Trackers and with other Peers.
Tracker
  is a logical entity that maintains the lists, as well as the status, of PPSP active peers storing and exchanging chunks for a specific media content.

## Slide 3: Terminology
SEGMENT (of partitioned media)
  is a resource that can be identified by an ID, an HTTP-URL or a byte-range, and used by a Peer for the purpose of storage, advertisement and exchange among peers.
SUBSEGMENT (of partitioned media)
  the smallest unit within segments which may be indexed at the segment level.
CHUNK
  is a generic term used to refer to a SEGMENT or SUBSEGMENT of partitioned streaming media.

## Slide 4: Changes since version 5
This draft corresponds to an enhanced merge of:
  draft-gu-ppsp-tracker-protocol-05
  draft-cruz-ppsp-http-tracker-protocol-01
Includes detailed messages syntax and XML-Schema
Addresses Authentication & Security aspects based on SASL
Adds Support for NAT Traversal service via ICE (STUN-Like Tracker)
Can Support DECADE interoperation
Is compatible with Distributed trackers organized by RELOAD
Provides Full PPSP Requirements compliance.
Changes in messages
  Removed STAT_QUERY message
  Re-designed FIND message
  Re-designed JOIN message

## Slide 5: Protocol Design
The PPSP Tracker Protocol is not used to exchange actual content data with Peers, but information about which Peers can provide which pieces of content.
The protocol design supports distributed tracker architectures, providing robustness to the streaming service in case of tracker node failure.
The PPSP Tracker Protocol is a request-response protocol.
  Requests are sent, and responses returned to these requests.
  A single request generates a single response.
The Tracker can provide NAT traversal services (STUN-like Tracker) by discovering the reflexive address of a Peer via PPSP Tracker Protocol messages

## Slide 6: Protocol Overview
To join an existing P2P streaming service and to participate in content sharing, any Peer must locate a Tracker and:
  Establish a CONNECTion to the system
  JOIN a swarm of Peers streaming a content
  Obtain or FIND a selected List of those Peers
A Peer can LEAVE a swarm but keep active in the P2P streaming service for other swarms
A Peer sends STAT-REPORTs to the Tracker to inform about its status and supply statistic information.
To terminate all its activity in the P2P streaming service the Peer DISCONNECTs for the Tracker.

## Slide 7: A Typical PPSP Session

## Slide 8: Request Messages
CONNECT:
  used when a Peer “connects” to the system.
    The Peer provides its PeerID, the IP addresses (IPv4, IPv6) of its network interfaces and attributes related with NAT traversal.
    The Tracker records the PeerID, connect-time, peer IP addresses and link status.
    The method allows a security layer to be negotiated in the authentication protocol exchange between the Peer and the Tracker

## Slide 9: Request Messages
JOIN:
  used by a Peer to notify the Tracker that it wishes to participate in a particular swarm (for both VoD or Live streaming modes):
    The tracker adds the Peer to the candidate peers list for the swarm.
    The joining peer may have none or just some chunks (LEECH), or all the chunks (SEED/LIVESEED) of a content.
    The type of participation in the swarm is announced and can be SEED, LIVESEED or LEECH
    The Peer may specify the starting Chunk of a content when joining, restrict the number of candidate peers to receive form the Tracker and provide NAT capabilities.

## Slide 10: Request Messages
STAT_REPORT:
  used by a Peer to inform the Tracker on statistic and status data:
    Is initiated by the peer, periodically while active.
    Contains activity statistics.
    Contains ChunkMaps for all the streaming contents the Peer is currently joined.

## Slide 11: Request Messages
FIND:
  allows peers to request to the Tracker the peer list for the swarm or for specific chunks of a media content:
    The Peer may specify the Chunks of interest in a content, restrict the number of candidate peers to receive form the Tracker and provide NAT capabilities.

## Slide 12: Request Messages
LEAVE:
  used by a Peer to notify the Tracker that it no longer wish to participate in a particular swarm (for both VoD or Live streaming modes):
    The Tracker deletes the corresponding activity records related to the peer.
    The Peer may however continue active in other swarms.

## Slide 13: Request Messages
DISCONNECT:
  Used when the Peer intends to leave the system and no longer participate in any swarm:
    The Tracker deletes the corresponding activity records related to the peer (including its status and all content status for all swarms)
    The Tracker MUST remove the peer from the peer lists and from all swarms the peer was joined.

## Slide 14: Messages Syntax
The PPSP Tracker Protocol messages follow the standard formats for HTTP Requests and Responses with XML encoded message bodies.
<Method> /<Resource> HTTP/1.1
Host: <Host>
Content-Lenght: <ContentLenght>
Content-Type: <ContentType>
<Request_Body>
HTTP/1.1 <StatusCode> <StatusMsg>
Content-Lenght: <ContentLenght>
Content-Type: <ContentType>
Content-Encoding: <ContentCoding>
<Response_Body>

## Slide 15: Messages Syntax
The PPSP Tracker Protocol message bodies are encoded in XML.
All Request messages except CONNECT MUST include authentication identity (PeerID) and authentication token.
The Response messages MAY use Content-Encoding entity-header with "gzip" compression scheme.
<?xml version="1.0" encoding="utf-8"?>
<ProtocolName version="#.#">
<Method>***</Method>
<Response>***</Response>
<PeerID>***</PeerID>
<AuthToken>***</AuthToken> <!-- on Request except CONNECT-->
<TransactionID>###</TransactionID>
...XML information specific of the Method...
</ProtocolName>

## Slide 16: Final Remarks
The PPSP Tracker Protocol (as well as the PPSP Peer protocol) are bound to VoD streaming or Live streaming of multimedia, not “file sharing”.
PPSP should be open to support:
  Structured Media streaming (SVC/MDC/MVC/multi-bitrate)
  Unstructured Media streaming (AVC or other formats)
  but not being involved in the decoding/encoding processes.
The Media Player application is the entity that should "know" (via a requester/re-assembler module) how and what to request (to a Peer) and decode the received Structured Media (from the Peer) in order to “prepare” it to present to the User.

## Slide 17
The Authors would like to ask for the Tracker Protocol defined in this draft to be adopted as PPSP Working Group draft

## Slide 18: Thank You !
Comments are welcomed!