## Slide 1: MAC Address Withdrawal Over Static PW draft-boutros-pwe3-mpls-tp-mac-wd-02.txt

## Slide 2: Background
MAC withdraw mechanism over static PW:
  Based on PW OAM message defined in “draft-ietf-pwe3-static-pw-status-xx.txt”
  A given MAC withdraw notification is not refreshed forever
  Acknowledgment of OAM messages is mandatory
  Duplicate messages are identified using sequence number in order to avoid repeated (unnecessary) flushing of MAC address(es)

## Slide 3
MAC Withdraw OAM Message
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| 0 0 0 1 |Version| Reserved | 0xZZ PW OAM Message |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| ACH TLV Header |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Refresh Timer | TLV Length |A| Flags |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|1|0 | Sequence Number TLV | TLV Length |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Sequence Number |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
| MAC List TLV |
~ ~
| MAC Flush Parameter TLV (optional) |
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+

## Slide 4
MAC Withdraw OAM Message (cont’d)
Refresh Timer field is not used
Message without Sequence Number TLV is dropped
ACK message (A bit set) does not include MAC TLVs

## Slide 5
Operation
A sender re-transmits a MAC withdraw message with a given sequence number if it does not receive ACK for that sequence number
A receiver always acknowledges any incoming MAC withdraw message (new or duplicate)
A receiver processes a MAC withdraw message only if the sequence number of that message is greater than that of the last processed MAC withdraw message

## Slide 6
Operation (cont’d)
A sender re-transmits a MAC withdraw message with a given sequence number if it does not receive ACK for that sequence number
A receiver always acknowledges any incoming MAC withdraw message (new or duplicate)
A receiver processes a MAC withdraw message only if the sequence number of that message is greater than that of the last processed MAC withdraw message

## Slide 7
IANA Allocation
LDP TLV type name space:
  Sequence Number TLV

## Slide 8
Thank You !