## Slide 1: Signaling Root-Initiated Point-to-Multipoint Pseudowire using LDP draft-ietf-pwe3-p2mp-pw-03.txt

## Slide 2: Background
Specifies a mechanism to signal Point-to-Multipoint (P2MP) Pseudowires (PW) tree using LDP.
Supports unidirectional P2MP traffic from Root-PE to Leaf-PE(s) as well as OPTIONAL P2P traffic from any Leaf-PE to Root-PE.
Supports RSVP-TE or mLDP signaled transport LSPs.
Introduces new FECs, TLVs, and LDP capability.

## Slide 3
Label Mapping Message for Upstream-Assigned Label
A mandatory message sent by a Root-PE to all Leaf-PE(s).
Contains:
  A P2MP Upstream PW FEC element (new)
  Interface Parameters TLV (new sub-TLV)
  Group ID TLV
  A Transport LSP TLV (new)
  A label TLV for the upstream-assigned label used by a Root-PE to forward traffic to Leaf-PE(s).

## Slide 4
Label Mapping Message for Downstream-Assigned Label
An optional message sent by a Root-PE to a given Leaf-PE.
Contains:
  A P2P Downstream PW FEC element (new)
  A label TLV for the downstream-assigned label used by a given Leaf-PE to forward traffic to a Root-PE.

## Slide 5
Selective Tree Interface Parameter Sub-TLV
To support selective multicast traffic, a new Interface Parameter sub-TLV is defined according to the format described in [RFC4447]:
+---------------------------------------------+
| Multicast Source Length (1 Octet) |
+--------------------------------------------- +
| Multicast Source (variable length) |
+---------------------------------------------+
| Multicast Group Length (1 Octet) |
+-------------------------------------------- +
| Multicast Group (variable length) |
+-------------------------------------------- +

## Slide 6
P2MP PW LDP Capability
An LSR having P2MP PW capability MUST recognize both P2MP Upstream FEC Element and P2P Downstream FEC Element in LDP Label Binding Message.

## Slide 7
IANA Allocations
FEC type name space:
  P2MP PW Upstream FEC Element
  P2P PW Downstream FEC Element
LDP TLV type name space:
  Transport LSP TLV
  P2MP PW Capability TLV
LDP MP Opaque Value Element type name space:
  L2VPN-MCAST application TLV
Pseudowire Interface Parameters Sub-TLV name space:
  Selective Tree Interface Parameter sub-TLV.

## Slide 8
Thank You !