## Slide 1: Pseudowire Communities draft-pkwok-pwe3-pw-communities-02
Paul Kwok
Pranjal Dutta
Frederic Jounay
draft-pkwok-pwe3-pw-communities-02
IETF-82

## Slide 2: History and Updates
Presented version-01 in IETF-81. Published version-02 after addressing comments.
Extended the scope of PW Communities Concept and Applicability.
Generalized definition and encoding PW Communities for extendibility.
IETF-82

## Slide 3: Objectives (Recap)
Generic method to simplify provisioning of Dynamic Pseudowires.
Aid in policy administration during dynamic multi-segment pseudowire (Dyn MS-PW) set-up across various S-PEs with minimal overhead.
IETF-82
draft-pkwok-pwe3-pw-communities-02

## Slide 4: Problem Statement (Recap)
Dyn MS-PW spans across multiple administrative domains. For security reasons strict access control is required at S-PEs. One way is to define policies at S-PEs based on SAII/TAII but adds complexity, administrative overheads, configuration mistakes.
Dyn MS-PW requires each S-PE to choose a unidirectional PSN tunnel to bind to a PW. T-PEs may require to signal the preference of PSN tunnels at S-PEs. Signaling each of the various types of PSN tunnel selection criteria adds significant burden to LDP messaging procedures.
IETF-82
draft-pkwok-pwe3-pw-communities-02

## Slide 5: Problem Statement (New)
IETF-82
draft-pkwok-pwe3-pw-communities-02
T-PE or S-PE needs to select PW next-hop from ECMP next-hops. Hashing rules can be based on AGI/SAII/TAII but imposes limits to addressing schemes in order to get proper load balancing. Operators need a predictable way for load balancing MS-PW across ECMP which is independent of MS-PW addressing schemes.

## Slide 6: Solution (Updated)
A “PW Communities” is defined as a LDP TLV
that contains a list of PW Community Sub-TLVs.
Each PW Community Sub-TLV has specific processing rules based on its type.
IETF-82
draft-pkwok-pwe3-pw-communities-02

## Slide 7: PW Template Community Type
Very generic method and any complex rules can be mapped to specific PW Template Community.
Can be considered as “Template” so that PW set-up decisions can be based on set of rules identified locally by Template ID.
Can have various PW Template Types.
IETF-82
draft-pkwok-pwe3-pw-communities-02

## Slide 8: PW Color Community Type
Can be considered as “Coloring” of PW that may be used by T-PE or S-PE to select PW next-hop from ECMP next-hops.
Can have various PW Color Types.
Concept is different from “PW Grouping ID” . It is not necessary that PW Grouping and PW Color Community be correlated.
IETF-82
draft-pkwok-pwe3-pw-communities-02

## Slide 9: Next Steps
Request discussions/feedbacks in mailing list.
WG Status?
IETF-82
draft-pkwok-pwe3-pw-communities-02