## Slide 1: Label Switched Path (LSP) Ping for IPv6 Pseudowire FECs
draft-chen-mpls-ipv6-pw-lsp-ping-01.txt
Mach Chen (mach.chen@huawei.com)
Ping Pan (ppan@infinera.com)
Carlos Pignataro (cpignata@cisco.com)
Rajiv Asati (rajiva@cisco.com)
IETF 82th PWE3 WG Taipei

## Slide 2: Problem Statement
Three PW related FEC sub-TLVs defined (RFC4379)
  "FEC 128" Pseudowire (Deprecated), "FEC 128" Pseudowire and "FEC 129" Pseudowire,
  Each contains the destination/source addresses of the target LDP session
  Currently, only IPv4 target LDP session is covered
  Can not be used when IPv6 target LDP session is used
IETF 82h PWE3 WG Taipei
Notes: <number>

## Slide 3: Solutions
Extensions to RFC4379,
  Add two new sub-TLVs
    IPv6 "FEC 128" Pseudowire
    IPv6 "FEC 129" Pseudowire
    No "FEC 128" Pseudowire (Deprecated) defined for IPv6
  No more new procedures introduced
IETF 82h MPLS WG Taipei
Notes: <number>

## Slide 4: Solutions (cont.)
Updates to RFC 4379,
  Change names and titles of existing sub-TLVs
  From:
    "FEC 128" Pseudowire (Deprecated)
    "FEC 128" Pseudowire
    "FEC 129" Pseudowire
  When referring to the PE addresses
  OLD
    Sender's PE Address
    Remote PE Address
  To:
    IPv4 "FEC 128" Pseudowire (Deprecated)
    IPv4 "FEC 128" Pseudowire
    IPv4 "FEC 129" Pseudowire
  New
    Sender's PE IPv4 Address
    Remote PE IPv4 Address
IETF 82h PWE3 WG Taipei
Notes: <number>

## Slide 5: Next steps
Comments?
WG document?
IETF 82th PWE3 WG Taipei