## Slide 1: RADIUS Accounting Extensions on Traffic Statistics draft-yeh-radext-ext-traffic-statistics-01 + IETF 82 – Radext Nov. 14th, 2011
Leaf Y. Yeh
Huawei Technologies

## Slide 2: Requirements
NAS must be able to report the separated IPv4 & IPv6 traffic statistics for the differential accounting and traffic recording in dual-stack (or other IPv6 transition) scenario.
More discussion on BBF TR-187 Section 9.4, which dedicates for PPPoE with IPv6-only and Dual-Stack scenarios?
  “The BNG might support a mix of IPv4 and IPv6 traffic in any single queue thus allowing for any existing QoS policy to be maintained irrespective of whether the customer is generating or receiving IPv4 or IPv6 traffic. The BNG must also be able to support separate queues for IPv4 and IPv6 traffic, as they may be used to offer IPv4 and IPv6 services with different policies.”
    The BNG MUST support forwarding IPv6 and IPv4 traffic in common traffic classes.
    The BNG MUST support forwarding IPv6 and IPv4 traffic in separate traffic classes.
    The BNG MUST support input and output octet counters that are separate for both IPv6 and IPv4 traffic.
    The BNG MUST support input and output packet counters that are separate for both IPv6 and IPv4 traffic.

## Slide 3: Interests on the same topic of ‘Traffic Statistics’ shown in I.D.s written before
[draft-maglione-radext-ipv6-acct-extensions-01] "RADIUS Accounting Extensions for IPv6", Mar. 2010
  Telecom Italia, Ericsson, Magyar Telecom & Huawei
[draft-hu-v6ops-radius-issues-ipv6-00], "RADIUS issues in IPv6 deployments", Feb. 2011
  China Telecom & ZTE
[draft-winter-radext-fancyaccounting-00], "RADIUS Accounting for traffic classes“, Mar. 2011
  Stefan Winter
[draft-yeh-radext-dual-stack-access-02], "RADIUS Attributes for Dual Stack Access", Mar. 2011
  Leaf Yeh @ Huawei

## Slide 4: Network Scenario
Note that traffic statistics reporting might also be required in any IPv4-IPv6 transition cases including dual-stack, NAT444, 6rd, DS-lite, or 4rd, and etc.

## Slide 5: Attribute Design - 1
Define in the traditional unassigned type space
  8x new attributes in ‘flat’ mode : 2x 2x 2
    (IPv4/IP6) * (Input/Output) * (Octets/Packets)
  Data Type: Interger64
  Format is shown as below:

## Slide 6: Enhanced Design – 1+
Still in the traditional unassigned type space
But 4x new attributes in ‘flat’ mode : 2x 2
  (Input/Output) * (Octets/Packets)
Add one-octet field named ‘Traffic-Type’, which provide the extensible space for future usage
Code of ‘Traffic-Type’ could be:
  0 for IPv4+IPv6
  1 for IPv4
  2 for IPv6
  3-10 for DSCP0-7 (TBD)
  11-255 Reserved
0+ in Accounting-Request message
Format is shown as below:

## Slide 7: Attribute Design - 2
Define in the Extended-Type space per draft-ietf-radext-radius-extensions-02
  8x new attributes in ‘flat’ mode : 2x 2x 2
    (IPv4/IP6) * (Input/Output) * (Octets/Packets)
  Codes of new attribute
    241.x or 242.x
  Data Type: Interger64
  Format is shown as below:

## Slide 8: Enhanced Design – 2+
Employ the extended type space
But 4x new attributes in ‘flat’ mode : 2x 2
  (Input/Output) * (Octets/Packets)
Add one-octet field named ‘Traffic-Type’, which provide the extensible space for future usage
Code of ‘Traffic-Type’ could be
  0 for IPv4+IPv6
  1 for IPv4
  2 for IPv6
  3-10 for DSCP0-7 (TBD)
  11-255 Reserved
0+ in Accounting-Request message
Format is shown as below:

## Slide 9: Design - 3
Define in the Extended-Type space per draft-ietf-radext-radius-extensions-02
TLV grouping in one Container attribute: Acct-traffic-statistics
4x sub-attribute are believed always to appear simultaneously in the accounting message, the format of the sub-attribute is almost the same as the one in Design 1 described above.
  Input-Octets (10x octets, TLV)
  Output-Octets (10x octets, TLV)
  Input-Packets (10x octets, TLV)
  Output-Packets (10x octets, TLV)
1x sub-attribute of ‘Traffic-Type’
  Traffic-Type (3x octets, TLV)
Code for the attribute & sub-attributes might be:
  Acct-traffic-statistics: 241.x
  Traffic-Type: 241.x.1
  Input-Octets: 241.x.2
  Output-Octets: 241.x.3
  Input-Packets: 241.x.4
  Output-Packets: 241.x.5
Code for the ‘Value’ of ‘Traffic-Type’ could be the same as Design-2+ described above.

## Slide 10: Design – 3 (Cont.)
0+ in Accounting-Request message
Format is shown as below: (46x Octets in total)

## Slide 11: Enhanced Design – 4 (or 1++)
Still in the traditional unassigned type space, but 1x new attributes in ‘flat’ mode, including 5x additional fields:
  Traffic-Type (1x octet)
  Input-Octets (8x octets)
  Output-Octets (8x octets)
  Input-Packets (8x octets)
  Output-Packets (8x octets)
Code of ‘Traffic-Type’ could be the same as Design-2+ described above.
0+ in Accounting-Request message
Format is simplified.
Same design can be adopted for the Extended-Type space if necessary.
  + 1 Octet for the field of ‘Extended-Type’ in the format

## Slide 12: Enhanced Design – 4 (Cont.)
Format is shown as below: (35x Octets in total)

## Slide 13: Discussion in the ML of Radext
With Alan DeKok
  Suggestion: TLVs Nesting (or Grouping)
  Turn to be Design-3 described above.
Stefan Winter
  draft-winter-radext-fancyaccounting-00
    container Attribute + TLV (sub-attributes)
    1-2 sub-attributes (Class-ID & Class-Name) for the traffic type

## Slide 14: Proposal for Next Step
Deserve to be a WG item?
  Clear requirements from the industry
  4+ proposed attribute design
Thanks for the discussion in the mail-list before this presentation with:
    Alan DeKok
    Stefan Winter