## Slide 1: RPL adaptation for asymmetrical links IETF 82 status
Slide #<number>
IETF 82 – ROLL WG – November 2011
draft-thubert-roll-asymlink
Pascal Thubert
Notes: <number>

## Slide 2: draft Status
-00 published in October.
Expects Bi-directionality but not metrics symmetry
Based on early discussions in the mailing list
  PLC
  Radios
Triggered by the industrial applicability work
  Cascading from PCE-computed DAG to classical RPL DAG.
Slide #<number>
IETF 82 – ROLL WG – November 2011
Notes: <number>

## Slide 3: Operations
Associates 2 RPL instances (DAGs), “up” and “down”
  Both use bidirectional links
  “upwards” DAG optimized for metrics up
  “downwards” DAG optimized for metrics down
Packets can jump from “upwards” to “downwards”
  Default routing initially occurs along “upwards” DAG,
  Longer match looked up on “downwards” DAG at each hop
  If found, the packet continues on the “downwards” DAG
More cascading is allowed
  E.g. into a default spanning DAG
Slide #<number>
IETF 82 – ROLL WG – November 2011
Notes: <number>

## Slide 4: DODAG Information Object (DIO)
0 1 2 3
0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1 2 3 4 5 6 7 8 9 0 1
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| RPLInstanceID |Version Number | Rank |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
|G|D| MOP | Prf | DTSN | Flags | Reserved |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| |
+ +
| |
+ DODAGID +
| |
+ +
| |
+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+
| Option(s)...
+-+-+-+-+-+-+-+-+
Slide #<number>
IETF 82 – ROLL WG – November 2011
Notes: <number>

## Slide 5: D flag and MOP relationship
Directional (D):
  The Directional (D) flag is set to indicate that the instance is intended for directional operation, and reset otherwise.
When ‘D’ is set,
  A MOP of 0 indicates the upwards direction
  All other values of MOP will be considered downwards unless explicitly specified otherwise.
Slide #<number>
IETF 82 – ROLL WG – November 2011
Notes: <number>

## Slide 6
Enough need / interest to progress this work
?
Slide #<number>
IETF 82 – ROLL WG – November 2011
Notes: <number>