## Slide 1: Reactive Discovery of Point-to-Point Routes in Low Power and Lossy Networks
draft-ietf-roll-p2p-rpl
M Goyal, E Baccelli, A. Brandt, M. Philipp, J Martocci. R. Cragie

## Slide 2: Goal
Extension of the basic RPL spec
Alternative, shorter sensor-to-sensor paths
Reactive discovery request/reply mechanism
R
S
D
R
S
D
R
S
D
DAG
Path with basic RPL
Path with P2P extension

## Slide 3: Functional Overview
DIO + Route discover option
Trickle + link local multicast
Temporary DAG rooted at source
Target sends DRO back to source
Hop-by-hop state or source route path establishment

## Slide 4: Drafts Status
draft-ietf-roll-p2p-rpl-05 published this week
  Editorial changes since -04
  Last call?

## Slide 5: Implementations & Interop
INRIA implementation
  MSP430, CC2420, 802.15.4
Sigma Designs implementation
  ZW0401, ZWAVE
Other implementations (on ns2 from UWM, LIX)
Interop happening this week between INRIA and Sigma Designs implementations

## Slide 6: Deployment
Senslab Lille testbed
  256 nodes
  2.4 GHz IEEE 802.15.4

## Slide 7: Experiments
  Significant path length reduction
  Significant traffic reduction near root

## Slide 8: Measurement of P2P Route in LLNs
draft-ietf-roll-p2p-measurement
M Goyal, E Baccelli, A. Brandt, J. Martocci

## Slide 9: Functional Overview
Measure quality of existing path
Decide to initiate discover of better path
Origin sends measurement request along path
Request accumulates info along path
Target unicasts back accumulated info
Not requirement (informative ref. in P2P)

## Slide 10: Draft Status & Implementation
draft-ietf-roll-p2p-measurement-02 published last month
INRIA implementation
  MSP430, CC2420, 802.15.4
Deployment on Senslab Lille testbed
Ready soon for last call?