## Slide 1: RTCWEB interim 2011-09-08 Remote recording use case / requirements
John Elwell

## Slide 2: Background
The SIPREC WG is specifying the use of SIP for delivering real-time media and metadata from a communication session to a recording device (remote recording)
  From Session Recording Client (SRC) to Session Recording Server (SRS)
Many business applications, e.g., in contact centres, where recording is needed for legal, non-repudiation, quality control and other reasons.
Active recording – with knowledge / implicit consent of participants
More background to SIPREC in back-up slides
How is session recording achieved in an environment using RTC-Web clients?
Out of scope for this presentation:
  Local recording (on client device)
  Voicemail / videomail

## Slide 3: SIPREC and RTC-Web (1)
There will be some environments that deploy RTC-Web clients and require communication sessions to be recorded centrally (SIPREC)
Can locate the SRC at a middlebox (e.g., a SIP B2BUA), as will be done in many SIP deployments
  Requires CSs to be routed through the middlebox concerned (if not already)
  Requires a standardized signalling protocol between RTC-Web application and the middlebox (e.g., SIP)
  In conflict with peer-to-peer principle of RTC-Web real-time media
  Will satisfy some deployments

## Slide 4: SIPREC and RTC-Web (2)
Or can have a decomposed SRC implemented partly in the application and partly in the browser
  SIP and metadata aspects in the application
  Media aspects in the browser
RTC-Web application
Client device
SIP UA
RTP/RTCP
SIP
CS
SRS
RS
RTP/RTCP
SIP + metadata
JS
Browser
Signalling
SRC

## Slide 5: Browser support for remote recording
Main requirement:
  Copy streams sent/received on one peer connection and send them on another peer connection to the SRS
Application responsibility
  SIP support for SIPREC (assuming SIP remains outside the browser)
  Gathering and sending of metadata to SRS
  Control of tones / announcements / notifications
  Control of the two peer connections
Issues with this approach (to be considered during work)
  Bandwidth considerations on the local link, particularly uplink (this is a concern for any UA implementation of a SIPREC SRC)
  Security issues in using device as a media relay - ensuring appropriate permissions given

## Slide 6: Questions for the RTCWEB WG
Is a middlebox approach to session recording sufficient for RTC-Web environments, or do we need support at the endpoint (i.e., in the browser)?
Is this support needed at day 1?
If not needed at day 1, should we ensure the architecture does not prevent support in the future (copying between peer connections without architectural re-design)?
Should we add a use case and corresponding requirements?

## Slide 7: Back-up

## Slide 8: Overview of SIPREC (1)
CS is the Communication Session between two or more participants
RS is the recording session between Session Recording Client (SRC) and Session Recording Server (SRS) (recording device)
SIP UA
SRC
SIP UA
RTP/RTCP
SIP
CS
SRS
RS
RTP/RTCP
SIP + metadata
Database of recordings

## Slide 9: Overview of SIPREC (2)
Media delivered to SRS in real-time using RTP, allowing applications such as real-time analytics
Only concerned with real-time media
The SRC must sit somewhere on the path of the CS with access to signalling and media
  at a B2BUA such as an SBC
  at a conference focus
  at an endpoint (SIP UA)
Present work assumes SRC is aware of policy concerning which calls / which media to record
SRC responsible for notifying participants in accordance with policy (e.g., by applying tones or announcements, explicitly signalling to recording-aware UAs)
Retrieval, playback, retention etc. of recordings out of scope

## Slide 10: Requirements for browser support for remote recording
Copy streams sent/received on one peer connection and send them on another peer connection to the SRS
  Possible need to mix streams before sending (e.g., mix sent and received audio streams)
  Possible need to use a different codec or other parameters for sending to the SRS
  Possible need to use a different encryption / integrity context for sending to the SRS
Possible need to insert tones or announcements into the original media path being recorded
Possible need to support SDP enhancements for indicating media being recorded or preferences for media to be recorded

## Slide 11: Proposed use case / requirements
As sent out 2011-08-25, augmented by a proposal from Jim McEachern 2011-08-22:
  4.2.yy Remote Session Recording
  In this use case, the web application user wishes to record a real-time communication at a remote third party (e.g., a recording device), such that transmitted and received audio, video or other real-time media are transmitted in real-time to the third party. The third party can perform recording, archiving, retrieval, playback, etc., but can also perform real-time analytics on the media. A typical deployment might be in a contact centre. For a given medium, the two directions of transmission can be transmitted together (mixed) or separately. The web application also sends metadata that gives context to the stored media. If required, the web application will direct the browser to insert an appropriate indication (e.g. an intermediate beep) into the media stream to show that the communication is being recorded.
  New requirements:
  Fyy1: The browser MUST be able to send in real-time to a third party media that are being transmitted to and received from remote participants.
  Ayy1: The web application MUST be able to ask the browser to transmit in real-time to a third party media that are being transmitted to and received from remote participants and, in the case of audio at least, ask for the two directions of transmission to be transmitted to the remote recording device mixed or separately.
  Ayy2: The web application MUST be able to ask the browser to insert an appropriate indication into the media stream to indicate that the communication is being recorded.