## Slide 1: RTCWEB Terminology
A Discussion of relation between RTCWEB Media Protocol Terminology and the PeerConnection API

## Slide 2: RTP Related Terminology
Multi-Media Session
  A communication session between two or more entities
  Can contain one or more RTP session
  Can be represented by the signalling context
  Example representations are in a SIP Dialog or RTSP Session
RTP Session
  One RTP SSRC space shared between 2 or more entities sending zero or more media streams
  From a single end-points perspective, usually represented by:
    A port(s) to receive RTP and RTCP
    One or more destinations to send RTP and RTCP to.
  Commonly single media type (RTCWEB multiplexing will have multiple types)
  Media for a particular purpose and usage in an application context.

## Slide 3: RTP Related Terminology
SSRC
  Sender Source identifier (also used by receiver only entities to ID its reports)
  Identifies a single media source (e.g. camera, microphone, audio mix)
  Intended to be unique within an RTP session
  Multi-channel audio is commonly sent as a single SSRC using a media format capable either packetizing multiple channels or encoding multiple channels as one bit stream.
CNAME
  Canonical Name
  Identifies a synchronization context
  Unique within a multi-media session
  CName is applied to the SSRCs in one or more RTP sessions that a receiver may synchronize
Payload Type (PT)
  An Identifier representing the encoding and packetization of the media present in the RTP packet body

## Slide 4: WEBRTC API Terminology
WebRTC 1.0: Real-time Communication Between Browsers
  Based on W3C editors draft dated: 23 Aug 2011:
  http://dev.w3.org/2011/webrtc/editor/webrtc.html
MediaStream object
  Contains zero or more tracks
  A MediaStream object be forked to create a child that is equal or a subset of the parent object
  MediaStream objects can share tracks so one object contains the same tracks, a sub or super set of tracks of another MediaStream object
  Each MediaStream has a Label
MediaStreamTrack
  A single media source, multi-channel audio is a single track
  Each track can originate from:
    Media device, such as video camera or microphone
    File which plays back in real-time
    Received over network

## Slide 5: WEBRTC API Terminology
Label
  A Label used to identify a MediaStream when delivered to the other peer
  Note: Child objects inherent their parent’s Label
PeerConnection
  A communication association between two peers
  Media negotiation signalling is done on PeerConnection level
  Is configured with STUN and TURN server resources
  Contains ICE, Media Transport, etc.

## Slide 6: Discussion: MediaStream and Label
A MediaStreamTrack can be mapped to a SSRC in an RTP session
A MediaStreamTrack has a synchronization context, that could be represented by the CNAME
  CNAME needs to be the same by all MediaStreamTracks that are part of the same context, e.g. captured in the same room
A MediaStream sent by a PeerConnection can be represented by a list of RTP session:SSRC tuples
The MediaStream label has no matching construct
  The SDP a=label attribute labels RTP sessions, not a set of SSRCs in possibly several RTP sessions
  Needs to be exchanged between peers
  The MediaStream Label can’t be CNAME:
    The same track can be part of multiple MediaStreams
  Needs to be specified!

## Slide 7: Discussion: RTP sessions
Lets look at the small non-centralized conference:
  Uses Mesh between A, B and C.
Current PeerConnection definition results in one Peer Connection between each pair of peers, i.e AB, AC and BC
The WebApp in A can bind the same MediaStream object to both PeerConnections (AB and AC)
  Thus delivering the same media sources to both peers
  The exact media configuration for each PeerConnection may be desirable to vary
    Different amount of screen estate at peers
    Application logic’s usage of streams
    Capability negotiation between peers may result in different codecs etc.
A
C
B

## Slide 8: Discussion: RTP sessions
Two possible RTP Session structures:
  The first is one RTP session over all PeerConnections
    Implies same media streams to all participants
    Allows for RTCP information for legs a peer is not directly involved in.
    No Use case requiring this structure currently
  The second alternative is to use individual RTP session(s) for each PeerConnection
    Allows different rates and codecs in each PeerConnection
    Adaptation modules needs to combine information across multiple PeerConnections and RTP sessions
The application context may need common information across the peers
  Identities of streams
  Synchronization contexts
Application Context
RTP Session
A
C
B
Application Context
A
C
B

## Slide 9: Discussion: Multi-Party RTP Sessions
In the centralized conference usage a common RTP session needs to be supported
  The RTP tools for centralized conferencing are built around a common session
  The RTP session still exist in the context of only one PeerConnection from the end-point’s (A, B, C or D) view
  A Mixer has a different view, but is after all a more advanced RTP entity
RTP Session
A
Mixer
B
D
C