## Slide 1: IP/LDP Fast-Reroute Using Maximally Redundant Trees draft-atlas-rtgwg-mrt-frr-architecture-01
Alia Atlas, Maciek Konstantynowicz, Robert Kebler,
Gábor Enyedi, András Császár,
Russ White, Mike Shand
IETF 82, Taipei, Taiwan

## Slide 2: Goals Met
Guaranteed 100% Coverage in an IGP area/level for single link/node failure.
Provide fast-reroute for IP Unicast, LDP Unicast, IP Multicast and LDP Multicast
Provide a live-live Multicast solution
Support Incremental Deployment.
Solve the IP/LDP Fast-Reroute Problem Fully

## Slide 3: Some Benefits of 100% Coverage
Networks frequently have maintenance events and other changes – so network topology is frequently not the complete designed architecture.
  Coverage is not dependent on specific architecture.
Allows for Micro-Forwarding Loop Prevention techniques (which inevitably delay convergence) to be used without traffic loss.

## Slide 4: Costs to Meet Goal
Tag Packets to indicate topology being used
  In MPLS networks, can basically allocate 2 additional labels per router loopback in area/level
IGP Capabilities signaling
  Learn what routers support MRT FRR for which forwarding and type of traffic.
New Algorithm – MRTs computation
  Computational complexity similar to a few SPFs
  Routers need to implement same algorithm/result

## Slide 5: Forwarding
Multi-Topology forwarding includes the topology (MT-ID) with the destination to find the next-hops.
For each topology for each destination, need to compute next-hops.
Interface-Specific Forwarding
U-turn alternates
Explicit Tunnels
NotVia,
Remote LFA
Multi-Topology
MRT
To go beyond LFA, it is necessary to use an additional forwarding mechanism.
MT-ID,
Destination
Next-Hops

## Slide 6: MRT FRR: Multiple Forwarding Topologies – 1 Network Topology
Fast-Reroute with MRT uses 3 forwarding topologies:
  current default topology – next-hops computed by SPF
  Blue MRT topology - MRTs computes next-hops
  Red MRT - MRTs computes next-hops
  Same network topology used as input to the SPF and MRT algorithms. Just different next-hops are computed as a result of different algorithms.

## Slide 7: MRT Unicast Forwarding: For Want of 2 bits…
IP and LDP Unicast – Recommended Minimum
  Simple and basic solution – no label-stacking needed
  MPLS label distributed by LDP to indicate FEC and MT-ID
  “Just works” with MPLS hardware.
Other Options Exist
  Topology-ID label
    Can reuse MPLS context-label space hardware
  IP-in-IP with different loopbacks

## Slide 8: Use of MRT FRR for Unicast Fast-Reroute
Before failure:
  Compute & Use Shortest-Path Tree Next-Hops
  Compute MRTs and LFAs. Select alternates for each primary next-hop for each destination.
  Install alternates into forwarding plane.
  Install MRT next-hops into forwarding plane.
At failure: PLR moves traffic to alternates.
After failure:
  Compute SPT next-hops and alternates. Install in forwarding plane.
  Wait until network converged.
  Install MRT next-hops into forwarding plane.

## Slide 9: Incremental Deployment
Before computing MRTs, prune out routers that don’t support MRT FRR – determine the local island.
Benefits possible as soon as two neighboring routers both support MRT FRR.
  Easy way to make long rings work.

## Slide 10: Next Application: Multicast Fast-Reroute
Traffic-Handling: A router only forwards alternate traffic when its upstream primary link(s) are down.
Link-Protection: PLR replication into tunnels using unicast alternate to reach next-hops.
Node-Protection: Do we need it?
  PLR replication with tunnels
  Distributed replication via alternate trees per (PLR, failure-point) – complexity and scaling…

## Slide 11: Next Application: Multicast Live-Live
Identify the MT-ID (Blue MRT or Red MRT) when signaling an (S,G) or mLDP.
  Separate G for each MT-ID
  Traffic can be distinguished on common link because of different G or MPLS label.
Receivers join both the (S,G-blue) on the Blue MRT and (S,G-red) on the Red MRT.
  Receivers determine which packets to keep
MRT natural fit for Multicast Live-Live
  MRTs rooted at the Multicast Source
  Automatically computes maximally disjoint trees.

## Slide 12: Summary
Meets 100% coverage goals.
Describes applications beyond unicast fast-reroute.
Control-plane computation and alternate selection has been implemented for examining behavior on different topologies.
Forwarding Plane is simple and no changes.
Control Plane – complexity confined to deterministic algorithm.
Good way forward to finish IP/LDP fast-reroute.
Ready to become a WG draft?