## Slide 1: Algorithms for computing Maximally Redundant Trees for IP/LDP Fast-Reroute draft-enyedi-rtgwg-mrt-frr-algorithm-00
Gábor Sándor Enyedi
egboeny@ericsson.com
Alia Atlas
akatlas@juniper.net
András Császár
eandcss@ericsson.com

## Slide 2: MRT
Maximally Redundant Trees
  A pair of directed spanning trees
  The common root is reachable along both of them
  The two paths along the two trees are maximally disjoint
a
b
f
d
c
root
h
i
k
g
j
e

## Slide 3: Why do we need this draft?
We need a pair of MRTs rooted at each node
  All the nodes should compute the same!
  We will need standardization for MRT computation (algorithm) or results of that computation.

## Slide 4
Principles
Partial order
ADAG
Blocks and GADAG

## Slide 5: Partial order
Partial order of a set (e.g. set of nodes)
  A relation like a normal set
  Except: not all the elements can be compared
    For some a and b neither a<b nor a>b
Graph representation:
  Directed Acyclic Graph (DAG)
min
max
min<a<b<f<c<e<max
a<d<e
a
b
f
d
c
e

## Slide 6: Finding node-disjoint paths
Suppose that
  We have a partial order of nodes
  Exactly one min and max
  Each node (except min and max) has a lower and greater neighbor
Walk down and up
  Min and max are reached
  The two paths are node-disjoint!
min
max
a
b
f
d
c
e
min<a<b<f<c<e<max
a<d<e

## Slide 7: Two paths to the same node
DAG is not enough
  Let min and max be the same node!
Resulting graph is an Almost DAG (ADAG)
  There is a single node, the root, such that without the root it is a DAG
min
max
root
a
b
f
d
c
e
min<a<b<f<c<e<max
a<d<e
root<a<b<f<c<e<root
a<d<e

## Slide 8: Redundant paths to the root
Blue path:
  Nodes must increase
Red path:
  Nodes must decrease
Load sharing is possible
root
a
b
f
d
c
e

## Slide 9: Finding an ADAG (2-connected networks)
Phase 1 – basic partial ADAG
  Find a partial ADAG for a cycle containing the root
    Use either direction
  Extend partial ADAG into all nodes
root
a
b
f
d
c
e

## Slide 10: Finding an ADAG (2-connected networks)
Phase 2 – extending
  Find a path from one “ready” node to the another
  Nodes along the path must not be ready (except the endpoints)
  Add the path to the ADAG in a “proper” direction
root
a
b
f
d
c
e

## Slide 11: Adding not used links
Some links may be out of the ADAG
BAD! e<f
OK
root
a
b
f
d
c
e

## Slide 12: How can ordering be kept up?
ADAG is almost a DAG
  Let root be now only the smallest one
  Now, it’s a DAG, create a topological sort
  This is a total order
    Add extra links with respect to this
2
3
5
4
root
a
b
f
d
c
e
6
7
1
Add back links to root and we have an ADAG using all links.

## Slide 13: What if the network is not 2-connected?
We need to split the graph into blocks
  Block:
    Maximally 2-connected subgraph
    Two connected nodes
    (Isolated node)
  Each block has its local-root
    That is the cut-vertex towards the root
  Compute an ADAG in all the blocks
  This is a Generalized ADAG

## Slide 14: Generalized ADAG
root
f
Block1: root, a, b, c, d, e, f
Block2: f, g
Block3: g, h, i, j, k
h
i
k
g
j
a
b
d
c
e

## Slide 15
The algorithm
MRTs in a block
MRTs in the whole network

## Slide 16: How to Find MRTs
If it is complex, then we break the problem down
  Transform network into its blocks
  Find ADAGs in each block
  Connect up the ADAGs to make a GADAG
  Add all the other links in – with the proper directionality
From a GADAG, compute your next-hops to each destination
  First for those in the same block
  Destinations outside the block inherit their next-hops from a proxy in the block

## Slide 17: How to Find MRTs
If it is complex, then we break the problem down
  Transform network into its blocks
  Find ADAGs in each block
  Connect up the ADAGs to make a GADAG
  Add all the other links in – with the proper directionality
From a GADAG, compute your next-hops to each destination
  First for those in the same block
  Destinations outside the block inherit their next-hops from a proxy in the block

## Slide 18: MRTs in a single block
As the computing router S: From the GADAG, can use SPF and reverse SPF to find next-hops to all destinations in the same block
  SPF gives nodes definitely greater
  rSPF gives nodes definitely lesser
  Remaining nodes are not ordered
Then use some simple rules

## Slide 19: MRTs in a single block: source perspective
Find greater and lesser nodes
Rules
  If S < D – increase to D decrease to root
  If S > D – increase to root decrease to D
  No order – decrease to root increase to root
  If D=root – increase to root decrease to root
  If S=root – increase to D decrease to D
Routing table of node c (S = c):
+
+
-
-
-
0
a
b
f
d
c
e
-
root
Dest ( D ) | Rule Used | Blue Next-hop | Red Next-hop
a | 2 | e | b
b | 2 | e | b
d | 3 | b | e
e | 1 | e | b
f | 2 | e | f
root | 4 | e | b

## Slide 20: MRTs in a single block: destination perspective
root
a
b
f
e
c
Destination: node c (D = c)
d
Find greater and lesser nodes
Rules
  If S < D – increase to D decrease to root
  If S > D – increase to root decrease to D
  No order – decrease to root increase to root
  If d=root – increase to root decrease to root
  If s=root – increase to D decrease to D
Src ( S ) | Rule Used | Blue Next-hop | Red Next-hop
a | 1 | b | root
b | 1 | c | a
d | 2 | a | e
e | 3 | root | c
f | 2 | c | e
root | 1 | a | e

## Slide 21: How to Find MRTs
If it is complex, then we break the problem down
  Transform network into its blocks
  Find ADAGs in each block
  Connect up the ADAGs to make a GADAG
  Add all the other links in – with the proper directionality
From a GADAG, compute your next-hops to each destination
  First for those in the same block
  Destinations outside the block inherit their next-hops from a proxy in the block

## Slide 22: Inter-block MRTs
h
i
k
g
j
Proxy node: the last vertex in the block to the destination (along any path)
root
a
b
f
d
c
e
Dest ( D ) | Rule Used | Blue Next-hop | Red Next-hop
a | 2 | e | b
b | 2 | e | b
d | 3 | b | e
e | 1 | e | b
f | 2 | e | f
root | 4 | e | b
Dest ( D ) | Proxy | Blue Next-hop | Red Next-hop
g | f | e | f
h | f | e | f
i | f | e | f
j | f | e | f
k | f | e | f

## Slide 23: Example – destination is node C
Block1: root, a, b, c, d, e
Block2: e, f
Block3: f, g, h, i, j
h
i
k
g
j
root
a
b
f
e
c
d

## Slide 24: Summary
Algorithm
  Find GADAG
    ADAG in each block
    Add not used links
  Find next-hops along the MRTs
    Do an SPF and an rSPF to find ordered nodes
    Use rules to find NHs your block
    Find proxy nodes

## Slide 25
Thanks for the attention