## Slide 1: FRR for IP and LDP based on Fast Notification
draft-csaszar-ipfrr-fn-02 IETF82, Taipei
András Császár Andras.Csaszar@ericsson.com
Gábor Enyedi Gabor.Sandor.Enyedi@ericsson.com
Jeff Tantsura Jeff.Tantsura@ericsson.com
Sriganesh Kini Sriganesh.Kini@ericsson.com
John Sucec sucecj@telcordia.com
Subir Das sdas2@telcordia.com

## Slide 2: Background
IP & LDP based on hop-by-hop forwarding
  Consistency between hops ensured by IGP
A failure creates inconsistency
  Wait for IGP global reconvergence (slow)
  Temporarily use faster means to notify changed routing configuration
    Encode information into data packet (bits, encaps, label change)
    Encode info into packet direction (interface specific forwarding)
    Explicit notification not allowed due to fears of slow performance
D
A
S
Default shortest path
Without any info in S: loop
Illusion of local repair!
Any difference?

## Slide 3: FN ≠ IGP Link State Advertisement
LFA local repair
IGP global repair
IPFRR-FN
Local or external trigger
linecard
control element
Local trigger
linecard
control element
local reconfig.
Pre-configure backup entries
download new entries
advertise further
linecard
control element
local reconfig.
Pre-configure backup entries
Local or external trigger
send up to CP
advertise further

## Slide 4: IPFRR-FN Principles
NOT modifying the IGP/LDP
  Only using its LSDB
Pre-computation
  Let the IGP prepare for each potential (single) failure case
Pre-installation of backup routes
  Which deviate from primary routes
Explicit failure notification in data plane
  Flooding with duplicate filtering and SHA256 auth check
IGP after global reconvergence only “confirms” routes
  Reducing micro-loops (FRR detour identical to final IGP path)

## Slide 5: Basic Fail-Over Mechanism with IPFRR-FN
LFA could not handle the failure of A-B link
Default path: C-A-B-D
A floods FN (B, too)
A reroutes traffic
C&E check FN and forward it
C&E re-route traffic
C&E receive duplicate FN, drop F checks FN and forwards it F does not need FIB update
…
A
B
D
C
F
G
H
X
E
An FN message
SHA256 pass Duplicate check pass
Does FRR and forwards FN
SHA256 pass Duplicate check pass
Does FRR and forwards FN
SHA256 pass Duplicate check fail
SHA256 pass Duplicate check fail
SHA256 pass Duplicate check pass
Doesn’t need new FIB entry Forwards FN

## Slide 6: Concerns – The Devil in the Details
Pre-calculation performance?
Backup database size?
Performance of FIB update from the backup database?
Time to originate an FN packet?
Time to forward an FN packet?
  Including duplicate and SHA256 authentication check
Time to process an FN packet?
Packet flow disruption time?

## Slide 7: Pre-Calculation & Pre-Install
Non-optimised implementation: ca. 1 SPF for each failure
A decent implementation should use incremental SPF for each new pre-calculated failure
  Drastic decrease of overhead
Only need to pre-install relevant cases:
  For failures downstream on the shortest path(s) towards the destination
    Only those failures, which result in next-hop change!

## Slide 8: Backup Database and FIB Update An Extreme Case
1000 nodes
20 hop diameter
  Worst case: every path is 20 hops long and each link/node failure results in a new alternative next-hop
9000 external prefix groups
  Prefix group = Set of prefixes with the same primary and secondary border routers
    9000 prefix groups correspond to 95 BRs, with each combination serving at least a prefix (95*94≈9000)
When storing in a very simple structure and assuming a failure impacts each route: FIB update can be solved with 50k memory transactions
  Assuming DRAM with 5MT/sec, and 1 memory controller: 10ms
3.4MB
Comparison: linecards equipped with 1+GB DRAM
Underestimate

## Slide 9: FN Packet Performance in Research Prototype
Prototype: Ericsson SmartEdge with PPA2-based linecards
  ca. 5-6 years old line card
FN packet origination < 250µs after failure detection
FN packet forwarding per hop < 180µs
  including SHA256 verification and duplicate check in each hop!
Linecard requirements:
Support packet origination locally
Support packet recognition locally
Support FIB update locally
Available if card can do BFD or ICMP Echo locally
Available if card can do LFA locally

## Slide 10: Packet Flow Disruption
Timelines:
A
S
10ms e.g. BFD
250µs FN orig
10ms FIB update
Failure happens
FIB updated
180µs FN forwarding
Failure detected locally by A
FN sent
Link delay
10ms FIB update
packet loss
forwarding towards A
forwarding towards B
FN recv’d
FN sent
FIB updated
D
A
S
B
Default shortest path

## Slide 11: E2E Packet Flow Impact
Traffic flow: 1 pkt / ms
Varying delay of “bold” links (D)
FN results in re-routing 10 hops away!
Dst
Src
1
2
6
9
10
5
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=Dms
Cost=1000
Cost=1
Packet loss below 20ms
Default path
X
FN
FN
FN
FN
FN
FN
FN
Packet loss largely independent of link delays

## Slide 12: Constraining FN Scope
Static pre-configuration the TTL for FN messages in routers based on best current practices and related studies of available ISP and enterprise network topologies
Dynamically pre-calculate the TTL value
Dynamically pre-calculate the set of neighbours for which a particular FN message should be forwarded
Any ideas/collaboration is welcome!

## Slide 13: Application to Provider Provisioned VPNs
Providing FRR for egress PE failure
  Existing approach: PEs running multi-hop BFD between in each other in (full) mesh
  E.g. 100 PEs, could be 10k multi-hop BFD sessions (each transmitting BFD packets every, say, 10ms), continuously, all time!
  Ingress PE router changes egress PE to alternative egress PE
PW-redundancy: new egress PE needs to activate standby PW with LDP, too
Why not let the network inform the PEs quickly that a failure happened?
  FN can distinguish link and node failures!
  Both ingress and new egress PE receive FN, can modify their routes/PWs upon primary PE node failure
PE1
PE2
PE3
PE4
PE8
PE7
PE9
PE6
PE5
PE0

## Slide 14
If I haven’t been shot down (yet)
And still have time

## Slide 15: Incremental Deployment
The more router support IPFRR-FN, the better
But even two routers can make wonder
Advertisement of FN capability
  E.g. Router Capability TLVs
    OSPF [RFC4970]
    IS-IS [RFC4971]
Let’s take the example on the first slide that LFA could not solve
  Even if only A and S support FN, they can start solving failure cases left by LFA
Remember: TTL=1 or 2 can already greatly improve coverage! (slide 12)
D
A
S
Default shortest path
legacy
legacy
legacy

## Slide 16: Incremental Deployment – Few Legacy Nodes Legacy Node Bypass
Legacy
  It can at least forward the multicast packets of FN (static conf)
  FN packets are not recognised/processed  routes are not changed!
FN-capable nodes
  When pre-calculating backups, have to consider that legacy nodes won’t change routes
Example:
  If B is FN capable: it will re-route
  If B is legacy: C can re-route
C
B
A
Dest
FN
FN
C
B
A
Dest
FN
FN
legacy

## Slide 17: Conclusions
Fast Notification based IPFRR
  is feasible
  has good performance
  uses the same paths as detours that the IGP will use after global re-convergence (reducing micro-looping)
  Complete coverage for
    all single link,
    all single node and
    all single SRLG (local and remote) failures and for
    a reasonable number of pre-configured multiple failure cases deemed important by the operator
  Does not require total network upgrade to show benefits
  SIMPLE TO GRASP: just let the routing engine pre-do what it would anyway do after the failure!
Applicable to
  IP
  LDP-MPLS: liberal label retention + downstream unsolicited mode
  L2VPN and L3VPN PE protection
  ASBR protection

## Slide 18
BACKUP

## Slide 19: E2E Packet Flow Impact Scenario 2
Traffic flow: 1 pkt / ms
Varying delay of bold link (D) and length of ring (n)
Dst
Src
1
2
3
n-2
n-1
n
i
Delay=Dms Cost=1000
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=1ms Cost=1
Delay=1ms Cost=1
Default path
X
Packet loss below 25ms
FN
FN
FN
FN
FN
FN
FN

## Slide 20: FIB Update on Linecard from Backup DB See numbers’ origin on slide 8
50k memory transactions
  Assuming DRAM with 5MT/sec, and 1 memory controller: 10ms
Route 1
Route 2
…
Route 1000
Route 1001
…
Route 10000
intra-area destinations
external prefix groups
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Alt Rt
Fail-ID
Main operation: binary search in each list
Underestimate