## Slide 1: Software-Defined Networking - Attributes, candidate approaches, and use cases -
MK. Shin, mkshin@etri.re.kr, ETRI
M. Hoffmann, hoffmann@nsn.com, NSN
SDN BoF - IETF82@Taipei
17th November 2011

## Slide 2: Why SDN from Operators’ perspective ?
Intelligence on networks and resource sharing
  A lot of the information is stored and processed on computers out on the network
    Data center, distributed clouds, etc.
Programmability
  Add operators’ own processing, control, program, etc.
    More intelligent control systems to orchestrate the behavior of thousands of routing machines
Service awareness
  E.g., On-demand “express lanes” with guaranteed QoS for voice and data traffic that is time-sensitive
Management and Operations
  Much easier to reduce management complexity rather than in configured networks
    Optimize resources, Decrease energy consumption
    CAPEX/OPEX reduction (cheap NEs)

## Slide 3
Data Plane
(Specialized Hardware)
Control Plane
Data Plane
(Specialized Hardware)
Control Plane
Network OS
Controller
(Software)
(e.g.,) Openflow
protocol
Abstract Network Model
(Open API, Script, Language)
Separation
A Single Physical Infrastructure
Virtualized Programmable Infrastructure
Network OS
Today’s Network vs. SDN
Content
Providers
Network
Operators
Client
Client
Contents
Server
Dumb Pipe
Smart Pipe
Network
Operators
Contents
Server
Mobility
Data Routing
Energy efficient forwarding

## Slide 4: SDN - Attributes
(1) Separation of data and control planes
(2) Open interface to control planes
(3) Open interface between control and data planes
(4) Virtualization and slicing of the underlying network

## Slide 5: SDN – Candidate Approaches ?
Separation of data and control planes
  Abstract Network Model ?
(2) Open interface to control planes
  Abstract Network Model  APIs, Script, Formal description languages, etc.
(3) Open interface between control and data planes
  E.g., OF Extensions …
(4) Virtualization and slicing of the underlying network
  Virtualization of resources (VM, Rspec, etc.)

## Slide 6: Use Cases and Goals
Data center and distributed clouds
  Increase network functionality while lowering the cost associated with operating networks
  Optimize resources (business-driven)
  Decrease energy consumption (routing planning)
Home network management
  Avoid complexity of management for heterogeneous devices
  Access broker
Mobile operator
  MVNO extensions
  Service Component Mobility
Campus networks and testing
  Experimentation (e.g., GENI racks, Beta slice)
  Polymorphic networks (e.g., CCN + IP legacy routing)

## Slide 7: Challenging Issues (In-Scope ?)
Scalability
  A single controller : a single point of failure
  Inter-domain issues
Interoperability
  Multi-controllers, multi-operators, etc.
Security
  Controllers attacked
    Malicious controllers destroy whole networks
Validation and verification (of dynamically defined networks)
Carrier grade
Monitoring