## Slide 1: Draft-ietf-sidr-bgpsec-protocol
Matt Lepinski
mlepinski@bbn.com

## Slide 2: Draft-ietf-sidr-bgpsec-01
Thank you to everyone who provided comments on the -00 draft
Additional thanks to Wes George and Sandy Murphy who have already sent comments on the -01 draft!

## Slide 3: pCount Field
There was consensus at the Quebec meeting that BGPSEC should accommodate route servers that do not wish to increase the length of the AS-PATH.
The -01 version adds a “pCount” field to address this route server issue and to permit adding multiple copies of an AS number without multiple signatures

## Slide 4: Example (copies of AS number)
OLD
NEW
AS-PATH : X Y Z Z Z
(5 signatures)
AS-PATH : X Y Z
pCount : 1 1 3
(3 signatures)
Note: This requires “expanding” the AS-PATH when we send an update
From a BGPSEC speaker to a non-BGPSEC speaker
Note: AS Path Length is Sum of pCount

## Slide 5: pCount = 0 (Route Servers)
A Route Server signs with its own AS
  Maintains the security properties of BGPSEC
A Route Server may set pCount to 0
  This way a route server does not bias traffic away from itself by increasing the length of the AS-PATH
Security Consideration
  An entity that is not a route server could set pCount to 0 to bias traffic towards itself
  If your peer is not a route server and sends you an update with pCount = 0, you should drop the update

## Slide 6: Another pCount Example
OLD
NEW
AS-PATH : W Y Z Z Z Z
(6 signatures)
AS-PATH : W X Y Z
pCount : 1 0 1 4
(4 signatures)
Question for the Working Group:
Is this a reasonable way to handle route servers?
Note: X is an “invisible” Route Server between W and Y

## Slide 7: Preventing Replay Attacks
The primary goal of BGPSEC is to prevent your routes from being hijacked by malicious entities that have never legitimately been on the path for your prefix
An additional goal of BGPSEC is to prevent someone that you used to do business with from replaying stale information to keep attracting your traffic

## Slide 8: Preventing Replay Attacks
Properties of replay attacks
  Business relationships change on a slow time-scale
  May be more difficult for humans to detect replay attacks than other types of route hijacking
Current -01 draft has an expire-time mechanism to limit vulnerability to replay attacks
  Goal of this mechanism is just to make sure that ancient business relationships do not come back to haunt you
  Intent is that validity periods will be long, because business relationships don’t change overnight

## Slide 9: Preventing Replay Attacks
There has been active discussion on the list on
  Whether the benefits (replay protection) of the current expire-time mechanism are worth the cost
  Concerns about the dangers of a misbehaving party who “beacons” too often
  Possible alternative mechanisms
We are not going to solve all this today
  In order to have an informed debate about this mechanism, we probably need a better analysis of what is truly the cost of the current mechanism