## Slide 1: SIPREC Recording Metadata for SRS (draft-ietf-siprec-metadata-05)
November 17th 2011
IETF 82 meeting
Authors: Ram Mohan R, R Parthasarathi, Paul Kyzivat

## Slide 2: Agenda
Changes in draft-ietf-siprec-metadata-05 from last version.
Discuss Open items in Metadata model
Discuss open items in the format (XML)
Next Steps

## Slide 3: Changes from Previous version
The new version of draft has following changes which were agreed upon during the last interim meeting:
  Removal of Extension data class/element from the model & XML
  "csrc" element added to Metadata XML schema
  "NameID" pair addition in XML schema
  Modified draft to use base64 encoding of URN UUID.
  Modified model to have representations of Association class
  Added some more Metadata XML examples (Disconnect cases) in the draft
Notes: csrc XML element has been added to schema. This element will have the contributing SSRC for cases where a mixed stream is being recorded. In case SRC is acting as mixer it may insert the contributing source in this XML element.
In case SRC is receiving a pre-mixed stream, it may learn this information from conf event package.
This is an optional XML element as per the schema definition.
NameID element has been added and it will have name/AoR pair
In the last interim it was agreed to have base64 encoding representation of UUID in the XML for all the IDs.

## Slide 4: Metadata Model in ver 05
sends
receives
Recording Session(RS)
Communication Session(CS) Group
Media Stream
Communication Session(CS)
Participant
1.. *
2..*
0..1
1..*
1..*
0..*
0.. *
0.. *
1.. *
0..*
1.. *
0..*
1..*
0..*
ParticipantCS
Association
ParticipantStream
Association
Notes: The above model represents Metadata as viewed by SRS.
This model is an abstract thing (class) . There can be several instances (objects) of this model for each RS.
  the advantage of UML is that it is very concise - you can express a *lot* in one or two diagrams.

## Slide 5: Metadata Model : Participant – CS linkage
The current model requires that each participant be associated with one or more sessions.
Any objections to allow a participant to be associated with *zero* or more sessions, rather than one or more ?
  Addresses certain persistent RS cases (e.g. Agent Phone (SRC) to SRS)
  Gives flexibility for XML representation (*possible* to represent a participant in XML with no associations to sessions. )
Communication Session (CS)
CS Identifier
Termination Reason
Association-Time
Disassociation-Time
Participant
Name / AoR pair
1..*
2..*
ParticipantCSAssoc
Capabilities
Association-Time
Disassociation-Time
0..*
Notes:   A Persistent recording session(e.g. setup from agent phone(SRC) to SRS) . If an SRC sends a snapshot before a CS starts it may have participant information without any session.
  This would help with the mapping to xml. If we go with participantSessAssoc (mentioned later) it becomes *possible* to define a participant with no associations to sessions. Allowing the same in the model at least makes them consistent.

## Slide 6: Metadata Model : Stream – CS linkage
The current model requires that each stream be associated with one or more sessions.
Any objections to allow a stream to be associated with *zero* or more sessions, rather than one or more.
  Addresses persistent RS cases (e.g. Agent Phone (SRC) to SRS)
  Gives flexibility for XML representation (*possible* to represent a stream in XML with no associations to sessions. )
Communication Session (CS)
CS Identifier
Termination Reason
Association-Time
Disassociation-Time
Stream
Media Stream Reference
Content-type
1..*
0..*
0..*
Notes:   A Persistent recording session(e.g. setup from agent phone(SRC) to SRS) . If an SRC sends a snapshot before a CS starts it may have participant information without any session.
  In this case if the RS has media stream (m-line) it may not have any senders/receivers and any CS associated.
  This would help with the mapping to xml. If we go with <participantStreamAssoc> (mentioned later) to represent Attributes of association of participant to a stream, it becomes *possible* to define a stream with no associations to sessions in XML. In that way the XML schema will be consistent. Allowing the same in the model makes them consistent.

## Slide 7: Metadata Model : Number of participants in CS
Currently each CS must have two participants
Its better to allow Zero or more participants:
  There may be use case where CS may have one participant
  An SRC may send a snapshot with Zero participants (persistent RS with out any CS setup yet)
  Any objections to allow a CS to have zero or more participants ?
Notes:   Studio recording – SRC(also acting participant) directly calls studio (SRS). Of course in this case SRS is logically the second UA
  If an SRC sends a complete metadata having zero or one participant SRS should still accept the metadata.
  In the current model, when a first participant joins ( it is start of session), when the last participant drops the session ends. Now this assumption goes wrong if we have a session with zero participants. Do we need to explicitly indicate start/stop for CS in addition to association times ?
  Persistent Communication Session (e.g. Hotline ? )

## Slide 8: Metadata Model Open item: Communication Session
Media Stream
Communication Session (CS)
CS Identifier
Termination Reason
Associate Time
Disassociate Time
Current draft has associate/disassociate time
  Associate-time – The optional attribute represents the time a CS is associated with a RS
  Disassociate-time- This optional attributes represents the time a CS disassociates from a RS.
  These must be attributes of association of CS to RS. Any objections ?
There was a comment to include start/Stop time also. Is it needed ?
Is there a need to track the times a CS is part of CS-Group ?
Recording
Session (RS)
1..*
0..*
Communication
Group (CSG)
0..1
1..*
1.. *
2..*
Participant
1.. *
0..*
Notes: Associate/Disassociate gives more flexibility listed in http://www.ietf.org/mail-archive/web/siprec/current/msg02585.html
(e.g. Cases where parts of CS is recorded via multiple RSs )
e.g. An SRC starts recording a CS1 as part of RS1. For policy reasons the recording of CS1 is stopped for a while.
After some time when SRC wants to resume recording of CS1. There are different possibilities:
1) SRC may have disconnected RS1. So, SRC may setup RS2 and continue to record CS1. In this case SRC after the CS1 finishes will indicate End Time in RS2.
2) SRC will not disconnect RS1 (as it is persistent) and continues to record CS1 as part of RS1 itself.
3) SRC will not disconnect RS1(persistent). But will continue to record CS1 as part of another RS (RS2).
2) SRC does not setup any more Recording Session for this CS (CS1). End Time for CS will never be indicated. Since End Time is optional, this is still fine.
Points:
Associate/Disassociate times are actually attributes of association if we want to retain it.
If we allow a CS to have Zero participants, how do we determine CS stop time ? The earlier discussions it was agreed that stop-time is the time the last participant drops from the CS.
If Start/End time is needed we will define it as:
  Start Time - This optional attribute represents CS start time
  End Time - This optional attribute represents CS end time

## Slide 9: Metadata Model: Participant
Participant
Name / AoR pair
Any objections to having a new attribute in Participant class to represent CNAME ?
  CNAME would be useful for identifying the participant
  Metadata already has optional SSRC attribute
  CNAME correlates stream before/after change
  CNAME can be optional XML element inside participant.
Communication Session
1..*
2..*
Media Stream
sends
receives
0.. *
0..*
1.. *
0..*
Notes: Metadata already has an attribute to indicate SSRC in case of mixed streams as part of <csrc> XML element
In case RTCP is sent from SRC to SRS, sending CNAME as participant attribute may be helpful to co-relate RTCP with participant. Alternatively this can be learnt indirectly from metadata.
SSRC may change due to collision, and that then CNAME is supposed to correlate the stream before/after the change.
I also gather that CNAME, rather than SSRC, is supposed to be used to correlate related streams, like audio and video from same source.
Does that mean that we should reference CNAME in metadata, rather, or in addition, to SSRC? Or if we update metadata when SSRC changes does that eliminate CNAME for tracking the change?
Summary:
CNAME would be useful for identifying the participant
SSRC would be useful for identifying a stream from a participant, in cases where the media packets from the participant make it to the SRS directly, or are incorporated into a mixed stream that ultimately make it to the SRS. In the second case, the SSRC from the stream sent by the participant to the SRC will be included as a CSRC in the mixed stream sent by the SRC to the SRS.
Charles text:
The SRC should be sending RTCP packets to the SRS. There RTCP include SDES packets, which provide the binding of SSRC/CSRC to CNAME. Each RTP packet from the SRC to the SRS contains an SSRC, and zero or more CSRCs. When the SRS receives these, it should be able to determine the corresponding CNAME(s). So far so good, the SRS exactly which CNAMES are associated with each RTP media packet.
The SRC also sends metadata to the SRS. This metadata contains a set of participant elements. One way for the SRS to perform the mapping of each media packet to one or more participants is to include the CNAME in the participate metadata element. There should always be a 1-1 association of CNAME to participant. It would be okay to include the set of SSRCs associated with each participant in the metadata as well, but this is not necessary as that information is already conveyed by the RTCP. The only reason the SSRCs would need to be included in the participant metadata element is if the SRC does not send RTCP to the SRS.

## Slide 10: Metadata Format: Attributes of association
  Proposal to have a new XML element for every association class. This xml element will NOT have a unique ID instead it references the ID of associated elements (shown below).
  <participant
  id="srfBElmCRp2QB23b7Mpk0w==">
  <nameID aor=sip:ram@blr.cisco.com />
  </participant>
  <participantSessionAssoc
  participant id="srfBElmCRp2QB23b7Mpk0w=="
  session="hVpd7YQgRW2nD22h7q60JQ==">
  <associate-time>2010-12-16T23:41:07Z</associate-time>
  <capabilities> TBD</capabilties>
  </participantSessionAssoc>
  <participantStreamAssoc
  participant id="srfBElmCRp2QB23b7Mpk0w==“
  stream ="UAAMm5GRQKSCMVvLyl4rFw==“>
  <associate-time>2010-12-16T23:41:07Z</associate-time>
  <csrc>contributing SSRC-1</csrc>
  </participantStreamAssoc>
Notes:   Association Classes aren't identified by a single ID. Rather they are identified by the IDs of the two things they associate. Thus when updating them those two IDs need to be transmitted. So any partial update to this element requires sending both the IDs.
Other approaches:
Approach 3:
  Define local IDs as aliases for globally unique IDs. This approach reduces the number of unique IDs on the wire per association from 3 to 1, replacing them with local IDs. Of course, the local IDs have to be defined. This might marginally penalize the VERY simple cases, but saves significantly for more complex situations.
  e.g.
  <session
  id="urn:uuid:855a5ded-8420-456d-a70f-6da1eeaeb425"
  local="123">
  ...
  </session>
  <participant
  id="urn:uuid:b2b7c112-5982-469d-9007-6ddbecca64d3"
  local="234">
  ...
  </participant>
  <participantSessionAssoc
  id="urn:uuid:acdf43ee-1441-478d-4eca-4d4f555a896d"
  participant="234"
  session="123">
  ...
  </participantSessionAssoc>
Approach 4:
Encapsulate associations within one of the object elements concerned, e.g., encapsulate sequence of participants in the <session/> element. This approach reduces the number of unique IDs on the wire per association from 3 to 1.
e.g.
<session
id="urn:uuid:855a5ded-8420-456d-a70f-6da1eeaeb425">
<sessionParticipant
participant="urn:uuid:b2b7c112-5982-469d-9007-6ddbecca64d3">
....
</sessionParticipant>
</session>
<participant
id="urn:uuid:b2b7c112-5982-469d-9007-6ddbecca64d3">
…
</participant>
  With Approach 4 , partial update requires sending complete element. So in the example above, if a participant drops out of a session you would have to send the whole <session/> element which has association encapsulated in it.
  Alternatively the association element can be encapsulated inside <participant>. In this case as soon as participant drops the association also ends.

## Slide 11: Metadata Format: Attributes of association
  <stream id="UAAMm5GRQKSCMVvLyl4rFw==">
  <label>96</label>
  </stream>
  This requires change to linkage in the model to allow a participant to be associated with Zero or more sessions ( to keep in consistent with XML)
  When one of the element in the association ends the association element also ends
  With this approach it is easy to interpret and update the association properties as it is a separate XML element.
  Any objections go with this approach ?
Notes: The changes to the model has been already discussed in the previous slides

## Slide 12: Metadata Format: representing send, recv attributes in XML
In the current XML schema send, recv are XML elements inside <participant>. Since these are attributes of association of participant to a Stream this must be inside participantStreamAssoc XML element (example below). Any objections ?
  <participantStreamAssoc
  participant="zSfPoSvdSDCmU3A3TRDxAw=="
  stream ="hVpd7YQgRW2nD22h7q60JQ=="
  send = "8zc6e0lYTlWIINA6GR+3ag==“
  recv = "i1Pz3to5hGk8fuXl+PbwCw==" >
  <associate-time>2010-12-16T23:41:07Z</associate-time>
  </participantStreamAssoc>

## Slide 13: Next steps
Close the remaining open items
Address the text /language issues with draft
Add more metadata examples
Publish next version (06) and ask for more review