## Slide 1: SIPREC Protocol draft-ietf-siprec-protocol-02
IETF 82 Taipei
Authors: H. Lum, L. Portman, A. Johnston, A. Hutton

## Slide 2: Status
Currently -02 draft
Changes from -01
Open items

## Slide 3: Changes from -01
Lot of editorial changes
Add “recordpref” for SDP answer as well

## Slide 4: Issue 1: ‘srs’ and ‘src’ feature tags
Motivation
  Indication of SRC and SRS capabilities and RS intent in order to support SRS discovery and routing of RS INVITES
Suggestion from Paul:
  Rename to ‘+sip.src’ and ‘+sip.srs’
  Abuse of the feature tags mechanism, should not be used for intent
  - Can we use presence of metadata as indication of RS?

## Slide 5: Issue 2: ‘siprec’ option tag
Motivation
  Make sure that only SRS and SRC will handle RS INVITE and not break other UAs in case of wrong configuration or routing mistakes
Suggestion from Paul:
  Two option tags: ‘srs’ and ‘src’
  And have:
    Supported: src
    Required: srs

## Slide 6: Issue 3: Multiplexing support
Support for RTP multiplexing
Support for RTP and RTCP multiplexing to maintain NAT bindings

## Slide 7: Issue 4: ‘recordpref’
Support for “recordpref” on session level as well
Same for “record” ?

## Slide 8: Addition open items
Remove ‘mute’ and ‘unmute’ text
Allow usage of ‘UPDATE’ for full metadata snapshot updates

## Slide 9: Metadata updates flow

## Slide 10: Next steps
Decide on different tags
Publish -03 version

## Slide 11: Discussion