## Slide 1: DS-Lite Management Information Base (MIB) draft-fu-softwire-dslite-mib-02
Yu Fu
Sheng Jiang
Yong Cui
Jiang Dong
Notes: <number>

## Slide 2: Why we need DS-Lite MIB
The NAT-MIB [RFC4008] is designed to carry translation from any address family to any address family, therefore supports IPv4 to IPv4 translation.
The tunnel MIB [RFC4087] is designed for managing tunnels of any type over IPv4 and IPv6 networks, therefore supports IP in IP tunnels.
So why we need DS-Lite MIB?
However, In DS-Lite scenario, the AFTR is not only the tunnel end concentrator, but also a 4-4 translator. Within the AFTR, tunnel information and translation information MUST be mapped each other.
Notes: <number>

## Slide 3: Subtree of DS-Lite MIB
Position of DS-Lite MIB: dsliteMIB ::= {transmission xxx}
dsliteTunnel: Information about Tunnel
dsliteNAT: Information aboute NAT
dsliteInfo: statistical information in the DS-Lite instance
dsliteTraps: the alarm information
dsliteConformance
dsliteMIB
dsliteTunnel
dsliteNAT
dsliteInfo
dsliteTraps
dsliteConformance

## Slide 4: dsliteTunnel::={dsliteMIB 1}
DS-Lite Tunnel parameters are defined in this object
Objects imported from Tunnel MIB: dsliteTunnelIfIndex
New objects defined in our MIB: dsliteTunnelID, dsliteTunnelStartAddress, dsliteTunnelStartAddPreLen, dsliteTunnelEndAddress (Since these objects defined in Tunnel MIB is not access, we define these new objects in our MIB)
dsliteTunnelStartAddress
dsliteTunnelStartAddPreLen
dsliteTunnelEndAddress
dsliteTunnelID
dsliteTunnelIfIndex
dsliteTunnel
dsliteTunnelTable
dsliteTunnelEntry

## Slide 5: dsliteNAT::={dsliteMIB 2}
DS-Lite NAT parameters are defined in this object
Objects imported from NAT MIB: 19 objects are imported from NAT MIB
New objects defined in our MIB: dsliteNATBindLocalAddr, dsliteNATBindLocalPort (Since these objects defined in NAT MIB is not access, we define this new objects in our MIB), dsliteB4Addr, dsliteB4PreLen
dsliteNAT
dsliteNATMapTable
dsliteNATMapEntry
……
dsliteNATBindTable
dsliteNATBindEntry
……

## Slide 6: Mapping information for Tunnel and NAT
We define dsliteTunnelStartAddress, dsliteTunnelStartAddPreLen in dsliteTunnel subtree to present the Ipv6 address and prefix for B4. These two objects can be used to identify the tunnel entry. So the dsliteB4Addr, dsliteB4PreLen in dsliteNATBindTable entry are equalled to the these two objects to map the dsliteTunnelTable entry
Open Question: Another method to create mapping information for Bind Enry is to use the RowPointer to point to the Tunnel entry, does that method better?
Entry 1 ...... dsliteB4Addr, dsliteB4PreLen
dsliteNATBindTable
Entry 2 ...... dsliteB4Addr, dsliteB4PreLen
Entry 3 ...... dsliteB4Addr, dsliteB4PreLen
Entry 4 ...... dsliteB4Addr, dsliteB4PreLen
........
Entry 1 ...... dsliteTunnelStartAddress
, dsliteTunnelStartAddPreLen
........
Entry n
Entry 2 ...... dsliteTunnelStartAddress
, dsliteTunnelStartAddPreLen
Entry 3 ...... dsliteTunnelStartAddress
, dsliteTunnelStartAddPreLen
...…
...…
...…
dsliteTunnelTable
Entry n
Entry 1 mapping to Entry 1
equal to
equal to

## Slide 7: dsliteInfo :: = { dsliteMIB 3 }
The statistical information for DS-lite scenario are described in this object.
  The number and type of session limit are defined in this object
  The number and type of port limit are defined in this object
  Some alarm scalars of AFTR are defined in this object
  The statistical parameters for packets and session are defined in this object.
dsliteInfo
dsliteStatisticTable
dsliteAFTRAlarmScalar
dslitePortLimitTable
edsliteSessionLimitTable
dsliteSessionLimitEntry
dslitePortLimitEntry
dsliteStatisticEntry
..….
Open Question: Shall we need to describe the statistical information in our mib?

## Slide 8: dsliteTraps :: = { dsliteMIB 4 }
The Alarm information for the DS-Lite scenario is defined in this object.
dsliteTraps
dsliteTunnelNumAlarm
dsliteAFTRUserSessionNumAlarm
dsliteAFTRPortUsageOfSpecificIpAlarm
Open Question: Shall we need the alarm information in our mib?
Are there any other alarm objects need to define?

## Slide 9
Comments and suggestions are welcome!
Adopt as softwire WG item?
Thank you !