## Slide 1: Multicast Extensions to DS-Lite Technique in Broadband Deployments draft-ietf-softwire-dslite-multicast-01
Wang, Q., Qin, J., Boucadair, M., Jacquenet, C., and Y. Lee

## Slide 2: Scope & Use case
Scope
  An IPv4 receiver accesses IPv4 multicast contents over an IPv6-only multicast-enabled network.
Use Case
  Deliver multicast-based service offerings to DS-Lite serviced customers in ASM and SSM modes

## Slide 3: Foundations
Address Mapping
  Use [I-D.boucadair-behave-64-multicast-address-format] to build multicast IPv4-embedded IPv6 addresses
  Use [RFC6052] to build unicast IPv4-embedded IPv6 addresses representing IPv4 sources in the IPv6 realm
The underneath network delivers encapsulated packets in standard multicast fashion
  Bandwidth optimization is ensured
All involved interworking functions are stateless
Two fundamental elements: mB4, mAFTR

## Slide 4
IPv4 Source
IPv4 Receiver
mAFTR
mB4
IGMP
MLD
QR
MLD Querier
IPv6 PIM
IPv4 PIM
IPv4 Flows
IPv4-in-IPv6 Flows
Stateless IPv4-IPv6 PIM Interworking Function
Stateless IGMP-MLD Interworking Function
Stateless encapsulation
&
IPv4 -> IPv6 header mapping
of multicast flows
Overall procedures with involved interworking functions:
Need to provision the mB4 with mPREFIX64 and uPREFIX64
IPv4 Realm
IPv6 Realm
IPv4 Flows
DR
R
S
IPv4 Realm
Stateless de-encapsulation of multicast flows
CPE

## Slide 5: Routing Considerations
The mAFTR interconnects the IPv4 multicast distribution tree (MDT) with the corresponding IPv6 MDT.
The mAFTR MUST use the uPrefix64 to build the IPv6 source addresses of the multicast group address derived from mPrefix64.
  In other words, the mAFTR MUST be the multicast source derived from mPrefix64.
The mAFTR MUST advertise the route of uPrefix64 to the IPv6 IGP.

## Slide 6: Demonstration for POC

## Slide 7: Next Step
Please check the demo for POC
Comments are welcome