## Slide 1: DHCPv6 Options for IPv6 DS-Lite Multicast Prefix draft-qin-softwire-multicast-prefix-option-01 IETF 82-Taipei, November 2011
J. Qin, M. Boucadair and T. Tsou

## Slide 2: Goal
This document defines DHCPv6 options to provision
  Unicast PREFIX64
  Multicast PREFIX64
Unicast PREFIX64 is used to synthesize unicast IPv4-embedded IPv6 address following RFC6052 specification
Multicast PREFIX64 is used to synthesize unicast IPv4-embedded IPv6 address as defined in I-D.boucadair-behave-64-multicast-address-format
  It may belong to the SSM range (i.e., ff3x::/32 [RFC4607]) or ASM range

## Slide 3: Use Cases
I-D.venaas-behave-mcast46
  Stateless local synthesize of source/group addresses
I-D.ietf-softwire-dslite-multicast: mB4 uses
  Unicast PREFIX64 for stateless synthesize of source IPv6 address based on a discovered IPv4 source address
  Multicast PREFIX64 for stateless synthesize of group IPv6 address
  Unicast PREFIX64 and Multicast PREFIX64 for stateless decapsulation of multicast IPv4-in-IPv6 packets
  The same Unicast PREFIX64 and Unicast PREFIX64 MUST be configured to the mAFTR

## Slide 4: Next Steps
Adopt it as a WG document?