## Slide 1
464XLAT : Combination of Stateful and Stateless Translation draft-mawatari-softwire-464xlat IETF 82 @ Taipei
2011 / 11 / 15
M.Mawatari @ Japan Internet Exchange Co.,Ltd.
M.Kawashima @ NEC AccessTechnica, Ltd.
C.Byrne @ T-Mobile USA

## Slide 2
What is 464XLAT?
464XLAT is a simple technique to provide IPv4 access service while avoiding encapsulation just by using twice IPv4/ IPv6 translation standardized in [RFC6145] and [RFC6146].

## Slide 3
Terminology
PLAT: Provider side translator(XLAT)
A stateful translator complies with [RFC6146] that performs 1:N translation. It translates global IPv6 address to global IPv4 address, and vice versa.
CLAT:Customer side translator(XLAT)
A stateless translator complies with [RFC6145] that performs 1:1 translation. It algorithmically translates private IPv4 address to global IPv6 address, and
vice versa.
Other features are IPv6 router, DHCPv6 Server/Client, Access Control, DNS Proxy, etc.
The presence of DNS64 [RFC6147] and any port mapping algorithm are not required.

## Slide 4
Network architecture
CLAT
PLAT
IPv6 Internet
198.51.100.1
192.168.1.2
IPv4 Internet
IPv4[P] IPv6
PLAT>
IPv4 pool [192.0.2.1 - 192.0.2.100] XLATE DST Prefix [2001:db8:1234::/96]
CLAT> XLATE SRC Prefix [2001:db8:aaaa::/96] XLATE DST Prefix [2001:db8:1234::/96]
IPv4 SRC 192.168.1.2
IPv4 DST 198.51.100.1
IPv6 SRC 2001:db8:aaaa::192.168.1.2
IPv6 DST 2001:db8:1234::198.51.100.1
IPv4 SRC 192.0.2.1
IPv4 DST 198.51.100.1
IPv4
2001:db8:aaaa::aa
IPv6
IPv4
IPv6
2001:db8:cafe::cafe
IPv6 Native
464XLAT
Stateless XLATE
Stateful XLATE
This architecture consist of CLAT and PLAT have the applicability to landline network (e.g. FTTH) and mobile network (e.g. 3GPP).

## Slide 5
The features that differentiate 464XLAT from others
 | 464XLAT
Location of NAPT44 Function | Provider side(PLAT)
Mesh vs. Hub & Spokes | Hub & Spokes
Translation vs. Encapsulation | Double translation (Stateful XLATE & Stateless XLATE)
How does the CPE “learns” its IPv4 address & port range? | Any port mapping algorithm are not required
Address mapping rules | The format is defined in Section 2.2 of [RFC6052] Not use the WKP “64:ff9b::/96”
Supports IPv6-IPv4 Communication | Requires DNS64

## Slide 6
Our experience
Current Status
  The codes already are running on the field.
  Landline network
    JPIX have started providing 464XLAT trial service since July/2010.
    CLAT is implemented to existing CPE router.
  Mobile network
    We have running code. N900 Mobile (CLAT) and T-Mobile USA (PLAT).
Application Availability
  Web, Mail, Video Streaming.. OK.
  Instant Message, Skype... OK.
  We have no major issue.
NEC AccessTechnica
CL-AT1000P

## Slide 7
Our experience
Traceroute from CLAT
  CL-AT1000P Web-GUI have the special tool of IPv6 traceroute.
IPv6 Network
IPv4 Network
[target] 2400:3000:abab:abab::d2ab:e22e
[3] 2400:3000:1000::1
[2] 2400:3000:1000::10
[1] 2400:3000:50::1
[src] 2400:3000:1::53
CLAT
PLAT
[5] 2400:3000:abab:abab::d2ab:e223
[4] 2400:3000:abab:abab::d2ab:e1a0 (IPv4 Pool Address)
Three IPv4 addresses (from 4Hop to 6Hop) embedded in the low-order 32 bits of the IPv6 address are shown in the traceroute result.
XLAT PREFIX : 2400:3000:abab:abab::/96

## Slide 8
Next steps
Adopt this I-D as a Softwire WG document.
Get more knowledges by running code.
  experiences from landline network and mobile network.

## Slide 9
Additional references
n900ipv6 (Running CLAT code for mobile)
  https://code.google.com/p/n900ipv6/wiki/Nat64D
JPIX experiences
  http://www.apricot.net/apricot2011/media/Masataka_Mawatari_IPv6v4_Exchange_Service_for_sharing_IPv4_address.pdf

## Slide 10
Comments and suggestions are welcome.
Thank you!