## Slide 1: Stateless Deterministic NAT (SD-NAT)
draft-penno-softwire-sdnat-01
Reinaldo Penno (rpenno@juniper.net)
Olivier Vautrin (olivier@juniper.net)
Alain Durand (adurand@juniper.net)
November 2011

## Slide 2: Motivation
Issues with current Stateless solutions:
  Those mapping approach requires an IPv6 access network and an IPv6 capable CPE.
  Tying IPv6 and IPv4 address reduce flexibility in managing IPv4 pool: add/deletion of IPv4 resources require IPv6 renumbering.
  Require an important CPE modification. Recent History has shown that it is the most difficult part.

## Slide 3: Time Crunch
Time is the enemy of Stateless solutions:
  Once CGNs are deployed, no reason to move away from them (CPE investment, Ipv6 access)
  Ratio Users/IP increasing, Stateless will become less attractive
CGN Smooth upgrade to SD-NAT:
  No CPE upgrade
  No Ipv6/Re-addressing needed
  Easy Mixed of CGN/SD-NAT

## Slide 4: Port mapping on SD-CPE
SP access
Customer Premises
1024
65535
Host 1
Host 2
Host 3
Host n
1024
65535
Internal Hosts
SD-CPE

## Slide 5: Port mapping on SD-CGN or SD-AFTR
1024
65535
IPv4 address 1
IPv4 address 2
IPv4 address 3
IPv4 address n
IPv4 address n+1
1024
65535
SD-CPE x
SD-CGN or SD-AFTR
1024
65535
SD-CPE y
SD-CGN or SD- AFTR is stateless. A simple formula maps inside and outside ports.
SP core
SP access

## Slide 6: CPE Modification
Example on Linux based CPE (DD-WRT, …)
/lib/firewall/uci_firewall.sh
OLD:
$IPTABLES -I zone_${zone}_nat 1 -t nat -o "$ifname" -j MASQUERADE
NEW:
$IPTABLES -I zone_${zone}_nat 1 -t nat -o "$ifname" -j MASQUERADE -p tcp --to-ports 1024-2023

## Slide 7: SD-NAT in a nutshell
Stateless operation on CGN
  No Logs, No State, Easy Redundancy, Low delay
Minimal CPE modification
  CPE chooses outgoing SRC ports to fit into a well-known range [1024-MaxPort]
    CPE can been configured with MaxPort (eg TR69)
    Alternatively, the CPE can dynamically discover MaxPort.
  That’s it! No IPv6 requirements, no complex IPv4/IPv6 mapping.
Flexibility
  Easily add/remove IPv4 global addresses from NAT pool without renumbering the access network.
  Access Network can be IPv4.
  Can work with an IPv6 access network (Very similar to DS-Lite).

## Slide 8: Time Crunch
Time is the enemy of Stateless solutions:
  Once CGNs are deployed, no reason to move away from them (CPE investment, Ipv6 access)
  Ratio Users/IP increasing, Stateless will become less attractive
CGN Smooth upgrade to SD-NAT:
  No CPE upgrade
  No Ipv6/Re-addressing needed
  Easy Mixed of CGN/SD-NAT

## Slide 9: Thank you
Questions?