## Slide 1: Why do standards matter?
The beauty about standards is that there are more than one to choose from….

## Slide 2: How many engineers does it take to plug a laptop into a socket?
Based on a true story…

## Slide 3: 1st Attempt
Hotel room socket
Wrong shape
Laptop plug

## Slide 4: 2nd Attempt
Laptop plug
“multi-protocol” socket
No ground

## Slide 5: 3rd Attempt
“multi-protocol” socket
AU adaptor
Ground safety prong missing
Laptop plug

## Slide 6: 4th Attempt
“multi-protocol” socket
UK adaptor
Wrong shape
Laptop plug

## Slide 7: 5th Attempt
“multi-protocol” socket
US adaptor
“Hot” prong too wide
Laptop plug

## Slide 8: 6th Attempt
“multi-protocol” socket v2.0
Victory!
Laptop plug

## Slide 9: Let’s not do that again…

## Slide 10: Taking stock from the Softwire Interim meeting
Charting the “stateless” problem space

## Slide 11: Don’t say stateless…
3 characteristics
  Per-flow NAT binding on CPE vs CGN
  Per-subscriber mapping
    Hub & Spokes, on PRR (static or learned)
    Hub & Spokes, on PRR (derived from address mapping rules)
    Mesh, on CPE (derived from address mapping rules)
  Translation vs Encapsulation

## Slide 12: A) per-flow NAT bindings
On CPE
Do not over-optimize port allocation mechanisms  If you need flexibility on port distribution, use a CGN
AGREED

## Slide 13: B1) per-subscriber state on PRR (static or learned)
High level:
  Scattered IPv4 address space
  Do not overload CPE with a large number of mapping rules
  Hub & spoke model
No use of algorithmic mapping rules
  neither on CPE nor on PRR
Per user state on PRR
Derivative of DS-Lite/4over6 using DHCP or PCP port distribution

## Slide 14: B2) per-subscriber mappings on PRR (derived from address mapping)
Same as B1), but without per-user state
Use address & port mapping algorithmic rules as “forwarding function” on PRR

## Slide 15: B3) per-subscriber mappings on CPE (derived from address mapping)
Mesh model
Use of provisioning and forwarding algorithmic rules on CPE
Consensus to converge toward a unified address & port mapping algorithm  Can the unified address & port mapping algorithm be specified to include B2 case?
  No rules on CPE: send all traffic to AFTR tunnel endpoint

## Slide 16: C) Translate vs Encap
Technically, mostly the same
  Minor differences: overhead vs loss of information
Operational perspective
  Discussion on what is easier to do for on-path processing (QoS/ACL/…):
    Look at IPv6-translated headers in middle points
    Look at encapsulated IPv4 headers in middle points
    Look at decapsulated IPv4 headers in end points only

## Slide 17: Way Forward

## Slide 18: Way Forward, part 1: Create Building Blocks
Design team to propose a unified address & port mapping algorithm
  Target: PS document
  Applicable to both H&S or Mesh and Encapsulation or Translate
Define unified DHCPv6 options for the above
  Target: PS document
  Applicable to both H&S or Mesh and Encapsulation or Translate

## Slide 19: Way Forward, part 2 Translation vs Encapsulation
One or multiple approaches?
  Impact on interoperability
  What to implement on CPEs?
We can publish them all as RFC
If we do, do they all have the same status?
  (Std track, Exerimental, Informational, BCP,…)

## Slide 20: Since the Interim
Formed MAP design team (chaired by Ole)
  2 drafts: MAPing & DHCP option
Lots of discussions
New proposals:
  “Unifying” theories (4rd-U,…)
  SD-NAT