## Slide 1: dIVI-pd: Dual-Stateless IPv4/IPv6 Translation with Prefix Delegation
X. Li, C. Bao, W. Dec,
R. Asati, C. Xie, Q. Sun
2011-11-12

## Slide 2: Introduction
The dIVI-PD is an extension of stateless IPv4/IPv6 translation with address sharing
  RFC6052: IPv6 Addressing of IPv4/IPv6 Translators
  RFC6145: IP/ICMP Translation Algorithm
The dIVI-PD is compatible with MAP design
  Mapping of Address and Port (MAP)
  DHCPv6 Options for Mapping of Address and Port

## Slide 3: IPv4/IPv6 translation
IPv4 over IPv6 behavior
IPv4/IPv6 translation
Stateful
Stateless
1:1 IVI
NAT64
1:N IVI
1:N dIVI-PD
1:N dIVI

## Slide 4: dIVI-PD scenario
L3 CPE
IPv4/
IPv6
BRAS
1:N stateless
Xlate
D
S
L
A
M
IPv6
IPv4
.
.
.
.
Radius
IPv6CP
(DHCPv6-PD)
IPv4: DHCP
IPv6: SLAAC
Single PD /64
ISP prefix
Domain-prefix
CPE prefix
IPv4 sharing-ratio
Domain subscriber
https://datatracker.ietf.org/doc/draft-xli-softwire-divi-pd
Notes: pref=2001:c68:f000::/48
ivi4=124.127.116.0/29
r=128
int4=202.97.255.1/30
hop4=202.97.255.2
int6=2001:c68:3000:100::1/64
hop6=2001:c68:3000:100::2
gw6=2001:c68:3000:100
nivi=2001:c68:5000
dns=2001:c68:3000:100::1

## Slide 5: Original design of dIVI-PD
Address format
Port mapping algorithm
Suffix coding

## Slide 6: MAP
Basic Mapping Rule (BMR)

## Slide 7: dIVI-PD and MAP (1)
Basic Mapping Rule (BMR)
Default Mapping Rule (DMR)

## Slide 8: dIVI-PD and MAP (2)
Generalized modulus algorithm (GMA)
P = R * M * j + M * K + i
K = (floor(P/M)) % R
R=0-65535  k bits
M<=65536/R  m bits
a bits
dIVI-PD: R=0-4096, M=1, a=4 bits

## Slide 9: DHCP options
Without default
  The IPv6 prefix/length
  The BR prefix/length
  The IPv4 address
  The PSID (K)
  The sharing ratio (R=128)
With default
  The maximum number of continue ports (M=1)
  The PSID length (c=7)

## Slide 10: dIVI-PD OpenWRT configuration example
echo Start IVI mapping
ip -6 route add 2001:da8:b00e:f37f:ca26:66f3:7f00:0007/128 via fec0::2 dev ivi1
ivimap -6 -H -l 64 -L 64 -b fec0::2
ip route add default via 10.0.0.2 dev ivi0
ivimap -4 -m -H -r 7 -o 127 -p 2001:da8:b00e:f37f:: -l 64 -P 2001:da8:b00e:ffff:: -L 64 -b -C 1340 10.0.0.2
ip -6 route add default via 3ffe:3200::1 dev eth0.1
PSID
DMR (BR prefix/len)
BMR (CE prefix/len)
IPv4
PSID
Ratio

## Slide 11: Dual stateless translation is not harmful
IPv4
  Options
    Dropped (no harm)
  Type of service
    Copied to traffic class
  MTU and fragmentation
    Processed according to RFC6145/RFC6146
  ICMP/ICMPv6
    Processed according to RFC6145
  Transport layer (TCP, UDP)
    Processed according to RFC6145

## Slide 12: Experimental data
Options
Fragmentation
DF=1 & MF=1
ICMP/ICMPv6

## Slide 13: It can use existing tools for O&M
Null route
ACL
eACL
PBR
QoS
Caching
Rate limit example

## Slide 14: Experimental Evaluation
Core translator
BRAS
CPE
It is tested at Tsinghua University and in China Telecom lab

## Slide 15: Remarks
dIVI-PD is an extension of IPv6/IPv6 stateless translation
dIVI-PD provides unique features for OPEX value
dIVI-PD is compatible with MAP design