## Slide 1: 4rd and 4v6 @ IETF 82
draft-murakami-softwire-4rd-01
(Satoru Matsushima / Tetsuya Murakami / Ole Trøan)
draft-murakami-softwire-4v6-translation-00
(Gang Chen / Hui Deng / Satoru Matsushima / Tetsuya Murakami / Woj Dec)
DS-lite
6rd
A+P
4rd

## Slide 2: Ideal document structure
Motivation draft: draft-operators-softwire-stateless-4v6-motivation-02
Applicability statement: draft-sun-intarea-4rd-applicability-01
4rd mapping rule
draft-mdt-softwire-mapping-address-and-port-01
4rd dhcp option
draft-mdt-softwire-map-dhcp-option-01
4rd encapsulation
draft-murakami-softwire-4rd-01
4rd translation
draft-murakami-softwire-4v6-translation-00

## Slide 3: 4rd in One Slide
IPv4 + IPv6
IPv4 + IPv6
IPv4 + IPv6
  Native dual-stack IP service to the Subscriber
Simple, stateless, automatic IPv4-in-IPv6 encap and decap functions
IPv4 traffic automatically follows IPv6 Routing
  BRs placed at IPv4 edge, addressed via anycast for load-balancing and resiliency
Defined in draft-murakami-softwire-4rd
IPv6
CE
4rd Border Relays
Dual Stack Core
4rd
4rd
4rd
4rd
“One line” global config for IPv6 Gateway
Subscriber IPv4 address or prefix derived from IPv6 address

## Slide 4: 4v6 in One Slide
IPv4 + IPv6
IPv4 + IPv6
IPv4 + IPv6
  Native dual-stack IP service to the Subscriber
Simple, stateless, automatic IPv4-in-IPv6 encap and decap double translation functions
IPv4 traffic automatically follows IPv6 Routing
  BRs placed at IPv4 edge, addressed via anycast for load-balancing and resiliency by using rfc6052 WKP
Defined in draft-murakami-softwire-4rd draft-murakami-softwire-4v6-translation
IPv6
CE
4v6 Border Relays
Dual Stack Core
4v6
4v6
4v6
4v6
RFC6052 WKP for IPv6 gateway
Subscriber IPv4 address or prefix derived from IPv6 address

## Slide 5: 4rd: encapsulation 4v6: double translation
Utilizing same mapping rule
  Mapping between IPv6 prefix and IPv4 address (+ port)
Difference
  Destination address to the outside of domain
    4rd encapsulation : BR address
    4v6 double translation : rfc6052
  Source address from the outside of domain
    4rd encapsulation : BR address
    4v6 double translation : rfc6052

## Slide 6: Concern in the map draft
Interface ID
  No need to embed IPv4 + PSID for both 4rd and 4v6
  How to extract 4rd packet toward the outside of 4rd domain at BR?
    Destination address
      Encapsulation -> tunnel end-point address
      Translation -> Well-known prefix
    If embedding IPv4 + PSID in IID of the destination address in the packet toward to the outside of 4rd domain, the destination address is not matched to the tunnel end-point address at BR.
Port-set
  Algorithm is stable, but the set of parameters are still varied.
  Should control port-set, shared ratio, etc with only IPv6 prefix delegation.

## Slide 7: Next:
Refer and follow the MAP
Cover hub and spoke case
  Doesn’t use Forwarding mapping rules
Request WG adoption