## Slide 1: Lightweight 4over6 in access network draft-cui-softwire-b4-translated-ds-lite-04
Y. Cui, P. Wu : Tsinghua University
Q. Sun, C. Xie : China Telecom
Y. Lee: Comcast
C. Zhou and T. Tsou: Huawei Technologies

## Slide 2: History of “lightweight 4over6”
draft-cui-softwire-b4-translated-ds-lite-00
October 2010
draft-sun-v6ops-laft6-00
March 2011
draft-cui-softwire-b4-translated-ds-lite-01
July 2011
draft-cui-softwire-b4-translated-ds-lite-04
Deploy in Hunan field trial with software client, Buffalo box, and run a demo system in IETF 81th.
October 2011
Jan ~ Aug 2011
Notes: October 2010

## Slide 3: Technical Matrix
Stateless
Pre-defined Port
Management
4rd, 4rd-u, dIVI-PD,
stateless 4over6,etc.
Stateful
subscriber-level
Dynamic Port Management
session-level
DS-Lite
Public 4over6
Lightweight 4over6
rule-level

## Slide 4: Motivation
A simple extension for DS-Lite without NAT, and address sharing mode for public 4over6
Good scalability in centralized deployment
Easy for traffic logging
No extra request on address/prefix planning
On-demand IPv4 address/port set provision
Flexible port management
No big impact on CPE when NAT44 has already widely supported

## Slide 5: What is Lightweight 4over6 ?
Lightweight 4over6 is an IPv4-over-IPv6 hub and spoke mechanism, which supports address sharing to deal with IPv4 address exhaustion, and places the IPv4 NAT on the initiator side.

## Slide 6: Components
Lw 4over6
initiator
Lw 4over6
Concentrator
Acquire public IPv4 address + Port set via DHCP/PCP/extension
NAT44 within restricted port set
  Tunnel encapsulation/de-capsulation.
Subscriber-level binding record
  Tunnel encapsulation/de-capsulation.
  No NAT anymore
Tunneling
Non-continuous port set algorithms (e.g. GMA in the design team) can be introduced to further improve the security.
[v6 address, v4 address, PSID]
public v4 address,
port set

## Slide 7: Lightweight 4over6 Example
IPv4 server
Access
Network
(IPv6)
Metro Network
(IPv6)
Backbone
(IPv4)
BR
BNG
Lw 4over6
concentrator
Lw 4over6
initiator
IPv4-only user
192.168.1.3
211.98.2.5
2001:c68:300::2
202.102.2.5 [2049~4096]
2001:c68:400::2
Src:192.168.1.3:10987
Dst: 211.98.2.5:80
Src:202.102.2.5:2049
Dst: 211.98.2.5:80
Src: 2001:c68:300::2
Dst: 2001:c68:400::2
Src:202.102.2.5:2049
Dst: 211.98.2.5:80c
Src: 211.98.2.5:80
Dst:202.102.2.5:2049
Src:211.98.2.5:80
Dst:202.102.2.5:2049
Src: 2001:c68:400::2
Dst:2001:c68:300::2
Src:211.98.2.5:80
Dst:192.168.1.3:10987
NAT44 + tunneling
IPv4 address | IPv6 address | Port set
202.102.2.5 | 2001:c68:300::2 | 2049~4096

## Slide 8: Prototype Implementation
LW 4over6 Initiator
LW 4over6 Concentrator
NE40e

## Slide 9: Our Practice on Commercial Network
IPv4 server
Access
Network
(IPv6)
Metro Network
(IPv6)
Backbone
(IPv4)
Backbone
(IPv6)
IPv6 server
BR
BR
BRAS/SR
LW 4over6
concentrator
LW 4over6
initiator
Dual-stack user
IPv4-only user
syslog system
It can be deployed rapidly, with little impact on existing addressing and routing.
We only need to configure our remaining public IPv4 address pools in concentrator.
Demo system in IETF 81th

## Slide 10: Application Test

## Slide 11: Performance Test
We have implemented concentrator with B+ tree-based algorithm for subscriber binding.
Performance test result on a normal PC concentrator:
  Maximum concurrent subscribers: 500,000
  Maximum concurrent sessions: 100 million
  Throughput: 800Mbps
 | 100,000 | 200,000 | 500,000
Total Tree Height | 7 | 7 | 8
Lookup Memory Access Number(ave.) | 22 | 23 | 28
Memory Consumption(ave.) | 27.1M | 28.2M | 32.4M
Subscriber #

## Slide 12: Conclusion
Lightweight 4over6 is a simple extension for DS-Lite without NAT, and it is an address sharing mode for public 4over6.
We have verified it in our commercial network.
It has good scalability, and support a majority of current IPv4 applications.
It can be deployed rapidly, with little impact on existing addressing and routing.
It is simple to achieve traffic logging.
It can be coexistent with DS-Lite easily.

## Slide 13: Next Step…
We have got a lot of online/offline feedback in the WG.
It is in the milestone of softwire WG charter
  Jul 2011 Adopt DS-Lite without NAT document as a Working Group document
We would like to ask for adoption of WG item
Comments and contributions are welcome
  http://tools.ietf.org/id/draft-cui-softwire-b4-translated-ds-lite-04.txt

## Slide 14
Thank you 
Q&A

## Slide 15: NAT offload in Lightweight 4over6
IP Network
CR (CT)
CPE(IT)
Public IPv4 address
Distributed NAT
CPE(IT)
CPE(IT)
Public IPv4 address
+ Port set 1
Public IPv4 address
+ Port set 2
CT
Concentrator
IT
Initiator
CGN