## Slide 1: Shared Use of TCP Experimental Options
07/30/26 21:33
<number>
draft-touch-tcpm-experimental-options-00
IETF 82
Joe Touch, USC/ISI

## Slide 2: Summary
Current experimental options overloaded
  Multiple concurrent uses cannot be distinguished
Add nonce to EO format
  Nonce used to differentiate concurrent uses
Goal
  Informational (or BCP?)
07/30/26 21:33
<number>

## Slide 3: TCP Exp. Options
Kind = 253 or 254 [RFC4727]
07/30/26 21:33
<number>
Kind
Len=var
Option fields
Option fields (con’t)
Notes: <number>

## Slide 4: TCP Experiments
Precursor to TCP AO (253, 254)
TCP Cookie Transactions
  As deployed (31, 32)
  As spec’d (253)
Tcpcrypt (76, 77, 78)
Other commercial products (33, 76, 77, 78)
07/30/26 21:33
<number>

## Slide 5: Approaches to increased experiments
Relax IANA assignment hurdles
  The pool is very small
  The pool already has collisions
Increase number of EOs from 2 to 18
  Per draft-eddy-tcpm-addl-exp-options
  Doesn’t address existing collisions
  Requires IANA oversight of new 16 values
07/30/26 21:33
<number>

## Slide 6: Problems with existing approaches
Usage collision
  Useful to avoid future collisions
  Useful to mitigate existing collisions
IANA oversight
  Useful to avoid need for oversight
Small codepoint space
  16 now; another 16, then another…
07/30/26 21:33
<number>

## Slide 7: Proposed Shared Use of TCP Exp. Options
Kind = 253 or 254 [RFC4727]
Nonce = arbitrary per-experiment value
  Typ. 32-bits, e.g., Unix time
07/30/26 21:33
<number>
Kind
Len=var
Nonce
Option fields
Option fields (con’t)
Nonce (con’t)
Notes: <number>

## Slide 8: Properties of this proposed solution
Helps avoid collisions
  Unlikely nonce will overlay with misbehaving experiment option values
Self-managed
  Self-assigned
  Can use any method, e.g., Unix time
Large codepoint space
  Consumes space, but experiments should leave room for future option use anyway
07/30/26 21:33
<number>

## Slide 9: Issues
Processing KIND=253/254
  Check nonce FIRST
  Process each nonce as a separate option kind
  Ignore if nonce not known
  Len = total option (including nonce)
Nonce length
  SHOULD be 32 bits
    Alignment unaffected if Nonce is removed if permanent
  MAY be 16 bits if desired
    high half of Unix time is enough if experiments aren’t created more than once every 20 hours
07/30/26 21:33
<number>

## Slide 10: Possible extensions
Nonce + checksum
  Detects/avoids legacy collisions
  Larger space, higher computation cost
Use in other exp. codepoints
  Notably TCP/UDP ports
07/30/26 21:33
<number>