## Slide 1: TCP Automatic IW
07/30/26 21:33
<number>
draft-touch-tcpm-automatic-iw-01
IETF 82
Joe Touch, USC/ISI

## Slide 2: Overview
TCP IW constant requires per-decade updates
  Originally defined as 1 MSS [Ja88]
  Originally implemented as 2 MSS
  Redefined as min(3 MSS, 4KB) [RFC2414, 1998]
  Proposed as 10 MSS [draft-ietf-tcpm-initcwnd]
TCP IW can auto-adjust like TCP
  AIMD
  Over long timescales
  React to loss during IW (as best possible) only
  Goal - experimental
07/30/26 21:33
<number>

## Slide 3: Proposed algorithm
At first boot:
  IW = maxIW
Increment loss counter when:
  SYN-ACK includes ECN
  Retransmit is within [ISN, ISN + IW]
Monthly or conn_count > max_conn:
  AIMD iff loss/conn_count > loss_thresh
07/30/26 21:33
<number>

## Slide 4: Algorithm properties
Self-adjusting
  No need to revisit every decade
Conservative
  AIMD
TCP-friendly operation
  Operates over very long timescales
  Affects only IW (start, restart)
Low-effort
  Act only during ECN or retransmission
07/30/26 21:33
<number>

## Slide 5: Proposed constants
AI <= 2 MSS
MD <= 0.5
Max_conn <= 1000
IW is multiple of 2 (helps compr. ACKs)
Loss_thresh >= 95%
AI limited to 2 MSS/year (??)
07/30/26 21:33
<number>

## Slide 6: Issues
Algorithm design
  Basic function
  Triggers (SYN-ACK ECN, retransmission)
  MSS vs. byte
  Seqno wrap
Constants
  (change based on discussion)
False positives
  Due to reordering
Granularity
  Per machine, interface, subnet
Additional state
  Per-conn – ISN, seqno wrap
  Across reboots (what if not available?)
07/30/26 21:33
<number>