## Slide 1: TRILL Fine Grained Labeling
Donald Eastlake 3rd
Huawei Technologies
d3e3e3@gmail.com
<number>
November 2011
TRILL WG
Notes: November 2011
<number>
TRILL WG

## Slide 2: Fine Grained Labeling
A way to label TRILL data with >4K labels.
Frames on Ethernet links still have regular VLAN labels with 12-bit VLAN IDs. Appointed Forwarder still in terms of VLAN.
A detailed presentation was given at the last IETF meeting in Quebec City.
draft-eastlake-trill-rbridge-fine-labeling-02.txt
November 2011
<number>
TRILL WG

## Slide 3: Fine Grained Labeling
Latest news:
  IEEE Registration Authority has granted EtherType 0x893B for use in TRILL fine-grained labeling.
November 2011
<number>
TRILL WG

## Slide 4: TRILL Label Format
<number>
Link Specific Header
V,F,M,TTL
Inner.MacDA
Inner.MacSA
Link Specific Trailer
Payload
Inner.Label
November 2011
Egress | Ingress
TRILL WG
If Header Flag needed
F = 0 -> Inner.VLAN
F = 1 -> Inner.Label

## Slide 5: TRILL Label Format
Comparison of
  C-tag + EX-tag
    In current draft
  EX-tag + C-tag
    An alternative
November 2011
<number>
TRILL WG
Notes: November 2011
<number>
TRILL WG

## Slide 6: TRILL Label Format
C-tag + EX-tag
  Maximum backwards compatibility
  Handling of legacy RBridges in the same network fully specified in current draft
  Requires a header flag (or EtherType stripping on input and look-ahead on parsing)
November 2011
<number>
TRILL WG
Notes: November 2011
<number>
TRILL WG

## Slide 7: TRILL Label Format
EX-tag + C-tag
  Requires software/firmware upgrade
  Would need to work out how to isolate legacy RBridges, which might drop new frames, in a campus
  No header flag required
November 2011
<number>
TRILL WG
Notes: November 2011
<number>
TRILL WG

## Slide 8: END
Donald Eastlake 3rd
Huawei Technologies
d3e3e3@gmail.com
<number>
November 2011
TRILL WG
Notes: November 2011
<number>
TRILL WG