## Slide 1: TRILL Multihoming Proposal
Pathangi Janardhanan

## Slide 2: Handling of Multihoming in TRILL
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
Switch Multi-homing to TRILL Campus (SW1)
  RB1, RB2 will elect a DRB and AF for VLANs on that link
  RB1 gets selected as the AF for the link
  RB1 – SW1 link will be used for traffic in and out of the TRILL Campus and SW1 on that set of VLANs
End host multi-homing to TRILL campus
  RB1 and RB2 will not see each other through the host
  In this configuration, the host should operate in Active-Passive mode, i.e. it should send and accept the data from only one link
  This link can be RB1 – H1 link
  If this link fails, than H1 will switch to the other link, which is H1-RB2 link
AF
SW1
H1

## Slide 3: Handling of Multihoming in TRILL
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
If the external node treats the two links as a LAG
No AF formed between RB1 and RB2
Unicast Data Handling
RB4 learns the MAC as behind RB1
RB4 learns the MAC as behind RB2
i.e. looks like a MAC Move
Node sends data to SW1
From SW1 to the network
  If packet is sent through RB1, RB4 learns the MAC as belonging to RB1
  Later when due to hashing another flow is sent through RB2, RB4 sees this as a MAC move
  Results in constant MAC Move and also potential packet re-ordering
  Can be avoided if SW1 uses MAC based or VLAN based hash distribution
From network to SW1
  If RB2 is the last seen RBridge for this MAC, packet is sent to RB2
  No Multipathing between RB1 and RB2 from the network

## Slide 4: Handling of Multihoming in TRILL
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
If the external node treats the two links as a LAG
No AF formed between RB1 and RB2
Multicast Data Handling
Remove AF for Multicast Traffic
  SW1 will receive duplicate traffic
  Traffic sent from SW1 to RB1, will again be reflected back to it on the RB2-SW1 link
  Traffic from the network, would get delivered twice, once through RB1 and next time through RB2

## Slide 5: Handling of Multihoming in TRILL – Virtual RBridge
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
RBv
Virtual RBridge
  The physical topology remains the same as before
  The RBridges RB1 and RB2 generate LSP as though there is a RBridge RBv, to which both of them are connected
  This is called the virtual RBridge
  Logically the network diagram looks as shown with the virtual RBridge, and the external host and switch connected to this Virtual RBridge
  There can be multiple nodes behind the same Virtual RBridge
  Useful for scaling compared to having one Virtual RBridge per connected node
Behavior of the external nodes
  The external nodes need to treat their links to the network as a LAG
  If using Dynamic LAG (LACP) will need coordination between RB1 and RB2 (This is out of scope of this proposal)

## Slide 6: Handling of Multihoming in TRILL – Virtual RBridge
Realization of Virtual RBridge
  IS-IS Control Plane
    RB1 and RB2 should generate LSP indicating connectivity to RBv
    This should be equal cost link from both RB1 and RB2
    Should not permit routing for normal traffic between RB1 and RB2 through RBv
      In LSP for RBv, set the IS-IS overload bit on
    Ensure RBv cannot be a root RBridge for multicast trees
  Creation of the Virtual RBridge
    RB1 and RB2 must know that they have to create a Virtual RBridge
    This will be because there are multiple nodes which are dual homed to these two nodes, and the Virtual RBridge is used to represent these nodes
    Could be by configuration or some dynamic learning protocol
      Out of scope of this proposal
    Both RB1 and RB2 must agree on the Virtual RBridge ID to be used for this purpose
      Could be by configuration or some dynamic protocol between the two
      Out of scope of the proposal

## Slide 7: Handling of Multihoming in TRILL – Virtual RBridge
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
RBv
Handling of Unicast data traffic
Data from External host/Switch to the network
SW1 sends traffic to RB1
RB1 knows that these ports are used for dual homing, and the associated Virtual RBridge is RBv
Sends the TRILL frame, with ingress RBridge set to RBv
RB4 now learns the MAC as being behind RBv
RB4 learns the MAC as behind RBv
SW1 due to hashing sends packet to RB2
RB2 also knows that these ports are used for dual homing, and the associated Virtual RBridge is RBv
Sends the TRILL frame with ingress RBridge set to RBv
RB4 now does not see this as MAC move, and no problems
RB4 sees no change, and MAC is still behind RBv
Data from Network to the external Switch/Host
RB4 gets data for SW1, and the lookup shows the MAC as reachable through RBv
RBv is reachable through multipath of RB1 or RB2
Uses ECMP and distributes traffic via RB1 and RB2
When RB1/RB2 receive traffic, they realize that RBv is owned by them (Virtual RBridge they created)
Decapsulate and forward the frame to the port

## Slide 8: Handling of Multihoming in TRILL – Virtual RBridge
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
LAG
LAG
RBv
Handling Flooding data traffic
Mandate use of minimum of two trees from each root node
One of the trees should be engineered to choose RB2 – RBv link, the other tree should be engineered to choose RB1 – RBv link
This is uniform for all RBridges in the network
In the example, it is RB4-1 (active link RB1-RBv), and RB4-2 (active link is RB2-RBv)
If RB1 is a root bridge, than form another tree with RB2 as the root bridge
Data from External host/Switch to the network
SW1 uses some load balancing and forwards the traffic to RB1
RB1 will send it on TRILL N/W Ingress RBridge as RBv, and Tree as RB4-1 (or any tree where RBv-RB1 link is active)
When traffic reaches RB2, RB2 will not forward to ports which belong to VRb, since it will be pruned for the tree RB4-1
H1
Data from External host/Switch to the network
SW1 uses some load balancing and forwards the traffic to RB2
RB2 will send it on TRILL N/W Ingress RBridge as RBv, and Tree as RB4-2 (or any tree where RBv-RB2 link is active)
When traffic reaches RB1, RB1 will not forward to ports which belong to VRb, since it will be pruned for the tree RB4-1

## Slide 9: Handling of Multihoming in TRILL – Virtual RBridge
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
LAG
LAG
RBv
H1
Handling Flooding data traffic
Data from Network
RB4, which is the ingress RBridge chooses either RB4-1 or RB4-2 as the tress
If it chooses RB4-1, as the distribution tree, then RB1 will forward the packets out to the ports belonging to RBv
If RB4 alternatively chooses RB4-2 as the distribution tree, then RB2 will forward it to the ports of RBv, and RB1 will drop it on these ports

## Slide 10: Handling of Multihoming in TRILL – Virtual RBridge
Requirements from the Hardware/Data Plane
  Nickname
    Ability to support multiple nickname
    One virtual bridge nickname for every set of ports that are being paired with another RBridge
  Unicast Data Forwarding
    Ability to set the ingress RBridge to one of the nicknames associated with this RBridge
    This should be selectable at least at the physical port level
    When receiving data, should be able to recognize multiple nicknames as being associated with this RBridge
    If MAC lookup fails for the Virtual RBridge nickname, either flood it to all relevant access ports (VLAN flooding) or flood it to ports associated with that Virtual RBridge and belonging to that VLAN
  Multicast Data Forwarding
    For a tree, for which the link between this RBridge and the virtual RBridge is not active, prune all the ports of the virtual RBridge
    Ability to choose the ingress RBridge and the distribution tree to use at least on a per port basis

## Slide 11: Handling of Multihoming in TRILL – Virtual RBridge
Handling Link Failures
Link between SW1 and RB1 fails
RB1 informs RB2 of this failure
RB2 knows the corresponding Link between RB2 and SW1
RB2 will move that link out of the set of ports controlled by VRb
Further packets from this port, will be encapsulated with ingress RBridge set as RB2
The rest of the network, sees this as a MAC move
From now on, the packets will be sent to RB2
Link becomes Operational again
RB1 should inform RB2 of the link up
RB1 will then revert to using VRb as the ingress RBridge for this port
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
RBv

## Slide 12: Handling of Multihoming in TRILL – Virtual RBridge
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
H1
LAG
LAG
RBv
Handling Node Failure
RB1 fails
If RB1 is the flooding packet forwarder for VRb, then RB2 should take over this role
RB2 will continue to advertise these ports using the VRb, so that when RB1 comes back, there is no MAC move operations

## Slide 13: Handling of Multihoming in TRILL – Virtual RBridge – Other options for multicast data
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
LAG
LAG
RBv
Handling Flooding data traffic
H1
In every tree of the network, either RB2 – RBv will be active or RB1-RBv will be active
One option is to insist on trees with RB1 and RB2 as root, but will not scale for if there are lots of RBv
Handling Traffic from Network
The ingress node would have picked a distribution tree
In this distribution tree, either RB1 or RB2 would have link to RBv
The other RBridge, should prune the ports of RBv from this distribution tree
Hence RBv ports will get this from packet only once either from RB1 or RB2
Handling Traffic from SW1 to network
The packet can reach either RB1 or RB2
If there is a tree with this RB – RBv as active link, use that as the distribution tree for these ports
If there is no such tree, then tunnel the packet to the other RB and have that forward the packet to the network ???

## Slide 14: Handling of Multihoming in TRILL – Virtual RBridge, Other options for multicast data
TRILL Campus
L2 Switch
RB1
RB2
RB3
RB4
RB5
RB6
SW1
LAG
LAG
RBv
Handling Flooding data traffic
H1
In every tree of the network, either RB2 – RBv will be active or RB1-RBv will be active
Handling Traffic from Network
The ingress node would have picked a distribution tree
In this distribution tree, either RB1 or RB2 would have link to RBv
The other RBridge, should prune the ports of RBv from this distribution tree
Hence RBv ports will get this from packet only once either from RB1 or RB2
Handling Traffic from SW1 to network
The packet can reach either RB1 or RB2
If there is a tree with this RB – RBv as active link, use that as the distribution tree for these ports
Send the packet with Ingress RBridge as RBv, but need to relax the RPF check Could be costly in case of temporary loops